## Slide 1: WF on SIB reading for cell reselection and HO in NR-U (RAN4#94-e email thread #46)
Intel, ….
R4-2002281
3GPP TSG-RAN WG4 Meeting #94-e

## Slide 2: Background
Observation 1: While camping on an unlicensed carrier, if there is PCI collision with the neighbor cells, the current cell reselection and HO requirements for NR-U [R4-1910551] can not be fulfilled because of the additional time for SIB reading.

## Slide 3: Way-Forward(1)
Proposal 1: The requirements for cell reselection in NR-U can be defined as :
DRX cycle length [s] | Tdetect,NR_Intra , Tdetect,NR_Inter [s] {number of DRX cycles} | Tmeasure,NR_Intra, Tmeasure,NR_Inter [s] {number of DRX cycles} | Tevaluate,NR_Intra, Tevaluate,NR_Intra [s] {number of DRX cycles}
0.32 | 0.32x([36]+Md)xM2 {([36]+Md)xM2} | 0.32x([4]+Mm) xM2 {([4]+Mm)xM2} | 0.32x([16]+Me) x M2 {([16]+Me)xM2}
0.64 | 0.64x([28]+Md) {[28]+Md} | 0.64x([2]+Mm) {[2]+Mm} | 0.64x([8]+Me) {[8]+Me}
1.28 | 1.28x([25]+Md) {[25]+Md} | 1.28x([1]+Mm) {[1]+Mm} | 1.28x([5]+Me) {[5]+Me}
2.56 | 2.56x([23]+Md) {[23]+Md} | 2.56x([1]+Mm) {[1]+Mm} | 2.56x([3]+Me) {[3]+Me}
... Note x: Requirements above are applicable when there is no PCI collision for measured neighbor cells deployed in CCA carriers |  |  | 

## Slide 4: Way-Forward(2)
Proposal 2: The requirements for HO in NR-U can be defined as [R4-1910551] :
- “The interruption time for NR FR1 – NR FR1 handover in NR-U:
Tinterrupt = Tsearch + TIU + [20] + ms
where
Tsearch is the time required to search the target cell when the target cell is not already known when the handover command is received by the UE. If the target cell is known, then Tsearch = 0 ms.
If the target cell is an unknown intra-frequency cell and no PCI collision for the neighbor cells measured in CCA carriers, and the target cell Es/Iot≥[-2] dB, then Tsearch = (1+ L1)* Trs + 2 ms. If the target cell is an unknown inter-frequency cell and the target cell Es/Iot≥[-2] dB, then Tsearch = [(3+ L1´)* Trs + 2] ms where L1 and L1´ is the number of DRS occasions missed due to DL LBT during the intra-frequency and inter-frequency detection period, respectively.

## Slide 5: Way-Forward(3)
Proposal 3: For Rel16 NR-U WI, RAN4 will not further discuss the case with PCI collision in carriers using CCA