## Slide 1: WF on NR-U RRM Requirements (Part 1) (all agreements in RAN4#94-e in email thread #46)
Ericsson
3GPP TSG-RAN WG4 Meeting #94-e R4-2002283
Electronic Meeting, February 24-March 06, 2020
Agenda Items: 8.1.4, 8.1.4.1-8.1.4.6, 8.1.4.14

## Slide 2
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Specification Structure
Do not add “a” in section numbers in 36.133 for NR-U sections. Follow the section naming outline earlier agreed in R4-1914628 (RAN4#93)

## Slide 4: General Applicability Rules
Option 2b: no applicability section, exclude the applicability to NR-U by default, unless explicitly stated and:
  the meaning of “for NR-U”/”to NR-U” is clearly defined, e.g. NR-U serving cell, NR-U neighbour cell, relevance for different NR-U scenarios A-C etc.

## Slide 5: SIB Reading in Cell Reselection and Handover Requirements
Discuss WF in R4-2002281 (WF on SIB reading in cell reselection and HO requirements for NR-U, Intel)
  If no agreement in RAN4#94-e, the topic shall not be pursued in the future meetings

## Slide 6: SI Reading in RRC Release with Redirection, RRC Re-establishment, and Paging Interruption Requirements
RAN4 to further discuss the maximum SI acquisition time in paging interruption, RRC re-direction and RRC re-establishment in NR-U
SI acquisition time
  SI maximum acquisition time is expressed as a variable (approach similar to Rel-15) but using a variable name which is different from Rel-15, e.g., TSI,CCA,
  the actual value for TSI,CCA is to be discussed in the performance part, considering LBT failures and receiver assumptions, etc.
Conclusion on soft combining of PDSCH for SIB1 reading:
  soft combing is to be further discussed under performance part
Paging interruption delay requirements
  Paging interruption requirements are to be updated based on the agreement on the above agreements on the SI maximum acquisition time

## Slide 7: Cell Reselection (Excluding SI Reading and Paging)
Mm,max for other DRX cycles (0.64 sec and 1.28 sec):
  Mm,max = [8] for DRX cycle = 0.64 seconds
  Mm,max = [4] for DRX cycle = 1.28 seconds
X dB offset condition for the at least one cell to be checked by the UE:
  Do not specify the X dB offset condition for the at least one cell to be checked by the UE
The maximum number of times Y when any of Md,max, Mm,max, and Me,max, is exceeded before the UE initiates cell selection procedures for the selected PLMN as defined in TS 38.304 is unspecified
  FFS whether and how to capture the above agreement in TS 38.133

## Slide 8: RRC Release with Redirection
Upon exceeding L1,max, the UE shall initiate cell selection procedures for the selected PLMN as defined in TS 38.304
UE behaviour upon exceeding L2,max (max. number of missed PRACH occasions) is FFS until the response LS on UL LBT failures is received from RAN2

## Slide 9: RRC Re-Establishment
Do not specify K3,max
Do not specify K1,max and K2,i,max
Do not specify KSI,max

## Slide 10: SCell Activation
Time period in the known cell condition for SCell activation:
  do not extend the time period in the known SCell condition
Does the interruption window length at SCell activation depend on DL LBT failures?
  Conclusion: postpone discussion till R15 get agreed

## Slide 11: SCell Activation Delay
X=5 ms, Y=5 ms, Z=5 ms
THARQ (in ms) is the timing between DL data transmission and acknowledgement as specified in TS 38.213. In the event of UE not being able to transmit the acknowledgment due to UL CCA failures: THARQ is extended to also include the time to all next HARQ feedback retransmission opportunities, until the time of its successful transmission, as specified in TS 38.213; no extension of THARQ due to UL LBT failures is allowed for channel access category 1
  The term “channel access category 1” needs to be aligned with RAN1 terminology (e.g., in TS 37.213)
TCSI_reporting = TCSI_reporting,ref +L4*TCSI-RS +CSI, where
  TCSI_reporting,ref is CSI reporting delay as specified in section 8.3.2,
  UE behavior upon exceeding L4,max (L4,max=TBD) is to abandon the SCell activation procedure,
  CSI is the total additional delay in CSI reporting due to UL LBT failures, according to TS 38.213
FFS: UE behavior and the SCell activation delay extension due to any LBT failures when sCellDeactivationTimer is not configured
FFS: condition on the delay due UL LBT failures for HARQ in SCell activation delay
  Option 1: For a known SCell:
    TFirstSSB+ Trs *L1+ 5ms, if the SCell measurement cycle is ≤160ms and HARQ≤[TBD] ms.
    (TSMTC_MAX + Trs )*(1+L2)+ 5ms, if the SCell measurement cycle is >160ms or HARQ>[TBD] ms,
    where HARQ is the total time by which THARQ was extended due to UL LBT failures according to the agreements above
  Option 2: Option 1 without the condition on HARQ

## Slide 12: PSCell Addition
Time period in the known cell condition for PSCell addition:
  do not extend the time in the known cell condition in PSCell addition delay requirement
In the event of UE not being able to transmit PRACH due to UL CCA failures on this carrier: PRACH is the total time extended to also include the time to all next PRACH retransmission opportunities, until the time of its successful transmission, as specified in TS 38.213; PRACH=0 for channel access category 1
  The term “channel access category 1” needs to be aligned with RAN1 terminology (e.g., in TS 37.213)

## Slide 13: Active TCI State Switching
Time period in the known state condition for active TCI state switching:
  do not extend the time in the known cell condition in active TCI switching delay requirement
RRC-based:
  FFS: need for RAN2 LS if the UE declares beam failure upon exceeding L1RRC,unknown,max or L2RRC,unknown,max
THARQ (in ms) is the timing between DL data transmission and acknowledgement as specified in TS 38.213. In the event of UE not being able to transmit the acknowledgment due to UL CCA failures: THARQ is extended to also include the time to all next HARQ feedback retransmission opportunities, until the time of its successful transmission, as specified in TS 38.213; no extension of THARQ due to UL LBT failures is allowed for channel access category 1
  The term “channel access category 1” needs to be aligned with RAN1 terminology (e.g., in TS 37.213)