## Slide 1: WF on the option for FR2 FWA UE
NTT DOCOMO, INC.,
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005176
Online Meeting, 20-30 Apr 2020

## Slide 2: Background(1/2)
RAN#87-e approved a new WI on introduction of FR2 FWA UE with maximum TRP of 23 dBm in [1]
  Although PC1 had been already introduced based on the assumption of FWA use, PC1 cannot be adopted by the countries/regions with lower power regulatory requirement.
  It is expected that the new power class requirement in this WI is specified with maximum TRP of 23dBm and maximum EIRP of 43dBm.
In addition to discussion of new power class related RF requirements, how to introduce it in specification is one of the scope of the WI[1]:
  To address the issue described in section 3, one option from the following is chosen:
    Option 1. Existing power class with any modifications/additions (e.g. new UE capability) is reused.
    Option 2. A new power class is defined.

## Slide 3: Background(2/2)
RAN4#94-e-bis discussed following options in [2]:
  Option 1: Existing power class with any modifications/additions (e.g. new UE capability) is reused.
    Option 1-A: Introduce P-max in FR2 so that PC1 can be adopted with maximum power limitation.
    Option 1-B: Introduce new capability to distinguish higher and lower maximum TRP and EIRP limitation.
  Option 2: A new power class (PC5) is defined.
    Option 2-A: Stay as it is.
    Option 2-B: Remove UE type definition.
Many companies support Option 2 but some companies commented that Option 1 need further study.
There was a comment that PC1 platform could be reused for the new power class feature by using IE P-max or new UE capability, which would make total economy scale larger.
  NOTE: As informed by RAN2 LS[3], IE P-max in FR2 has already been introduced at least from signalling perspective.
    2. Introducing a new parameter p-UE-FR2 in the RRCReconfiguration message to configure the total maximum transmit power to be used by the UE across all cell groups for NR-DC on FR2.
  The feasibility of introduction of IE P-max in FR2 will be discussed in WI “Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements” in RAN4.

## Slide 4: Way Forward
RAN4#95-e should decide on following options:
  Option 1: Existing power class with any modifications/additions (e.g. new UE capability) is reused.
    Option 1-1: Introduce new signalling to reuse PC1 platform
    Option 1-2: Define new UE capability for power classes with same min peak EIRP and different spherical coverage requirement, provided the max EIRP and max TRP are same
  Option 2: A new power class (PC5) is defined.
    Option 2-1: Stay as it is.

## Slide 5: Reference to be updated
[1] RP-200503, “New WID on Introduction of FR2 FWA UE with maximum TRP of 23dBm for band n257 and n258”, SoftBank
[2] R4-2005118, “Email discussion summary for [94e Bis][32] NR_FR2_FWA_Bn257_Bn258”, Moderator (SoftBank Corp.)
[3] R4-2003363, “LS on power control for NR-DC”, vivo