## Slide 1: WF on Tx Power for FR2 Rx Requirements
MediaTek Inc.
3GPP TSG-RAN WG4 #94bis-e Meeting R4-2005215
Online, April 20th – April 30th, 2020

## Slide 2: Background
Tx power setting for FR2 ACS and in-band blocking requirements has been missing in current specifications [1].
In [2], the reasoning for defining Tx power at (PUMAX – 4dB) for maximum input power level, ACS case 1, ACS case 2, and in-band blocking requirements as proposed in [3] was provided.
Options for Tx power setting for FR2 Rx requirements are proposed in this meeting [2] for consideration to facilitate the closure of the incomplete specifications for ACS and in-band blocking transmitter output power in FR2.
Two companies preferred Option 1 in first round discussions. No other comment received.

## Slide 3: Way Forward
Options for Tx power settings for FR2 UE Rx requirements:
RAN4 to agree on one of the options in the above table (down-selected from [2]) as the transmitter output power settings for UE Rx requirements in FR2 in next RAN4 meeting.
 | Option 1 | Option 2 | Option 3 | Option 4
REFSENS | PUMAX | PUMAX | PUMAX | PUMAX
Maximum Input Level | PUMAX – 4 dB | PUMAX_L – 4 dB | PUMAX – 4 dB | PUMAX_L – 4 dB
ACS case 1 | PUMAX – 4 dB | PUMAX_L – 4 dB | PUMAX – 4 dB | PUMAX_L – 4 dB
ACS case 2 | PUMAX – 4 dB | PUMAX_L – 4 dB | PUMAX – 24 dB | PUMAX_L – 24 dB
In-band Blocking | PUMAX – 4 dB | PUMAX_L – 4 dB | PUMAX – 4 dB | PUMAX_L – 4 dB

## Slide 4: References
[1] 3GPP TS 38.101-1 V15.9.0 (2020-03)
[2] R4-2003528, “Clarifications on transmitter power for FR2 Rx requirements”, MediaTek Inc.
[3] R4-2000749, “CR for TS 38.101-2: Clarifications on transmitter power for receiver requirements”, MediaTek Inc.