## Slide 1: Way Forward on SCell Dormancy
Ericsson, ...
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, 20 – 30 April, 2020
R4-2005329
Document for: Approval

## Slide 2: Background
Agreements from RAN4#94e
RAN4 to define UE requirements for:
  BWP switch delay from dormancy to non-dormancy
  BWP switch delay from non-dormancy to dormancy
RAN4 to define UE non-dormancy to dormancy switch delay requirements for:
  DCI-based switch
  Timer-based switch
RAN4 to define UE dormancy to non-dormancy switch delay requirements for:
  Scheduled DCI dormancy switch indication
  Non-scheduled DCI dormancy switch indication
  WUS indicated dormancy switch indication
RAN4 initially defines dormancy switch delay requirements for one SCell, after which RAN4 will define dormancy switch delay requirements for multiple SCells

## Slide 3: Background
At RAN4#94e-Bis, the following was discussed:
Triggering method for switching from non-dormancy to dormancy
Conditions for switching requirements to apply
Switching delay from dormancy to non-dormancy
Switching delay from non-dormancy to dormancy
Interruption at switching from non-dormancy to dormancy
Interruption at switching from dormancy to non-dormancy
Measurement requirements during SCell dormancy
Interruptions due to measurements during SCell dormancy
Potential actions due to LS from RAN2 to RAN1

## Slide 4: Issue 2-1-1: Triggering method for switching from non-dormancy to dormancy
Agreement:
Timer-based switching to remain within the requirement scope until otherwise indicated by RAN2
RAN4 to send LS to RAN2 to ask whether RAN2 expects RAN4 to develop delay requirements for timer-based switching from non-dormancy to dormancy

## Slide 5: Issue 2-2-1: Conditions for switching requirements to apply
Agreement:
RAN4 develops generic requirements using Rel-15 BWP switching delay requirements as baseline
RAN4 will further study under which conditions w.r.t. parameter changes and system configurations a faster switching than in the baseline can be achieved

## Slide 6: Issue 2-3-1: Switching delay from dormancy to non-dormancy
Agreement:
For switching during active time, switching delay is the same for
  dormancy indication via DCI 0-1 and DCI 1-1, respectively
  dormancy indication via DCI 1-1 with indication per SCell group and indication per SCell, respectively

## Slide 7: Issue 2-3-2: Switching delay from non-dormancy to dormancy
Agreement:
For switching during active time, switching delay is the same for
  dormancy indication via DCI 0-1 and DCI 1-1, respectively
  dormancy indication via DCI 1-1 with indication per SCell group and indication per SCell, respectively

## Slide 8: Issue 2-4-1: Interruption at switching from non-dormancy to dormancy
Agreement:
Existing Rel-15 BWP change interruption requirements, except for zero interruption, serve as baseline for interruptions on PCell and other SCells due to switching of single SCell from non-dormancy to dormancy
RAN4 is to further study whether triggering outside or inside active time, certain BWP parameter changes, and UE capabilities call for other than baseline interruption requirements

## Slide 9: Issue 2-4-2: Interruption at switching from dormancy to non-dormancy
Agreement:
Existing Rel-15 BWP change interruption requirements, except for zero interruption, serve as baseline for interruptions on PCell and other SCells due to switching of single SCell from dormancy to non-dormancy
RAN4 is to further study whether triggering outside or inside active time, certain BWP parameter changes, and UE capabilities call for other than baseline interruption requirements

## Slide 10: Issue 2-5-1: Measurement requirements during SCell dormancy
Agreement:
Measurement requirements for non-dormancy SCell serve as baseline for measurement requirements for dormancy SCell
RAN4 will further study whether relaxations in RRM and/or CSI measurement requirements shall be allowed for dormancy SCell

## Slide 11: Issue 2-5-2: Interruptions due to measurements during SCell dormancy
Agreement:
The UE is allowed to cause interruptions to communication with other serving cells due to measurements on dormancy SCell
RAN4 will further study what requirements shall apply to the interruptions caused due to measurements during dormancy

## Slide 12: For RAN4#95e
Interested companies are encouraged to provide further analyses on:
Switching delay from dormancy to non-dormancy
  Including conditions under which switching can be faster than in the baseline
  Including whether to consider CSI reporting on top of the BWP switching delay
Switching delay from non-dormancy to dormancy
  Including conditions under which switching can be faster than in the baseline
Interruption at switching from non-dormancy to dormancy
Interruption at switching from dormancy to non-dormancy
Measurement requirements during SCell dormancy
Interruptions due to measurements during SCell dormancy

## Slide 13: For RAN4#95e
For the incoming LS R4-2003371, particularly on Q3, interested companies are encouraged to provide analyses on:
Whether there is an impact on transition between dormancy and non-dormancy by not supporting Aperiodic CSI reporting for dormancy SCell
Whether there is an impact on transition between dormancy and non-dormancy by not supporting SRS transmissions for dormancy SCell
  Including potential impact to UL TA, UL PC, and UL beam management