## Slide 1: Completing the WI including the "blind scheme" that is not blind
Ericsson
3GPP TSG-RAN WG4 Meeting #96-e
Electronic meeting, 17 – 28 August 2020
R4-2010350
Agenda item: 9.2.2
Document for: Approval

## Slide 2: Completing the WI
Two outstanding issues:
Baseline solution supported by all UEs indicating EN-DC PC2 for an FDD-TDD band combination?
Fall-back when EUTRA and NR duty cycles exceeded?

## Slide 3: The ”blind” scheme should be baseline or part thereof
because it
is Rel-15 EN-DC power control
  The total average nominal power can never exceed 23 dBm in line with all other HPUE solutions
  100% FDD duty cycle possible while transmitting on the TDD
can be implemented by a Rel-15 UE (release independence)
can be tested according to the existing 38-101-3 Rel-15 conformance tests
  such as verification of TDD dropping, same principle as PC3
does not require CG coordination for full functionality
  tight coordination on TTI level not supported by inter-node signaling
is actually not blind... neither is an EN-DC PC3 Rel-15
but it requires setting a UE-specific PLTE < 23 dBm
  standard for EN-DC PC3 to make sure TDD is not dropped with LTE at full power, PLTE released if EN-DC is released

## Slide 4: The ”blind” scheme is standard Rel-15 power control
At EN-DC connection establishment, a UE receives by dedicated signaling the UE-specific PLTE (and EN-DC P-Max if configured) along with all other information for the SCG (TDD) needed for establishing the connection like the common U/D pattern(s). Regardless of EN-DC power class
  An EN-DC PC3 uses the power class and the EN-DC P-Max (if configured) to set the maximum total EN-DC power threshold specified in 38.213 Rel-15: the threshold is ≤ 23 dBm
  An EN-DC PC2 would use the power class, the PLTE (set to < 23 dBm) the EN-DC P-Max (if configured), compute the maximum TDD UL duty cycle uD from the common U/D pattern to obtain the maximum total EN-DC power threshold specified in 38.213 Rel-15: the threshold is > 23 dBm up to 26 dBm depending on PLTE and duty cycle
The only difference between PC3 and PC2. Where is the complication?

## Slide 5: The 38.213 Rel-15
The total EN-DC power threshold detemines SCG power scaling (DPS)
and for non-DPS the sum of PLTE and PNR (the blind scheme does not require DPS)
Higher threshold for EN-DC PC2, the only difference from EN-DC PC3

## Slide 6: Example
Set PLTE = 22 dBm (1 dB power reduction) and assume max TDD UL duty cycle 25% as computed from the common pattern(s)
EN-DC PC3:
  total EN-DC threshold: 23 dBm
  max TDD power with concurrent LTE at full power (PLTE): 16 dBm, risk of TDD dropping (more the 6 dB scaling), PLTE = 21 dBm would be safer
  max TDD power without concurrent LTE = EN-DC power = 23 dBm
EN-DC PC3 with NR PC2:
  total EN-DC threshold: 25 dBm
  max TDD power with concurrent LTE at full power (PLTE): 22 dBm, no TDD dropping
  max TDD power without concurrent LTE = EN-DC power = 25 dBm
PC2 yields 6 dB increase of the TDD power for concurrent transmissions
  gain reduced with increased TDD duty-cycle and PLTE (still below 23 dBm)
Uncertain additional benefit with added duty-cycle reporting (including “UE-based P-MPR”)

## Slide 7: The PLTE and maximum duty cycle
The PLTE is UE-specific and is
  configured at EN-DC connection setup (RRC reconfiguration)
  released when EN-DC is released
  not changed during the EN-DC connection (requires a reconfiguration)
Setting the PLTE value for a UE is up to the network
The maximum duty cycle uD is unambiguosly derived from the common U/D patterns
  the cell-specific U/D patterns sent to the UE in dedicated signaling (like all SI for the SCG)
  count the flexible symbols as UL (then uD is unchanged if a dedicated pattern is sent)

## Slide 8: Duty-cycle reporting should be optional
Duty-cycle reporting add-on to the baseline if supported by the UE, i.e. optional with capability reporting
Interpretation of the reported duty-cycle capability uncertain both in the power- and time domain, see [1]
  tight CG coordination is required, but uncertain gain if any
In the example: the UE may be able to set the total EN-DC power threshold at 26 dBm if duty-cycles (EUTRA and NR) are within capability, but uncertain gain for the example in practice
Better consider the PMPR method in addition to the ”blind” scheme, then the EN-DC power threshold can be configured up to 26 dBm also when the operator configures PLTE = 23 dBm or absent
  even if UE behaviour unspecified in that case, the PMPR method is blind, see [1]

## Slide 9: Fallback when duty cycles exceeded
The ”blind” scheme does not need fallback to PC3 (23 dBm), can be the total EN-DC power threshold (25 dBm in the example)
  independent of duty cycles, can be 100% on the FDD as required in SAR testing
For duty-cycle reporting schemes (including ”full duty supported”), fall-back to PC3 is proposed
  then most likely still configure PLTE < 23 dBm to make sure TDD is not dropped in fallback
The baseline ”blind” scheme set the (minimum) fallback level when duty-cycle schemes are used as add-on
  Why fallback to 23 dBm when a PLTE < 23 dBm is configured? Would be a waste of power

## Slide 10: Can be applied to other MR-DC
The blind scheme readily applies for both NR-DC PC2 and TDD-TDD EN-DC PC2
  based on Rel-16 NR-DC and Rel-15 EN-DC power control

## Slide 11: Proposals for closing the work item
The PMPR method with the ”blind scheme” as baseline (default)
  fall back to the blind scheme, the PMPR scheme should provide gains on top of the so-called ”blind” scheme
Duty cycle reporting optional, requires further studies, see [1]
  Finalize details as part of Rel-16 maintenance
CR in [2] with baseline, details on duty-cycle reporting FFS
The WI can be closed without completing RAN2 work, an LS to RAN2 can be sent at a later stage (if needed) as part of Rel-16 maintenance

## Slide 12: What the Ericsson CR does
Set the the total EN-DC power threshold in a range, the minimum level set by the ”blind” scheme, the maximum up to 26 dBm
The total EN-DC power (threshold) never below the level set by the blind scheme
Can be implemented by a Rel-15 UE
Additional test case for the PMPR method, see [1]

## Slide 13: Annex: a note on P-MPR
P-MPR can always be used on each CG as required (no difference from EUTRA)
Applies to all EN-DC PC2 schemes
  The ”blind” scheme only sets a total EN-DC power threshold at which the SCG should be scaled according to 38.213 Rel-15
  The output power on each CG can be reduced as much as required, e.g. if triggered by proximity sensors
    The total EN-DC power threshold need not be modified by P-MPR

## Slide 14: References
R4-2010349, ” Feasibility of reporting: expected UE behaviour with duty-cycle reporting and PMPR method? ”, Ericsson
R4-2010351, ” Introduction of EN-DC power class 2 for FDD-TDD band combinations ”, Ericsson