## Slide 1: WF on EN-DC large BW Cross Band Noise
Qualcomm, Skyworks, Huawei, [ZTE], […]
­­­3GPP TSG-RAN WG4 Meeting # 97-e R4-2016839
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: 2 options were proposed this meeting
Option 1a) (left): Specify RB position for valid MSD for all supported BWs
  Supported by [1], [3], [4].
  Similar approach to LTE, NR single carrier 1UL/2DL NCCA.
Option 1b) (Appendix): Specify MSD for large BW regardless of RB position
  Proposal from last meeting [5].
Problem with Option 1a), 1b) is that it conflicts with Note 3 in the UL configuration table which already limits the UL BW, so no counter IMD type MSD will be observed, unless the note is clarified that it will not apply for the specified BWs indicated.
Option 2 (right): Specify MSD as a function of BW
  Proposal is on principle the same as option 1b), but identifies the MSD issue due to counter IMD specifically.
  May need to introduce MSD in another sub-clause similar to IMD.
  Supported by [2], [MediaTek].
  CIM3 is actually the IM3 of TX with actual CIM3 and can be labelled as CIM3*.
  Consider adding additional column for RB position for no MSD
NOTE 3: When the maximum UL RB allocation “LCRB” value is less than the maximum transmission bandwidth configuration “NRB” defined in Table 5.3.2-1 in 38.101-1 [2] for the specified UL band SCS, the UL band should be configured using the lowest CBW that is compatible with the maximum specified LCRB value.

## Slide 3: WF
Existing MSD values and UL configuration are agreeable [5]
UL RB position or start value of RB allocation for no added MSD is also agreeable
  RB position is assumed to be relative to a start value of 0.
Choices:
  Tentatively Choose option 2 to introduce MSD due to counter IMD due to large BW
    Proponent of option 2 to bring CR next meeting
  Choose no action where UL BW is limited
  Other options not precluded

## Slide 4: References
R4-2014170, “Handling new channel bandwidths for ENDC and NRCA band combinations with MSD”, Qualcomm Inc., 3GPP TSG-RAN WG4 #97-e
R4-2015552, “Consideration on Cross band isolation impact with larger BW”, Huawei, 3GPP TSG-RAN WG4 Meeting # 97-e
R4-2015795, “Discussion on handling the cross-band isolation requirement for larger channel BW in Rel.16”, CHTTL, 3GPP TSG-RAN WG4 #97-e
R4-2015042, “Discussion on the MSD of the new channel BW for EN-DC and NR CA band combinations”, ZTE, 3GPP TSG-RAN WG4 #97-e
R4-2011777, “WF on handling new channel BW’s for EN-DC and NR CA band combinations with MSD”, Qualcomm, MediaTek, CHTTL, [ZTE], 3GPP TSG-RAN WG4 #97-e

## Slide 5: Appendix
Proposal from last meeting 96-e
E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB) | 
n13 | 3 | 3.0 | 2.3 | 2 | 1.8 |  |  |  |  |  |  |  |  | 
n13,5 | 3 | [4.5] | [4.1] | [3.9] | [3.8] |  |  |  |  |  |  |  |  | 
n13,6 | 3 | [16.9] | []16.0 | [14.3] | [13.2] |  |  |  |  |  |  |  |  | 
NOTE 3: These requirements apply when the uplink is active in Band n1, n84 and the separation between the lower edge of the uplink channel in Band n1, n84 and the upper edge of the downlink channel in Band 3 is < 60 MHz. For each channel bandwidth (≤20MHz) in Band 3, the requirement applies regardless of channel bandwidth in Band n1, n84. NOTE 5: Applicable only for n1 UL BW = 25, 30, 40MHz. NOTE 6: Applicable only for n1 UL BW = 50MHz. |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB)
n40 | 1 | 8.3 | 8.3 | 8.3 | 8.3 |  |  |  |  |  |  |  | 
n40 | 13 | [21.5] | [21.5] | [21.5] | [21.5] |  |  |  |  |  |  |  | 
NOTE 3: Applicable only for n40 UL BW = 80MHz. |  |  |  |  |  |  |  |  |  |  |  |  | 
E-UTRA or NR Band / SCS / Channel bandwidth of the affected DL band / UL RB allocation of the agressor band |  |  |  |  |  | 
UL band | DL band | SCS of UL band (kHz) | 5 MHz (LCRB) | 10 MHz (LCRB) | 15 MHz (LCRB) | 20 MHz (LCRB)
n403 | 1 | 30 |  | [50] | [50] | [50]
NOTE 3: Applicable only for n40 UL BW = 80MHz. |  |  |  |  |  | 
NOTE 1: The UL configuration applies regardless of the channel bandwidth of the UL band. UL resource blocks allocation in the table shall be further limited to that specified in Table 7.3.1-2 in TS 36.101 [4] or Table 7.3.2-3 in TS 38.101-1 [2]. NOTE 2: The UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth. NOTE 3: When the maximum UL RB allocation “LCRB” value is less than the maximum transmission bandwidth configuration “NRB” defined in Table 5.3.2-1 in 38.101-1 [2] for the specified UL band SCS, the UL band should be configured using the lowest CBW that is compatible with the maximum specified LCRB value.