## Slide 1: Motivation for supporting non-colocated scenarios for band 42 and n77/n78
SoftBank Corp.
3GPP TSG RAN WG4 Meeting #98-e
Electronic Meeting, January 25 – February 5, 2021
Agenda Item: 16.2.2
Document for: information
R4-2100941
Revision of RP-202563

## Slide 2: Background – Spectrum point of view
Co-existence with other systems
Timing of Spectrum allocation
  The 3 blocks in C-band were allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
SoftBank
X
X
Y
SoftBank
3400
3440
3480
3520
3560
3600
X
Y
Z
SoftBank
Y
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
3rd allocation

## Slide 3: Background – 3GPP point of view
3GPP standards
  Rules for “intra-band” apply to EN-DC 42_n77
  TS38.133 cls. 7.6.3 defines MRTD limit for intra-band EN-DC (=3us)
  Power imbalance limit has been discussed in Rel-16
    One candidate value is 6dB
   These limitations reduce the availability of EN-DC in our network

## Slide 4: Scenario and target value for new perf. Req.
Conditions bw. eNB and gNB
Very short Rx time difference(3us)
Power imbalance (6dB)
Rel-16
eNB
gNB
Deployment scenario
Colocated
Different antenna pattern
Our Proposal
eNB
gNB
Conditions bw. eNB and gNB
Short Rx time difference([10]us)
Power imbalance ([25]dB)
More discussion is necessary to determine the target values
Deployment scenario
Non-colocated (at maximum 3 Tx points)
Different antenna pattern
Our goal: Define UE performance requirements for intra-band EN-DC and NR-CA for non-colocated scenarios

## Slide 5: Proposals
Add the following scope in the WI “Further enhancement on NR demodulation performance”
Requirements for non-colocated scenario for intra-band non-contiguous EN-DC/NR-CA (e.g. band 42, n77/n78)
    Requirements are applicable for UEs capable of FG 2-19 Type 2.
    First investigate the applicable MRTD and power imbalance level, considering the network deployment scenario and UE implementation feasibility.
    Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.

## Slide 6: EOF