## Slide 1: WF on Simultaneous Rx/Tx
Huawei, HiSilicon
R4-2105377
3GPP TSG-RAN WG4 #98-bis-e
Electronic Meeting, Apr. 12-Apr. 20, 2021

## Slide 2: Background
The following issues related to principles for simultaneous Rx/Tx capability have been discussed in RAN4#98-bis-e meeting
  Topic #1: Principles for simultaneous Rx/Tx capability
    Issue 1-1: Applicability of simultaneous Rx/Tx capability for similar band combination
    Issue 1-2: Rules to decide simultaneous Rx/Tx capability for a band combination
    Issue 1-3: Specification impact
    Issue 1-4: Release independent

## Slide 3: WF
Issue 1-1-1: Whether same simultaneous Rx/Tx capability for LTE CA band combination can be applied for the corresponding inter-band NR CA band combination
Agreement
  Yes. Simultaneous Rx/Tx capability for LTE CA band combination can be applied for the corresponding inter-band NR CA band combination.

## Slide 4: WF
Issue 1-1-1a: Whether same simultaneous Rx/Tx capability for NR CA band combination can be applied for the corresponding inter-band NR DC band combination
Options
  Option 1: Yes, same simultaneous Rx/Tx capability for inter-band NR DCCA band combination can be applied for the corresponding inter-band ENDC band combination.
  Option 2: whether the NR-DC configuration is synchronous or not can have an impact on the capability as that for CA
WF
  To be further discussed.

## Slide 5: WF
Issue 1-1-2: Whether same simultaneous Rx/Tx capability for inter-band NR CA ENDC band combination can be applied for the corresponding inter-band ENDC CA band combination
Options
  Option 1: Yes, same simultaneous Rx/Tx capability for inter-band NR CA ENDC band combination can be applied for the corresponding inter-band ENDC CA band combination.
  Option 2: whether the NR-DC configuration is synchronous or not can have an impact on the capability as that for CA
WF
  [Option 1] To be further discussed.

## Slide 6: WF
Issue 1-2-1a: The capability shall be mandatory if low-band (below 1GHz) is aggregated with high (i.e. 2.69GHz and above) and mid-band (1GHz to 2.69GHz) TDD cells
Options
  Option 1: Yes. The capability shall be mandatory if low-band (below 1GHz) is aggregated with high (i.e. 2.69GHz and above) and mid-band (1GHz to 2.69GHz) TDD cells.
  Option 2: The frequency separation can be considered together with MSD rule
WF
  [Option 1] To be further discussed.

## Slide 7: WF
Issue 1-2-1b: The capability shall be mandatory if mid-band (1GHz to 2.69GHz) FDD is aggregated with frequency above 3.3GHz high band TDD cells
Options
  Option 1: study case by case
  Option 2: Yes. Simultaneous capability shall be mandatory for the band combination in mid-band (1GHz to 2.69GHz) aggregated with frequency above 3.3GHz high band TDD cells.
  Option 3: Yes. On top of mandatory capability, for the band combination has MSD issue, specify the corresponding MSD requirements.
WF
  To be further discussed.

## Slide 8: WF
Issue 1-2-1c: The capability shall be mandatory if FR1 FDD band is aggregated with FR2 TDD bands
Options
  Option 1: The capability shall be mandatory if FR1 FDD band is aggregated with FR2 TDD bands
  Option 2: More analysis is needed as FR1 is extended to 7GHz
WF
  [Option 1] To be further discussed.

## Slide 9: WF
Issue 1-2-2: Whether MSD value/threshold or harmonic / IMD order can also be considered as criteria to decide simultaneous Rx/Tx capability
Options
  Option 1: MSD degradation can be considered as a rule to decide whether simultaneous Rx/Tx capability can be supported.
  Option 2: MSD can be considered together with frequency separation. For some mandatory support band combinations, MSD may need to be defined.
  Other options are not precluded
WF
  To be further discussed.

## Slide 10: WF
Issue 1-2-3: Simultaneous Rx/Tx capability according to duplex mode and frequency range
Issue 1-2-3a: Mandatory simultaneous Rx/Tx capability should be supported for all of the FR1+FR1 FDD-TDD CA band combination
Options
  Option 1: Study case by case. Can be considered together with MSD rule.
  Option 2:Mandatory support
WF
  To be further discussed.

## Slide 11: WF
Issue 1-2-3b: Simultaneous Rx/Tx capability should be discussed case by case for the FR1+FR1 TDD-TDD CA band combination
Agreement
  It is agreed that simultaneous Rx/Tx capability should be discussed case by case for the FR1+FR1 TDD-TDD CA band combination.

## Slide 12: WF
Issue 1-2-3c: Mandatory simultaneous Rx/Tx capability should be supported for all of the FR1+FR2 TDD-TDD CA band combination
Options
  Option 1: Yes. Mandatory simultaneous Rx/Tx capability should be supported for all of the FR1+FR2 TDD-TDD CA band combination.
  Option 2: More analysis is needed.
WF
  [Option 1] To be further discussed.

## Slide 13: WF
Issue 1-2-3d: FFS on simultaneous Rx/Tx capability for FR2+FR2 TDD-TDD CA band combination
Options
  Option 1: Study case by case
  Option 2: Not a valid scenario
WF
  To be further discussed.

## Slide 14: WF
Issue 1-2-3e: For SUL band combination, if SUL band is from FDD band, mandatory simultaneous Rx/Tx capability should be supported. If SUL band is from TDD band, simultaneous Rx/Tx capability should be discussed case by case.
Options
  Option 1: Study case by case
  Option 2: Mandatory support
WF
  To be further discussed.

## Slide 15: WF
Issue 1-3-1: Specify the text for the general criteria in the specification so that the combinations that satisfy the general criteria will be mandatory simultaneous RxTx support
Options
  Option 1: Documented in TR
  Option 2: Documented in TS if needed.
WF
  The general criteria can be documented in TRsomewhere. Whether it can be captured in TS is FFS.
  Further discussion based the two options.

## Slide 16: WF
Issue 1-4-1: From which release the capability indicated for a band combination introduced in Rel-17
Options
  Option 1: Rel-17
  Option 2: Follow the normal release independent manner
WF
  To be further discussed.

## Slide 17: WF
Issue 1-4-2: Specify/change the simultaneous TxRx capability only in the Rel-17 spec in this WI and keep Rel-15/Rel-16 simultaneous capability unchanged to avoid NBC issue.
Options
  Option 1: Spec impact for Rel-17 only
  Option 2: Could allow changes for Rel-15/Rel-16 specs.
WF
  To be further discussed.

## Slide 18
Reference
[1] R4-2105194, Email discussion summary for [98-bis-e][121] Simultaneous_RxTx