## Slide 1: WF on Test cases for MR-DC Idle mode CA measurements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #98e - bis
E-meeting, April 12th – April 20th, 2020
R4-2105841
Document for: Approval

## Slide 2: Test case list for [204] LTE_NR_DC_CA_RRM_1_NWM
Baseline agreements for the test cases to be developed were agreed in RAN4#97 and RAN4#98.
  WF R4-2017358
  WF R4-2103547
The TC list on the following page 3 is Approved (in RAN4#98).

## Slide 3: Test cases for MD-DC EMR
TC# | Pcell and serving carrier in idle mode | PSCell and target carrier for early measurements | Cell status for cell measured for early measurements | Beam level reporting configured for early measurements? | s-NonIntraSearch configured? | TC Summary description | Company
1 | NR FR1 | NR FR1 | New Cell | no | no | UE in connected mode with Pcell only, UE configured with early measurement reporting with 1 FR1 carrier which has not been configured in connected mode, Connection is released, New cell is turned on, UE is in Idle mode with time allowing enough measurement time, Connection setup within T331, Network requests early measurement report. | Apple
2 | NR FR1 | NR FR2 | Known cell | yes | no | UE in connected mode with PCell (FR1) and PSCell (FR2), UE configured with early measurement reporting with PSCell carrier, Connection is released, UE is in Idle mode, Change Rxlevel of FR2 cell, Connection setup within T331, Network requests early measurement report. | Nokia
3 | NR FR1 | LTE | Known cell | N/A | yes | UE in connected mode with PCell (FR1) and LTE PSCell, UE is configured with early measurement reporting with LTE PSCell carrier, Connection is released, UE is in idle mode, Change Rxlevel of LTE cell, Connection setup within T331, network requests early measurement report. | Nokia
4 | LTE | NR FR1 | New Cell | yes | yes | UE in connected mode with LTE PCell and NR PSCell (FR1), UE is configured with early measurement reporting with NR PSCell carrier, Connection is released, UE is in Idle mode, New cell is turned on, Change Rxlevel of NR FR1 cell, Connection setup within T331, network requests early measurement report. | Huawei
5 | LTE | NR FR2 | New Cell | no | no | UE in connected mode with LTE PCell only, UE is configured with early measurement reporting with NR FR2 carrier which has not been configured in connected mode, Connection is released, New cell is turned on, UE is in Idle mode allowing enough measurement time, Connection setup within T331, network request early measurement report. | Ericsson

## Slide 4: Measurement performance test cases for SS-RSRP and SS-RSRQ
During 1st round discussions following was summarized:
  Tentative agreements:
    Option 2: ’Test the measurement accuracy within core requirements’ (Ericsson, Huawei, Nokia, Qualcomm, Apple, MediaTek)
Open in 2nd round discussion:
  There are still some open aspects for discussion related to following:
    how to test (Apple, Nokia and Huawei) and
    the actual test case layout (Anritsu, R&S)

## Slide 5: Measurement performance test cases for SS-RSRP and SS-RSRQ
During 1st round discussions following was summarized:
  Tentative agreements:
    Option 2: ’Test the measurement accuracy within core requirements’ (Ericsson, Huawei, Nokia, Qualcomm, Apple, MediaTek)
During 2nd round discussion the tentative agreement was agreed:
  Agreement:
    Test the measurement accuracy within core requirements

## Slide 6: Way Forward
During RAN4#98bis following aspect related to measurement performance testing remained open:
  Companies should provide input on how to ensure that the test cases also enable testing measurement performance for (SS-)RSRP and (SS-)RSRQ.
    Proposals
      Option 1: Include the needed test settings in the test case to enable that measurement performance requirements can be tested against agreed accuracies.
      Option 2: Other

## Slide 7: For RAN4#99
Test cases endorsed in RAN4#98e-bis will be collected in a Big Draft CR, which after e-mail endorsement will serve as baseline for future work.
This Big CR should be as baseline for further work on the test cases.

## Slide 8: Collection of some agreements from RAN4#98bis
Define measurement performance test cases for SS-RSRP and SS-RSRQ measurement accuracies for LTE-NR_DC_CA
  Measurement period and accuracy shall be verified in the same test.
Issue 2-5-1: Measurement performance test coverage.
  Option 1: Follow the test case list for serving cell and measured target cell. Hence, include measurement performance on all test cases
Issue 2-6-1: Measurement performance test of RSRP and RSRQ.
  Option 1: Test measurement performance of (SS-)RSRP and (SS-)RSRQ in each test case.