## Slide 1: WF on duty cycle signaling for RF exposure mitigation for PC1.5 FWA
Samsung
R4-21xxxxx
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May 19th – 27th 2021
Agenda: 8.31

## Slide 2
In [1], it is agreed to reuse existing mechanism for PC1.5 to meet the regional SAR limit for n77 and n78 handheld device
  Currently, the default duty cycle limit is 25% for PC1.5 if nothing is reported
  Otherwise, it is half the reported value since the same IE is used for PC2 reporting as well
In RAN4#98-bis-e, following approaches were discussed without consensus
  P-MPR: Baseline method. UE centric solution with other optional solutions
  Duty cycle: Optional method. e.g., same with smartphone (25%), or others (e.g. 50%)
  Antenna gain (G_tx): Optional method. e.g., G_tx assumption with/without duty cycle
  Other options are not precluded
Background

## Slide 3
In [2], it is presented that Gtx based specification is found to be challenging due to the uncertainty and variation in Gtx as well as the possible declared value of distance, R, by the manufacturer for compliance
In RAN4#99-e, following options were discussed for FWA MPE handling. Option 2 is discarded based upon the discussion (See Annex for detail)
  Option 1: Adopt the FR1 maxUplinkDutyCycle-PC2-FR1
  Option 2: Adopt the FR2 maxUplinkDutyCycle-FR2
  Option 3: Adopt the hybrid maxUplinkDutyCycle-FWA-FR1
RAN4 will further discuss how to define the optional solutions along with the signaling method for FWA devices in RAN4#100-e
Way Forward: FWA MPE

## Slide 4
Proposed duty cycle options
Annex

## Slide 5
[1] | RP-202912 | New WID on high-power devices operation use cases over Band n77 and n78 | 
[2] | R4-2109843 | MPE handling for high power FWA UE in FR1 | Samsung
References