## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 AH Hong Kong, China, 28 - 30 June, 2016
Nokia, Ericsson, Huawei, ZTE, [DoCoMo]
Way forward on NPRACH simulation assumptions
R4-79AH-0256

## Slide 2: Background
It is observed that significant gap exists between NPRACH detection performance and timing estimation performance.
  Ref: R4-164350, R4-164351
It is observed that cell-ID and signature have significant impact on NPRACH ToA estimation performance
  Ref: R4-79AH-0067

## Slide 3: Way Forward
The choice of cell-ID and signature shall be included in NPRACH simulation assumptions
Assumptions of cell-ID and signature 0
  Signature: 0
  Cell-ID: [0, random ID]
  Timing offset delay: [30us] for NPRACH PF0

## Slide 4: Updated Simulation assumptions
Parameter | Values
NPRACH preamble format | 0
Number of Repetitions | 2, 8, 32
Number of Subcarriers | 12
Antenna configuration | 1 x 2
Cell-ID | [0, random cell-ID 503, 447]
NPRACH signature | 0
Timing offset (us) | [30]
frequency offset | 0Hz (AWGN); [200Hz] EPA1
Propagation channels | AWGN, EPA1
Detection performance | Missed detection rate (1%) with false alarm rate (0.1%)
Timing estimation | Timing error probability with limits 2.5us, [5us]