## Slide 1: 3GPP TSG-RAN WG4 Meeting #AH-1808 Montreal, Canada, 2th – 6th July, 2018
Huawei, …
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1809292

## Slide 2: PUCCH Requirements
Format:
  Define requirements for PUCCH format 0,1,2,3 and 4
  Define the applicability for each PUCCH format based on gNB declaration

## Slide 3: Test setup
Test metric
  PF0
    DTX to Ack probability <1%
    Missed Ack probability < 1%
  PF1
    DTX to Ack probability <1%
    Missed Ack probability < 1%
    PF1: NACK to ACK probability < 0.1%
  PF2/3/4:
    Option 1: Use 1% DTX to ACK, [0.1% NACK to ACK] and 1% ACK missed detection test metric for payload size of 3-11 bits; Use 1% BLER for payload size larger than 11 bits
    Option 2: Use 1% BLER for all kinds of UCI bits
Modulation: QPSK
Only slot-based PUCCH performance requirements
Hopping
  Intra-slot frequency hopping: enable
  Group and sequence hopping: disable

## Slide 4: Simulation assumption for format 0
Number of bits: 1bit
Number of OFDM symbols
  2 OFDM symbol

## Slide 5: Simulation assumption for format 1
Number of bits: 2 bits
Number of OFDM symbols
  {4,10,14} OFDM symbols

## Slide 6: Simulation assumption for format 2
Case 1: Small block length of UCI [3-11] bits
  Number of bits: 4 bits
  Number of OFDM symbols: 1 symbol
  Number of PRBs: 4 PRBs
Case 2: Polar code for UCI >=12bits and < 20bits
  Number of bits: 16 bits
  Number of OFDM symbols: 1 symbols
  Number of PRBs: 5 PRBs
Case 3: Polar code for UCI >=20bits
  Number of bits: 22 bits
  Number of OFDM symbols: 2 symbols
  Number of PRBs: 9 PRBs
small block lengths with
bits information

## Slide 7: Simulation assumption for format 3
Case 1: Small block length of UCI [3-11] bits
  Number of bits: 4 bits
  Number of OFDM symbols: 4 symbol
  Number of PRBs: 1 PRB
Case 2: Polar code for UCI >=12bits and < 20bits
  Number of bits: 16 bits
  Number of OFDM symbols: 14 symbols
  Number of PRBs: 1 PRB
Case 3: Polar code for UCI >=20bits
  Number of bits: 22 bits
  Number of OFDM symbols: 10 symbols
  Number of PRBs: 2 PRBs
DMRS pattern
  With additional DMRS

## Slide 8: Simulation assumption for format 4
Case 1: Small block length of UCI [3-11] bits
  Number of bits: 4 bits
  Number of OFDM symbols: 4 symbol
Case 2: Polar code for UCI >=12bits and < 20bits
  Number of bits: 16 bits
  Number of OFDM symbols: 10 symbols
Case 3: Polar code for UCI >=20bits
  Number of bits: 22 bits
  Number of OFDM symbols: 14 symbols
Number of PRBs: 1 PRB
Block-wise spreading:
DMRS pattern
  With additional DMRS