## Slide 1
NB-IoT SIG Test Issues
for Discussion
2016.5
CATT, CMCC, TDIA, StarPoint

## Slide 2: New Test States 1/2
The figure below shows NB-IOT UE test states which can be used in the initial condition of the test cases.
(Note: In some TCs the UE may be transferred from State 1 to State 2 directly, while in some others the UE may be transferred from State 1 to State 2 through State 2B, FFS)
State 1 Switched OFF
State 2B Registered without PDN Idle Mode
State 2 Registered Idle Mode
State 2A Registered Test Mode Activated
State 2C Registered without PDN Test Mode Activated for Data over NAS
State 3B SRB Established
State 3 Generic RB Established
State 3A Generic RB Established Test Mode Activated
State 3C SRB Established Test Mode Activated for Data over NAS
State 4 Loopback Activated
State 4A Loopback Activated for Data over NAS

## Slide 3: New Test States 2/2
 |  | RRC | ECM | EMM | ESM
State 1 | Switched OFF | ----- | ----- | ----- | -----
State 2 | Registered, Idle Mode | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | 1 default EPS bearer context active.
State 2A | Registered, Idle Mode, UE Test Mode Activated | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | 1 default EPS bearer context active.
State 2B | Registered, without PDN, Idle Mode | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | No EPS bearer context active
State 2C | Registered, without PDN,Idle Mode, UE Test Mode Activated | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | No EPS bearer context active.
State 3 | Generic RB Established | RRC_CONNECTED 1 + N (0 ≤ N ≤ 1) data radio bearers configured as specified in the test cases. | ECM-CONNECTED | EMM-REGISTERED | 1 default EPS bearer context active and N (0 ≤ N ≤ 1) dedicated EPS bearers active as specified in the test cases.
State 3A | Generic RB Established, UE Test Mode Activated | RRC_CONNECTED 1 + N (0 ≤ N ≤ 1) data radio bearers configured as specified in the test cases. | ECM-CONNECTED | EMM-REGISTERED | 1 default EPS bearer context active and N (0 ≤ N ≤ 1) dedicated EPS bearers active as specified in the test cases.
State 3B | SRB Established | RRC_CONNECTED | ECM-CONNECTED | EMM-REGISTERED | No EPS bearer context active
State 3C | Loopback Activated, CP CIOT optimization only | RRC_CONNECTED | ECM-CONNECTED | EMM-REGISTERED | No EPS bearer context active.
State 4 | Loopback Activated | RRC_CONNECTED 1 + N (0 ≤ N ≤ 1) data radio bearers configured as specified in the test cases . | ECM-CONNECTED | EMM-REGISTERED | 1 default EPS bearer context active and N (0 ≤ N ≤ 1) dedicated EPS bearers active as specified in the test cases.
State 4A | Loopback Activated(for data over NAS under CP only) | RRC_CONNECTED | ECM-CONNECTED | EMM-REGISTERED | No EPS bearer context active.
Note: States in black are imported from legacy LTE, states in red are new.

## Slide 4: New Test loop function
The existing UE test loop functions for layer 2 (MAC, RLC, PDCP) and data radio bearer testing of Legacy LTE are based on DRB data’s loopback through User Plane.
It has been agreed that CP solution is mandatory for NB-IoT UE. A New UE test loop function is required in TS 36.509 and New Layer 2 test models are required in TS 36.523-3 for MAC/RLC and Data over NAS testing through Control Plane.
Affected test cases:
almost all MAC test cases, all RLC test cases and some multilayer test cases under CP solution.

## Slide 5: New AT Command
    On the UE side, since the CP CIOT optimization , UP CIOT optimization and attach without PDN are related to UE’s behavior, and CP solution is mandatory , it may be possible to add two new AT commands, one for UE initiating UP CIOT optimization negotiation and one for attach without PDN negotiation.
    On the test system side, it may be possible to specify generic procedures for bringing UE into state 2B, state 2C, state 3C, and state 4A respectively.

## Slide 6: Issues left for Clarifications
The conditions, restrictions and usages for RRC connection established with cause “mo-ExceptionData” (RAN2/CT1)
Whether resume procedure could be applied under CP solution (RAN2/SA2)

## Slide 7: Test Case Optimization Policies
Using a single TC cover several general features under normal in different layers, such as: PLMN selection, Attach/Detach, AUT, SEC, Paging, RRC Con Est/Reconf/Release…
REJECT/Abnormal TCs
Using CP solution / Single Tone as the default configurations and avoiding duplicated testing for the same functionality under other configurations (UP / Multi Tone)
RAN2 has agreed that both RRC connection Establishment and Resume are subject to Access Barring. Is the AC test cases under resume scenario need?( same situation in MFBI test cases TC 6.1.2.19, TC 6.1.2.20, TC6.1.2.21 and EAB test cases TC 8.1.2.7 and so on.)

## Slide 8: Organization of Test Specs
287 signaling testcases roughly estimated (before Testcase optimization)
12 sub clauses covers most chapters of 36.523-1
60% testcases may be co-exist with the legacy test cases, 20% testcases need modification greatly, 20% are totally new.
Proposals：
Separate all testcases in 36.523-1 within all chapters
Separate chapter for NB-IoT in 36.523-1 (36.508)
Separate TS for NB-IoT(IoT)

## Slide 9
Thanks