## Slide 1: Discussion of RF/RRM test frequency selection approach
China Mobile
3GPP TSG RAN WG5 Meeting #72 R5-166172
Gothenburg, Sweden 22nd - 26th August 2016

## Slide 2: Background: WF from 1#Adhoc
NB-IoT core requirements for reference design architecture are based on one wideband filter across all bands in low frequencies (729MHz – 1GHz) and one across higher frequencies (1805MHz – 2200MHz), which is reflected in the RAN4 WF for OOBB, in R4-164900.
Based on this approach the test frequency selection for all TRx test cases will be made across all the bands UE supports in these lower or higher frequencies
  E.g. Tested Frequency: Low range of the lowest supported band in 729MHz-1GHz frequencies
For most cases the test frequency selection can be generic across chapters 6 & 7, but some requirements need exceptions :
  E.g. Occupied bandwidth, UE Co-existence, Out-of-band blocking

## Slide 3
WF in 1#Adhoc was agreed based on a R4-164900. This Tdoc provided an analysis only for OOB test case. However, RAN5 applied R4-164900 conclusions to all TRx test cases
  According to RAN4, OOB blocking UE performance is mainly determined by the wide band filter considered in the UE architecture. Such information was used to define UE requirements.
  However, for other UE requirements, wide band filter will not be dominant factor in the UE performance. For example, in MOP test case, PA in UE architecture is supposed to have more impact on UE performance than filters.
  Hence, each UE requirement will be mainly determined by different elements on UE TRx chain.
Observations of 1#Adhoc WF (1/2)

## Slide 4: Observations of 1#Adhoc WF (2/2)
In R5-165691, concerns are expressed, with this method some bands will never be tested and UE performance are unknown.
  The previous WF only considers the filter side and has not considered other RF components as described in R5-165691. The PA, switch, etc, may perform differently in different bands which will cause TX/RX performance difference;
  The insertion loss of wide band filter used for NB-IoT UE is non-ideal and the differences within 300MHz BW may even be larger than 2dB which also cannot be ignored.
Only test two edge of the wide-band filter could not guarantee UE performance under bands in the middle.

## Slide 5: Discussion of additional test frequency selection
Considering the problems mentioned above, there are two methods to verifying UE performances in the middle bands.
  Method 1: Test all the mid freq of each supported mid bands;
    Pros: UE performance in all the bands can be verified;
    Cons: Test time will increase with supported bands.
  Method 2: Test only one mid freq of all the supported mid bands which is closest to the middle.
    Pros: Test time will not be added much and UE performance can be verified partially;
    Cons: There still is possibility that UE could have poor performance in some unverified bands.
Depending on test case, either method 1 or 2 may be most suitable.
  In individual test cases, other selection methods can not be precluded but those will need to be analyzed and justified.
Proposal:
  For most important cases such as Max Output Power and Reference Sensitivity test all the mid freq of each supported mid bands (method 1).
  For other cases as default only test one mid freq of all supported mid band which is closest to the middle (method 2).
  Pros: Test time will be acceptable and most important TX/RX cases in the mid bands can also be verified;