## Slide 1: Further enhancements on signalling reduction to enable light connection for LTE
Intel Corporation
3GPP TSG RAN Meeting #71 RP-160425
Gothenburg, Sweden, 7th – 10th March 2016

## Slide 2: Limitations of current LTE Idle/Active transition
Current design for LTE (Rel-12) is not efficient in term of scalability to support a large number of devices that generate frequent small volume of data
  Frequent small burst transmission: device wakes up and sends data every few minutes.
    For the normal procedure, UE may need to follow the RACH procedure and subsequently establish an RRC connection with the eNB.
    The signalling overhead is substantial when considering only a small amount of data is transmitted in the uplink
    Excessive signaling also leads to
      Additional latency
      Additional power consumption
    Signaling reduction is required not just for stationary NB-IoT/MTC devices but also for all UEs that are mobile

## Slide 3: NB-IOT User plane solution and its applicability
User plane optimisation:
  Provides user plane solution with Signalling reduction during “Idle/Active” transition by storing and re-using last used Access Stratum configuration
  Designed primarily for NB-IOT but expected to be extended to non-NB-IoT devices
    Radio interface changes (Resume message) for resumption in another eNB may also be supported
Limitations of User plane solution in Rel-13
  Not possible to optimise based on UE mobility and traffic mix due to:
    UE tracking based on NAS TA
    UE Paging based on NAS DRX
  Idle/Active transitions generate S1 signalling towards CN
=> Non-optimal configuration limits applicability of suspended state
NB-IOT (eMTC) is discussing User plane optimisation solution for signalling optimisation (called solution 18)

## Slide 4: Limitations of keeping UE in Connected mode DRX
No reduction in signalling during UE mobility
  Handover procedure needs to be supported at every cell change causing:
    Radio and network signalling, UE power consumption and network processing
    CN related S1 signalling
  HO Procedure needed even if the UE has no data to send over several cell changes
    Cell crossing more likely in dense urban deployment
  Longer DRX leads to increased RLF
    Non-optimal recovery procedure leading to additional signalling
    Recovery procedure needed even if there is no data for UE
=> Keeping UE in connected mode DRX is not optimal for UEs that are mobile but generate data less frequently compared to Handovers

## Slide 5: Lightly Connected state to reduce signalling
Lightly connected state to reduce signalling
  Network and UE store UE configuration
  No Handover
  Re-use Suspend/Resume procedures from User plane solution
Further enhancements to allow RAN to choose optimum parameters
  The flexibility for RAN to adjust DRX parameters applicable in Lightly connected state
    Allows RAN to optimise DRX taking into account UE’s current data QoS requirements
  RAN controlled UE specific tracking area that could be different (e.g., smaller) than TA
    Allows RAN to optimise tracking area/Paging area taking into account UE’s current mobility and traffic pattern and trade-off among UE power consumption, signalling overhead, and MO/MT data latency
  Optimum parameters allow eNB to use Lightly connected state more often
Reduce signalling to CN over S1 interface due to mobility and Idle/Active transition. E.g.,
  Hide Lightly connected state from CN
  RAN originated Paging message
  Use Anchor/Gateway function

## Slide 6: Overall benefits summary
Signalling reduction over radio interface
  Larger network capacity
  Lower UE battery consumption
  Lower Idle/Active transition delay
Signalling reduction over network interfaces
  Reduced load on MME during Idle/Active transition and UE mobility
Wider application of LC-state provides more saving
  Allows LC-state to be applied for all UEs
  Optimum choice of LC-state parameters based on traffic/mobility pattern provides more scenarios where LC-state can be used
Evaluation criteria | LC-state
Over-the-air signaling overhead reduction: UL | 63.9% (for one UL/DL packet)
Over-the-air signaling overhead reduction: DL | 73% (for one UL/DL packet)
C-plane latency – idle to connected transition (legacy*: ~96ms) | ~30.5ms (66% reduction)
Number of radio messages (legacy: 8) | 4 (50% savings)
Handover signalling reduction | No HO signalling in LC-state within a given area
Paging message savings | Can be controlled by eNB
*Reference: TR 36.912, TS 36.331