## Slide 1
Andrew Bennett (SA2 Chair, Samsung)
Maurice Pope (SA2 Support, MCC)
SA2 Status Report to
TSG SA#107

## Slide 2: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 3: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 4: 1) General Aspects (1/7)
SA2 meetings held since SA#106
  SA2#166AHE: 20 - 24 January (e-meeting)
  SA2#167: 17 - 21 February 2025, Athens, Greece
Upcoming SA2 meetings (Q2 2025)
  SA2#168: 07 – 11 April 2025, Goteborg, Sweden
  SA2#169: 19 – 23 May 2025, Fukuoka, Japan

## Slide 5: 1) General Aspects (2/7)
SA2 WG leadership
  Chair: Andrew Bennett (Samsung)
  Vice Chairs: Dario Serafino Tonesi (Qualcomm), Wanqiang Zhang (Huawei)
  Secretary: Maurice Pope (MCC)
Many thanks to Maurice Pope, and Vice Chairs Wanqiang Zhang and Dario Serafino Tonesi, for their outstanding support during this quarter
Many thanks also to the moderators of the Rel-20 5GA topics discussed so far

## Slide 6: 1) General Aspects (3/7)
Statistics at SA WG2 #166-Ad-hoc-e (20-24 January 2025, electronic meeting):
148 delegates ‘attended’ (checked-in) for SA WG2 #166-Ad-hoc-e 368 registered for the e-meeting
  1313 documents (including revisions), (184 documents were not handled) including:
    965 CRs (including revisions)
    75 Incoming LSs, of which 22 were postponed
    22 Outgoing LSs Approved
  124 other documents postponed
Total CRs agreed: 219 (excluding agreed CRs which were revised at SA2#167)
Statistics at SA WG2 #167 (17 – 21 February 2025, Athens, Greece):
348 delegates ‘attended’ (checked-in) for SA WG2 #167 95 registered for ‘On-Line’ participation
  1321 documents (including revisions), (299 documents were not handled) including:
    962 CRs (including revisions)
    31 Incoming LSs, of which 10 were postponed
    9 Outgoing LSs Approved
  36 other documents postponed
Total CRs agreed: 179
823 people registered on the SA WG2 e-mail reflector on 3 March 2025

## Slide 7: 1) General Aspects (4/7)
Chart: SA WG2 meeting attendance

## Slide 8: 1) General Aspects (6/7) Document Handling / Meeting
Number of Tdocs
Chart: 

## Slide 9: 1) General Aspects (7/7) SA2 Agreed CRs by Release / Meeting
Number of CRs
Chart: 
| REL-14 FREEZE: 116-bis | 117 | 118 | 118bis | 119 | 120 | 121 | 122 | 122bis | 122e | 123 | REL-15 FREEZE: 124 | 125 | 126 | 127 | 127bis | 128 | 128bis | 129 | 129bis | 130 | 131 | 132 | REL-16 FREEZE: 133 | 134 | 135 | 136 | 136AH | 137-e | 138-e | 139-e | 140-e | 141-e | 142-e | 143-e | 144-e | REL-17 FREEZE: 145-e | 146-e | 147-e | 148-e | 149-e | 150-e | 151-e | 152-e | 153-e | 154 | 154AH-e | 155 | 156-e | 157 | 158 | 159 | 160 | 160AH-e | 161 | 162 | 163 | 164 | 165 | 166 | 166AH-e | 167
Rel-15 PCR/draftCR | 63 | 126 | 117 | 121 | 171 | 214 | 62 | 287 | 328 | 182 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-15 CR | 19 | 19 | 27 | 27 | 12 | 351 | 201 | 213 | 119 | 159 | 100 | 102 | 78 | 74 | 50 | 40 | 17 | 6 | 10 | 3 | 4 | 6 | 2 | 5 | 6 | 0 | 3 | 2 | 1 | 2 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-16 PCR/draftCR | 43 | 80 | 170 | 147 | 181 | 171 | 207 | 250 | 88 | 87 | 71 | 103 | 26 | 39 | 30 | 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-16 CR | 2 | 3 | 66 | 133 | 117 | 233 | 279 | 205 | 260 | 174 | 197 | 248 | 31 | 123 | 79 | 9 | 74 | 8 | 29 | 38 | 0 | 31 | 17 | 1 | 13 | 8 | 2 | 1 | 3 | 1 | 2 | 2 | 3 | 1 | 2 | 0 | 3 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Rel-17 PCR/draftCR | 48 | 55 | 91 | 0 | 0 | 348 | 407 | 356 | 276 | 158 | 113 | 146 | 144 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-17 CR | 12 | 0 | 0 | 0 | 209 | 135 | 262 | 314 | 189 | 236 | 202 | 107 | 57 | 77 | 45 | 12 | 36 | 4 | 26 | 4 | 24 | 13 | 8 | 4 | 13 | 6 | 0 | 4 | 1 | 0 | 3 | 2
Rel-18 PCR/draftCR | 245 | 440 | 599 | 535 | 306 | 69 | 57 | 17 | 27 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rel-18 CR | 0 | 0 | 0 | 0 | 25 | 83 | 240 | 215 | 290 | 272 | 226 | 184 | 198 | 208 | 118 | 75 | 21 | 88 | 41 | 2 | 37 | 15
Rel-19 PCR/draftCR | 85 | 126 | 35 | 126 | 119 | 36 | 31 | 27 | 37 | 0 | 26 | 29 | 168 | 175 | 228 | 85 | 36 | 9 | 13 | 14 | 10
Rel-19 CR | 67 | 69 | 23 | 111 | 156 | 44 | 50 | 39 | 36 | 0 | 0 | 0 | 0 | 0 | 6 | 15 | 144 | 108 | 148 | 179 | 162

## Slide 10: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 11: 2.1) Rel-16 and before Maintenance (1/1)
Rel-12 |  | None
Rel-13 |  | None
Rel-14 |  | None
Rel-15 | 5GS_Ph1 | TEI17: 2 CRs to TS 23.502 TEI18: 1 CR to TS 23.501, 1 CR to TS 23.502 TEI19: 6 CRs to TS 23.501, 4 CRs to TS 23.502, 1 CR to TS 23.503, 1 CR to TS 23.228
Rel-15 | Excluding 5GS_Ph1 | None
Rel-16 |  | Vertical_LAN, TEI18: 1 CR to TS 23.501, 1 CR to TS 23.502
Maintenance CR’s since SA#106
(Cat A CR’s are not counted in these totals)

## Slide 12: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 13: 2.4) Rel-17 Work Summary
Acronym | Work Item Title | WID# | Progress since last TSG SA meeting
5GSAT_ARCH | Architecture aspects for using satellite access in 5G | SP-200445 | No CRs
eEdge_5GC | Enhancement of support for Edge Computing in 5G Core network | SP-201107 | 1 CR to TS 23.501 (Rel-19)
IIoT | Study on enhanced support of Industrial Internet of Things | SP-200973 | No CRs
5G_ProSe | Proximity based Services in 5GS (5G_ProSe) | SP-201132 | No CRs
MUSIM | System enablers for Multi-USIM devices | SP-200978 | No CRs
5MBS | Architectural enhancements for 5G multicast-broadcast services (5MBS) | SP-201106 | 2 CRs to TS 23.247 (1 Rel-17, 1 Rel-19)
eNS_Ph2 | Enhancement of Network Slicing Phase 2 | SP-200976 | No CRs
eNA_Ph2 | WID on Enablers for Network Automation for 5G - phase 2 | SP-201133 | 3 CRs to TS 23.288 (Rel-19)
eNPN | Enhanced support of Non-Public Networks | SP-200980 | No CRs
ID_UAS | Support of Unmanned Aerial Systems Connectivity, Identification, and Tracking | SP-200979 | 2 CRs to TS 23.256 (Rel-17)
eV2XARC_Ph2 | Architecture enhancements for 3GPP support of advanced V2X services – Phase 2 | SP-210090 | No CRs
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture Phase 2 | SP-200977 | No CRs
5G_AIS | 5G System Enhancement for Advanced Interactive Services | SP-190564 | No CRs
5G_eLCS _Ph2 | Enhancement to the 5GC LoCation Services-Phase 2 | SP-200082 | No CRs
MPS2 | Multimedia Priority Service (MPS) Phase 2 | SP-200519 | 1 CR to TS 23.228 (Rel-17)
MINT | Minimization of Service Interruption | SP-210582 | No CRs
ARCH_NR_REDCAP | Architecture Enhancement for NR Reduced Capability Devices | SP-211100 | No CRs
IoT_SAT_ARCH_EPS | Architecture support for NB-IoT/eMTC Non-Terrestrial Networks in EPS | SP-211306 | No CRs
NR_QoE_enh-Core | [RAN3] Core part: Enhancement on NR QoE management and optimizations for diverse services | RP-223488 | No CRs

## Slide 14: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 15: 2.5) Rel-18 Study/Work (1/5)
Acronym | Work Item Title | WID# | Remarks
5GSATB | 5G System with Satellite Backhaul | SP-230111 | No CRs
5GSAT_Ph2 | Satellite access, Phase2 | SP-230109 | No CRs
PIN | Personal IoT Networks | SP-221343 | No CRs
UAS_Ph2 | Phase 2 of UAS, UAV and UAM | SP-230091 | 1 CR to TS 23.256
Ranging_SL | Ranging based services and sidelink positioning | SP-230106 | 1 CR to TS 23.273, 2 CRs to TS 23.586
5G_eLCS _Ph3 | Enhancement to the 5GC LoCation Services-Phase 3 | SP-230093 | 4 CRs to TS 23.273
5G_ProSe_Ph2 | Proximity-based Services in 5GS Phase 2 | SP-230097 | 1 CR to TS 23.304
GMEC | Generic group management, exposure and communication enhancements | SP-230101 | 1 CR to TS 23.502

## Slide 16: 2.5) Rel-18 Study/Work (2/5)
Acronym | Work Item Title | WID# | Remarks
AIMLsys | System Support for AI/ML-based Services | SP-230095 | No CRs
5MBS_Ph2 | Architectural enhancements for 5G multicast-broadcast services Phase 2 | SP-230099 | 1 CR to TS 23.247
eNS_Ph3 | Network Slicing Phase3 | SP-230104 | 2 CR to TS 23.501
XRM | XR (Extended Reality) and media services | SP-230092 | 1 CR to TS 23.501, 1 CR to TS 23.502, 3 CRs to TS 23.503
NR_REDCAP_Ph2 | 5GS support of NR RedCap UE with long eDRX for RRC_INACTIVE State | SP-230171 | No CRs
NG_RTC | System architecture for next generation real time communication services | SP-230098 | 2 CRs to TS 23.228
ATSSS_Ph3 | Access Traffic Steering, Switching and Splitting support in the 5G system architecture; Phase 3 | SP-221334 | No CRs

## Slide 17: 2.5) Rel-18 Study/Work (3/5)
Acronym | Work Item Title | WID# | Remarks
UPEAS | UPF enhancement for Exposure And SBA | SP-230103 | 2 CRs to TS 23.501, 4 CRs to TS 23.502
EDGE_Ph2 | Edge Computing Phase 2 | SP-230112 | 1 CR to TS 23.501, 1 CR to TS 23.502, 4 CRs to TS 23.548
TRS_URLLC | 5G Timing Resiliency and TSC & URLLC enhancements | SP-230107 | No CRs
VMR | Architecture Enhancements for Vehicle Mounted Relays | SP-230105 | No CRs
5WWC_Ph2 | Support for 5WWC, Phase 2 | SP-230367 | 1 CR to TS 23.502, 2 CRs to TS 23.316
MPS_WLAN | MPS when access to EPC/5GC is WLAN | SP-230108 | No CRs
AMP | 5G AM Policy | SP-221335 | No CRs
eNA_Ph3 | Enablers for Network Automation for 5G - phase 3 | SP-230110 | 1 CR to TS 23.501, 6 CRs to TS 23.288

## Slide 18: 2.5) Rel-18 Study/Work (4/5)
Acronym | Work Item Title | WID# | Remarks
eNPN_Ph2 | Enhanced support of Non-Public Networks | SP-230096 | No CRs
eUEPO | Enhancement of 5G UE Policy | SP-230094 | 1 CR to TS 23.502, 2 CRs to TS 23.503
SFC | System Enabler for Service Function Chaining | SP-230120 | No CRs
DetNet | 5GS DetNet interworking | SP-230172 | 1 CR to TS 23.501, 1 CR to TS 23.503
SUECR | Seamless UE context recovery | SP-220810 | No CRs

## Slide 19: 2.5) Rel-18 Study/Work (5/5)
Acronym | Work Item Title | WID# | Remarks
TEI18_SDNAEPC | Secondary DN authentication and authorization in EPS IWK case | SP-220798 | No CRs
TEI18_MLR | Multiple location report for MT-LR Immediate Location Request for the regulatory service | SP-220795 | No CRs
TEI18_MBS4V2X | MBS support for V2X services | SP-220793 | No CRs
TEI18_SLAMUP | Spending Limits for AM and UE Policies in the 5GC | SP-220794 | No CRs
TEI18_ADEE | Enhancement of Application Detection Event Exposure | SP-220796 | No CRs
TEI18_IPv6PD | General Support of IPv6 Prefix Delegation | SP-220797 | No CRs
TEI18_DCAMP_Ph2 | Dynamically Changing AM Policies in the 5GC Phase 2 | SP-230102 | No CRs
eNSAC | Enhancement of NSAC for maximum number of UEs with at least one PDU session/PDN connection | SP-230113 | No CRs
TEI18 mini WIDs

## Slide 20: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 21: SA WG2 progress -Summary
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1010029 | Study on Energy Efficiency and Energy Saving | FS_EnergySys | 06/06/2024 | 100% | SP-231391 | 100% | 
1050112 | (WA) Energy Efficiency and Energy Saving | EnergySys | 12/12/2024 | 70% | SP-241388 | 100% | 
1040033 | Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML) | AIML_CN | 12/12/2024 | 85% | SP-240991 | 98% | 
1020068 | Study on Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML) | FS_AIML_CN | 06/06/2024 | 100% | SP-231800 | 100% | 
1020071 | Study on Architecture support of Ambient power-enabled Internet of Things | FS_AmbientIoT | 12/12/2024 | 90% | SP-240969 | 100% | 
1010033 | Study on Integration of satellite components in the 5G architecture Phase 3 | FS_5GSAT_Ph3_ARCH | 06/06/2024 | 100% | SP-231199 | 100% | 
1040027 | Integration of satellite components in the 5G architecture Phase III | 5GSAT_Ph3-ARC | 12/12/2024 | 65% | SP-240986 | 100% | 
1010032 | Study on Extended Reality and Media service (XRM) Phase 2 | FS_XRM_Ph2 | 09/09/2024 | 100% | SP-231671 | 100% | 
1040032 | Extended Reality and Media service (XRM) Phase 2 | XRM_Ph2 | 12/12/2024 | 65% | SP-240990 | 100% | 
1040035 | UPF enhancement for Exposure And SBA Phase 2 | UPEAS_Ph2 | 12/12/2024 | 100% | SP-240995 | 100% | 
1020003 | Study on UPF enhancement for Exposure And SBA Phase 2 | FS_UPEAS_Ph2 | 06/06/2024 | 100% | SP-231795 | 100% | 
1040036 | Enhancement of support for Edge Computing in 5G Core network - Phase 3 | eEDGE_5GC_Ph3 | 12/12/2024 | 97% | SP-240996 | 100% | 
1020004 | Study on Enhancement of support for Edge Computing in 5G Core network - Phase 3 | FS_eEDGE_5GC_Ph3 | 09/09/2024 | 100% | SP-240962 | 100% | 
Updates in RED

## Slide 22: SA WG2 progress -Summary
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1040034 | Multi-Access (ATSSS_Ph4) | MASSS | 12/12/2024 | 100% | SP-240994 | 100% | 
1020070 | Study on Multi-Access (DualSteer and ATSSS_Ph4) | FS_MASSS | 09/09/2024 | 100% | SP-240467 | 100% | 
1040026 | System architecture for Next Generation Real time Communication services Phase 2 | NG_RTC_Ph2 | 12/12/2024 | 70% | SP-240985 | 98% | 
1010030 | Study on system architecture for next generation real time communication services phase 2 | FS_NG_RTC_Ph2 | 09/09/2024 | 100% | SP-231196 | 100% | 
1020069 | Study on (Stage 2 of) Phase 3 for UAS, UAV and UAM | FS_UAS_Ph3 | 09/09/2024 | 100% | SP-231801 | 100% | 
1040037 | (Stage 2 of) UAS, UAV and UAM Phase 3 | UAS_Ph3 | 12/12/2024 | 99% | SP-240997 | 100% | 
1020002 | Study on System aspects of 5G NR Femto | FS_5G_Femto | 09/09/2024 | 100% | SP-231797 | 100% | 
1040028 | System aspects of 5G NR Femto | 5G_Femto | 12/12/2024 | 100% | SP-240629 | 100% | 
1020066 | Study on Proximity-based Services in 5GS Phase 3 | FS_5G_ProSe_Ph3 | 09/09/2024 | 100% | SP-231798 | 100% | 
1040030 | Proximity-based Services in 5GS Phase 3 | 5G_ProSe_Ph3 | 12/12/2024 | 100% | SP-240988 | 100% | 
1020067 | Study on Vehicle Mounted Relays Phase 2 | FS_VMR_Ph2 | 09/09/2024 | 100% | SP-240493 | 100% | 
1040031 | Vehicle Mounted Relays Phase 2 | VMR_Ph2 | 12/12/2024 | 100% | SP-240989 | 100% | 
1020063 | Study on User Identities and Authentication Architecture | FS_UIA_ARC | 09/09/2024 | 100% | SP-231804 | 100% | 
1040085 | Identifying non-3GPP Devices Connecting behind a UE or 5G-RG | UIA_ARC | 12/12/2024 | 90% | SP-240971 | 100% | 
1040029 | (stage 2 of) MPS for IMS Messaging and SMS services | MPS4msg | 12/12/2024 | 100% | SP-240987 | 100% | 
1010031 | Study on MPS for IMS Messaging and SMS services | FS_MPS4msg | 06/06/2024 | 100% | SP-231197 | 100% | 
Updates in RED

## Slide 23: SA WG2 progress – (TEI19) (1/2)
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1030010 | On-demand broadcast of GNSS assistance data | TEI19_OBGAD | 12/12/2024 | 100% | SP-240487 | 100% | No CRs
1040078 | Stage 2 of Minimize the Number of Policy Associations | TEI19_MINPA | 03/03/2025 | 100% | SP-240118 | 100% | No CRs
1030014 | Spending Limits for UE Policies in Roaming scenario | TEI19_SLUPiR | 06/06/2024 | 100% | SP-240486 | 100% | 1 CR to TS 23.502
1040079 | Stage 2 of Enhancing Parameter Provisioning with static UE IP address and UP security policy | TEI19_IP_SP_EXP | 12/12/2024 | 100% | SP-240121 | 100% | 1 CR to TS 23.501, 1 CR to TS 23.502
1030017 | Multiple Location Procedure for Emergency LCS Routing | TEI19_MLR4RTR | 12/12/2024 | 100% | SP-240123 | 100% | 1 CR to TS 23.273
1030018 | Roaming traffic offloading via session breakout in HPLMN | TEI19_HSBO | 12/12/2024 | 100% | SP-240491 | 100% | 1 CR to TS 23.501
1030019 | Deferred 5GC-MT-LR Procedure for Periodic Location Events based NRPPa Periodic Measurement Reports | TEI19_DLPMR | 12/12/2024 | 100% | SP-240125 | 100% | 2 CRs to TS 23.273
1030011 | (Stage 2 of) Indirect Network Sharing | TEI19_NetShare | 06/06/2024 | 100% | SP-240488 | 100% | 3 CRs to TS 23.501
1030013 | Architecture support of roaming value-added services | TEI19_RVAS | 06/06/2024 | 100% | SP-240119 | 100% | No CRs
Updates in RED

## Slide 24: SA WG2 progress – (TEI19) (2/2)
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1030016 | ProSe support in NPN | TEI19_ProSe_NPN | 06/06/2024 | 100% | SP-240122 | 100% | No CRs
1030020 | QoS monitoring enhancement | TEI19_QME | 06/06/2024 | 100% | SP-240961 | 100% | 1 CR to TS 23.501, 1 CR to TS 23.503
1030021 | Subscription control for reference time distribution in EPS | TEI19_TIME_SUB_EPS | 12/12/2024 | 100% | SP-240127 | 100% | No CRs
1040080 | Stage 2 of Providing per-subscriber VLAN instructions from UDM and DN-AAA | TEI19_VLANSUB | 12/12/2024 | 100% | SP-240128 | 100% | 1 CR to TS 23.501
1030023 | NF discovery and selection by target PLMN | TEI19_NFsel_by_tPLMN | 06/06/2024 | 100% | SP-240490 | 100% | 1 CR to TS 23.502
1060030 | Network Controlled Network Slice Selection | TEI19_SliceSel | 12/12/2024 | 100% | SP-241502 | 100% | 2 CR to TS 23.501, 2 CR to TS 23.502, 1CR to TS 23.503. One EN needs to be resolved via Cat F CR
1060031 | PRU Usage Extension supported by Core Network | TEI19_PRUE | 12/12/2024 | 100% | SP-241504 | 100% | No CRs
1060028 | MSISDN verification operation support to Nnef_UEId Service | TEI19_MVOSNS | 12/12/2024 | 100% | SP-241498 | 100% | 1 CR to TS 23.502
1060029 | ATSSS Rule Provisioning via 3GPP access connected to EPC | TEI19_ARP3E | 12/12/2024 | 100% | SP-241500 | 100% | No CRs
Updates in RED

## Slide 25: FS_5GSAT_Ph3_ARCH/ 5GSAT_Ph3-ARC
Progress since SA#106
  KI#1 (regenerative payload satellite access): 2 CRs are approved, and this KI is completed
  KI#2 (S&F): 1 LS out to reply LS from SA3-Li, 1 LS out to reply LS from RAN2 and 12 CRs are approved, and then this KI is completed.
  KI#3 (UE-satellite-UE): 8 CRs are approved to support UE-satellite-UE communication with IMS-AGW onboard satellite, and 1 CR is approved for maintenance.
  RAN impacts and dependencies
  Yes, KI#1 depends on RAN3 conclusion, and KI#2 has RAN impact
Contentious issues
  None
Next Steps
  Maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1040027 | Integration of satellite components in the 5G architecture Phase 3 | 5GSAT_Ph3_ARCH | 14/03/2025 | 90 | SP-240986 | 100 | Completed
1010033 | Study on Integration of satellite components in the 5G architecture Phase 3 | FS_5GSAT_Ph3_ARCH | 21/06/2024 | 100 | SP-231199 | 100 | Completed

## Slide 26: FS_NG_RTC_Ph2/NG_RTC_Ph2
Progress since SA#106
  In SA2 #166AHE and #167 meetings 96 contributions were submitted and 58 contributions were handled with 23 CRs agreed
  Achievements:
    Issues in the exception list were all resolved
    CRs related to maintenace of KI#4 and KI#1 were handled
    A reply LS on AF authorization is sent to SA3
    A LS to SA4 is sent to trigger their work on DC multiplexing
Impacts and dependencies on other WGs
  None
Controversial issues
  None
Next steps
  Continue the maintenance and alignment with other WGs for all KIs (Only Cat F CR needed )
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1010030 | Study on system architecture for next generation real time communication services phase 2 | FS_NG_RTC_Ph2 | 12/12/2024 | 100% | SP-231196 | 100% | Complete
1040026 | System architecture for next generation real time communication services phase 2 | NG_RTC_Ph2 | 12/12/2024 | 70% | SP-240985 | 98% | Remaining issues in exception list have been resolved

## Slide 27: FS_XRM_Ph2/XRM_Ph2
  Progress since SA#106
  Normative and maintenance work at SA2#166AH-e and SA2#167
  SA2#166AH-e: 1 LS OUT, a related CR with its Rel-18 mirror and 15 more CRs are approved (KI#1: 2 CR, KI#2: 3 CRs, KI#3: 1 CR, KI#4: 1 CR, KI#5: 5 CRs, KI#6: 1 CR, KI#9: 2 CRs)
  SA2#167: 1 LS OUT with 3 related CRs and 16 more CRs are approved (KI#1: 4 CRs, KI#2: 2 CRs, KI#4: 3 CRs, KI#5: 2 CRs, KI#9: 5 CRs)
  All KIs completed
  Impacts and dependencies on other WGs
  None
  Controversial issues
    None
  Items not part of Rel. 19
  Application Layer Forward Error Correction (AL-FEC) awareness at NG-RAN
  Differentiated QoS handling for ciphered multiplexed traffic other than SRTP
Next steps
  Maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1010032 | Study on Extended Reality and Media service (XRM) Phase 2 | FS_XRM_Ph2 | 09/09/2024 | 100% | SP-231671 | 100% | 
1040032 | Extended Reality and Media service (XRM) Phase 2 | XRM_Ph2 | 12/12/2024 | 65% | SP-240990 | 100% | 

## Slide 28: FS_EnergySys/EnergySys
  Progress since SA#106
  Discussion on CRs for maintenance of TS documents has been started
  The revised WID to discontinue the unfinished issues of Rel-19, based on decision at SA#106, is submitted to SA#107
  140 Tdocs were submitted to SA2#166AH and #167 (120 CRs and 2 LSs are handled, 27 CRs and 1 LS are agreed)
  Impacts and dependencies on other WGs
  1 LS to SA5 regarding energy information collection from OAM to EIF (S2-2501217)
  1 LS to RAN2/RAN3 regarding energy saving indication from CN to RAN (S2-2413034)
  Contentious issues
  None
  Next steps:
  Maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1010029 | Study on Energy Efficiency and Energy Saving | FS_EnergySys | 18/06/2024 | 100% | SP-231192 | 100% | Study has been completed
1050112 | 5GS Enhancement for Energy Efficiency and Energy Saving | EnergySys | 12/12/2024 | 70% | SP-241388 | 100% | Normative work complete

## Slide 29: FS_MPS4msg/MPS4msg
Progress since SA#106:
  No contributions submitted.
  Normative work is 100% complete
Impacts and dependencies on other WGs:
  None
Controversial issues:
  None
Next steps:
  Maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1010031 | Study on MPS for IMS Messaging and SMS services | FS_MPS4msg | 06/06/2024 | 100% | SP-231197 | 100% | 
1040029 | MPS for IMS Messaging and SMS services | MPS4msg | 12/12/2024 | 100% | SP-240987 | 100% | 

## Slide 30: FS_VMR_Ph2/VMR_Ph2
Progress since SA#106:
  11 CRs to TS 23.501 and TS 23.273 were agreed.
  Updates to: Additional ULI support, AMF determination of UE served by a MWAB, Impact of MWAB mobility, UE mobility served by MWAB, QoS handling of Xn traffic, Regulatory service via MWAB, Location services when roaming, and Privacy check for MWAB
Impacts and dependencies on other WGs:
  OAM support is expected to be handled by SA5, and security to be handled by SA3
Next steps:
  Alignment based on work progressed in other working groups
  Maintenance work
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020067 | Study on Vehicle Mounted Relays Phase 2 | FS_VMR_Ph2 | 09/09/2024 | 100% | SP-240493 | 100% | 
1040031 | Vehicle Mounted Relays Phase 2 | VMR_Ph2 | 12/12/2024 | 100% | SP-240989 | 100% | 

## Slide 31: FS_5G_ProSe_Ph3/5G_ProSe_Ph3
  Progress since SA#106
  18 CRs to TS 23.304 and one CR to TS 23.502 were agreed.
  1 reply LS sent to RAN WG2 on relay discovery announcement.
  1 reply LS sent to SA WG3 on multi-hop U2N relay architecture aspects.
  1 LS OUT sent to RAN WGs 2 and 3 on Authorization information for Layer-2 multi-hop U2N relaying to NG-RAN
  Impacts and dependencies on other WGs
  Layer 2 UE-to-Network Relay has dependencies in related work item in RAN.
Outstanding issues
  None.
Next steps
  Continue maintenance work.
  Alignment with RAN for Layer 2 UE-to-Network Relay
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020066 | Study on Proximity-based Services in 5GS Phase 3 | FS_5G_ProSe_Ph3 | 18/06/2024 | 100% | SP-231798 | 100% | 
1040030 | Proximity-based Services in 5GS Phase 3 | 5G_ProSe_Ph3 | 18/12/2024 | 100% | SP-240988 | 100% | 

## Slide 32: FS_UIA_ARC/UIA_ARC
Progress since SA#106
  50 documents were submitted to SA2 #166-AH-e. 17 were approved, 3 were merged, 10 were noted, 1 was postponed, 19 were not handled.
  UIA_ARC was not on the SA2 #167 agenda.
  In sumary 17 CAT-F CRs were approved: 2 for TS 23.316 CR, 7 for TS 23.501 CRs, 5 for TS 23.502 CRs, and 3 for TS 23.503 CRs.
Impacts and dependencies on other WGs
  None identified
Contentious Issues
  None identified
Next Steps
  Maintenance work and alignments based on feedback from and progress in CT WGs
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020063 | Study on User Identities and Authentication Architecture | FS_UIA_ARC | 09/09/2024 | 100% | SP-231804 | 100% | 
1040085 | Identifying non-3GPP Devices Connecting behind a UE or 5G-RG | UIA_ARC | 30/12/2024 | 90% | SP-240971 | 100% | Previously 90% pending exception discussion. That exception sheet was not agreed.

## Slide 33: FS_eEDGE_5GC_ph3/ eEDGE_5GC_ph3
Progress since SA#106
  45 Tdocs received, 25 CRs were approved
  Impacts and dependencies on other WGs:
  None
Controversial issues:
  None
Next steps:
  Continue maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020004 | Study on Enhancement of support for Edge Computing in 5G Core network - Phase 3 | FS_eEDGE_5GC_Ph3 | 09/09/2024 | 100% | SP-240962 | 100% | 
1040036 | Enhancement of support for Edge Computing in 5G Core network - Phase 3 | eEDGE_5GC_Ph3 | 12/12/2024 | 97% | SP-240996 | 100% | 

## Slide 34: FS_UAS_Ph3/UAS_Ph3
Progress since SA#106
  10 CRs to TS 23.256 and 1 CR to TS 23.502 were agreed
  Impacts and dependencies on other WGs
  CT3: Using Nnef_RetrieveInfoUAVFlight_Get in the procedure for USS changeover during a UAV flight
  RAN3: Procedures for altitude reporting for aerial UEs
   CT3 and RAN3 related aspects are expected to be progressed during Q2 meetings.
  SA3: check USS list aspect progressed in SA3 and follow-up if necessary
Outstanding issues
  None
Next steps
  Maintenance work and alignments based on feedback from and progress in other WGs
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020069 | Study on (Stage 2 of) Phase 3 for UAS, UAV and UAM | FS_UAS_Ph3 | 09/09/2024 | 100% | SP-231801 | 100% | 
1040037 | (Stage 2 of) UAS, UAV and UAM Phase 3 | UAS_Ph3 | 12/12/2024 | 99% | SP-240997 | 100% | 

## Slide 35: FS_UPEAS_Ph2/UPEAS_Ph2
Progress since SA#106
  Continue maintenance work at SA2#166e and SA2#167
  9 CRs are approved at SA2#166e and 1 CR is approved at SA2#167
Impacts and dependencies on other WGs
  None
Controversial issues
  None
Next steps
  Maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020003 | Study on UPF enhancement for Exposure And SBA Phase 2 | FS_UPEAS_Ph2 | 06/06/2024 | 100% | SP-231795 | 100% | 
1040035 | UPF enhancement for Exposure And SBA Phase 2 | UPEAS_Ph2 | 12/12/2024 | 100% | SP-240995 | 100% | 

## Slide 36: FS_5G_Femto/5G_Femto
  Progress since SA#106
  A total of 5 CRs (4 CRs for TS 23.501 and 1 CR for TS 23.502) were agreed on the clarification on CAG information provisioning and roaming aspect.
  LS on NR Femto node shared by PLMN and PNI-NPN is approved and forwarded to RAN3 (S2-2502787)
  RAN impacts and dependencies
  Depending on the LS response, there may be dependencies on the RAN
Outstanding issues
  None
Next steps
  Maintenance work and alignment based on work progressed in other working groups
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020002 | Study on System aspects of 5G NR Femto | FS_5G_Femto | 09/09/2024 | 100% | SP-231797 | 100% | 
1040028 | System aspects of 5G NR Femto | 5G_Femto | 12/12/2024 | 100% | SP-241327 | 100% | 

## Slide 37: FS_MASSS/MASSS
  Progress since SA#106
  16 maintenance CRs and 1 discussion paper were submitted. 11 CRs were approved (TS 23.501/23.502/23.503)
  RAN impacts and dependencies
  None
Contentious issues:
  None
Next steps
  Maintenance
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020070 | Study on Multi-Access (DualSteer and ATSSS_Ph4) | FS_MASSS | 09/09/2024 | 100% | SP-240467 | 100% | 
1040034 | Multi-Access (ATSSS_Ph4) | MASSS | 12/12/2024 | 100% | SP-240994 | 100% | 

## Slide 38: AmbientIoT/FS_AmbientIoT
Progress since SA#106
  TR is 100% complete, and will be sent to SA for approval.
  Started normative work in the new TS 23.xyz. Several pCR are agreed and incorporated in the new TS.
  SA2 approved Rel-19 AmbientIoT WID
  Other WG impacts and dependencies
  Several issues need coordination with RAN & SA WG3 in the normative phase
Outstanding issues
  How the AIoT Device ID privacy protection and including ID authentication is done will be concluded by SA WG3. SA2 alignment with SA3 TR conclusions for AIoT Device security including AIoT Device ID privacy protection is FFS
Next steps
  Address the outstanding issue (as mentioned in the TR cover sheet)
  Continue the normative work, and target for TS completion by SA#108 meeting
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020071 | Study on Architecture support of Ambient power-enabled Internet of Things | FS_AmbientIoT | 12/12/2024 | 90% | SP-240969 | 100% | Now complete
N/A | Architecture support of Ambient power-enabled Internet of Things | N/A | June, 2025 | / | SP-241979 | 30% | 

## Slide 39: FS_AIML_CN/AIML_CN
General
  Of 254 input papers 121 were handled, and 43 CRs were agreed:
    15 CRs for KI#1 (AI/ML based positioning),
    20 CRs for KI#2 (VFL),
    4 CRs for KI#3 (NWDAF-assisted policy control enhancement),
    4 CRs for KI#4 (mitigating network abnormal behavior)
  Impacts and dependence with other WGs :
  RAN Impact on KI#1
    Any data to be collected from UE/RAN by LMF for the model training/model inference/model performance monitoring for LMF-side model is assumed to be defined by RAN WGs and coordination with RAN is needed.
    Feedback from RAN1/RAN2/RAN3 for the current progress of case 2b and case 3b to handle/specify the corresponding procedures in SA2 e.g. data collection from RAN and/or UE.
  Impact SA3: consent/privacy aspects need to be resolved, in coordination with SA3
Controversial issues
  None
Next Steps
  Maintenance. KI#1 to align with RAN and SA3 based on RAN/SA3 feedback
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020068 | Study on Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML) | FS_AIML_CN | 06/06/2024 | 100% | SP-231800 | 100% | 
1040033 | Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML) | AIML_CN | 12/12/2024 | 85% | SP-240991 | 98% | 

## Slide 40: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 41: FS_*
General
Impacts and dependence with other WGs :
Controversial issues
Next Steps
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
 |  | FS_* |  | % |  | % | 
Placeholder

## Slide 42: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 43: 2.7) IETF and External SDO Normative Reference Update
23.501: Change IETF draft-ietf-detnet-yang to RFC 9633 in the references
23.503: Change IETF draft-ietf-detnet-yang to RFC 9633 in the references

## Slide 44: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 45: 3) SA2 Work Planning: Rel-19
Summary of status of Rel-19 work and study items (excluding TEI19)
 | Study Item status | Work Item status | Comment
FS_5GSAT_ARCH_Ph3/5GSAT_Ph3-ARC | 100 | 100 | 
FS_NG_RTC_Ph2/NG_RTC_Ph2 | 100 | 98 | EN’s remaining – alignment/Cat-F CRs
FS_XRM Ph2/XRM Ph2 | 100 | 100 | 
FS_EnergySys/EnergySys | 100 | 100 | 
FS_MPS4msg/MPS4msg | 100 | 100 | 
FS_VMR_Ph2/VMR_Ph2 | 100 | 100 | 
FS_5G_ProSe_Ph3/5G_ProSe_Ph3 | 100 | 100 | 
FS_UIA_ARC/UIA_ARC | 100 | 100 | 
FS_eEDGE_5GC_ph3/eEDGE_5GC_ph3 | 100 | 100 | 
FS_UAS_Ph3/UAS_Ph3 | 100 | 100 | 
FS_UPEAS_Ph2/UPEAS_Ph2 | 100 | 100 | 
FS_5G_Femto/5G_Femto | 100 | 100 | 
FS_MASSS/MASSS | 100 | 100 | 
FS_AmbientIoT/AmbientIoT | 100 | 30 | 
FS_AIML_CN/AIML_CN | 100 | 98 | EN’s remaining – alignment/Cat-F CRs

## Slide 46: 3) SA2 Work Planning: Rel-20
The TU budget was discussed and endorsed in SA2#166 Orlando and further endorsed by SA Plenary in Madrid
Following the decision to have normative Ambient IoT work in Rel-19 SA have now allocated 4 TU’s in Q2 for this
This required a small adjustment of the TU plans and this was endorsed in SA2#167 Athens
SA2 briefly discussed the TU split between 5G Advanced and 6G topics in Rel-20 but couldn’t reach consensus on what the split should be and what the reasoning behind the split should be
SA2 Chair provides some insight into the planning implications of different splits in a separate contribution to this meeting

## Slide 47: 3) SA2 Work Planning: Rel-20 5GA
Guidance from SA#106 on target to submit SIDs
  SA2 should prioritize following “core” topics for Q1 2025 and should aim to submit SIDs at SA#107 for approval (as per normal consensus). Remaining topics may also be discussed if time permits
Progress on Set A and Set B items shown on the next slide
Guidance from SA#106 on two items not for Q1 discussion
  For topic SMS to emergency centre, no SA2 moderated discussion expected in Q1 2025
  For topic User Identities and Authentication, whether moderated discussion can take place in Q2 2025 will be determined in TSG#107
NWM-based discussion of SMS to Emergency Centre will be organised in Q2
SA should discuss whether User Identities and Authentication discussion can start
There should also be a discussion of when the Rel-20 AmbientIoT item should be discussed by SA2

## Slide 48: 3) SA2 Work Planning: Rel-20 5GA
Progress on 5GA items in SA2
Topic | Moderator | Set | Status
Integration of satellite components in the 5G architecture Ph4 | Hucheng Wang (CATT) | A | SID approved in SA2
AI/ML Enhancements | Xiaobo Wu (vivo) | A | SID approved in SA2
Ambient IoT | Runze Zhou (Huawei) | - | AmbientIoT Rel-19 work ongoing
Integrated Sensing and Communication | Jianing Liu (Xiaomi) | A | SID approved in SA2
Energy Efficiency Enhancements | Jungshin Park (Samsung) | A | SID not approved – sustained objection
XR and Media Services | Georgios Gkellas (Nokia) | B | NWM discussion completed
Indirect Network Sharing Phase 2 | TianQi Xing (China Unicom) | B | NWM discussion completed
User Identities and Authentication Architecture – Phase 2 | Mike Starsinic (interdigital) | - | Decision by SA#107 required
Enhancements for ePDG based access to 5GC | Stefano Faccin (Qualcomm) | A | SID not approved
Mission Critical Services, Multimedia Priority Services | Robert Streijl (Peraton) | B | NWM discussion completed
Industrial network enhancements | Shabnam Sultana (Ericsson) | A | SID not approved
SMS to Emergency Centre | Krisztian Kiss (Apple) | - | NWM discussion planned for Q2
NG_RTC continuation | Yi Jiang (China Mobile) | B | NWM discussion complete

## Slide 49: 3) SA2 Work Planning: Rel-20 6G
Expect to need NWM-based discussion of the content of the 6G Study Item Description during Q2
Any guidance SA Plenary is able to give based on the input to the 6G Workshop will be taken into account
There will also be time for face to face discussion of potential content in the April SA2 meeting
Discussion and approval of the SID is scheduled for the May SA2 meeting
Details of the process and timeline to be followed by SA2 will be circulated after the SA Plenary meeting

## Slide 50: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 51: 4) Documents for Information and Approval (1/4)
Revised SID/WID for Approval
TSG SA# | Type | Title | Acronym
SP-250069 | WID REVISED | Revised WID on Energy Efficiency and Energy Saving. | EnergySys

## Slide 52: 4) Documents for Information and Approval (2/4)
New SID/WID for Approval
TSG SA# | Type | Title | Acronym
SP-250065 | WID NEW | New WID on Architecture support of Ambient power-enabled Internet of Things. | 
SP-250066 | SID NEW | New SID on Study on Integration of satellite components in the 5G architecture Phase 4. | 
SP-250067 | SID NEW | New SID on Study on Architecture Enhancement to support Integrated Sensing and Communication. | 
SP-250068 | SID NEW | New SID on Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML)_Ph2. | 

## Slide 53: 4) Documents for Information and Approval (3/4)
TSs/TRs for Approval
TSG SA# | Title | Release | TR/TS | WI Acronym
SP-250070 | Cover sheet for presentation of TR 23.700-13 to TSG SA for Approval | Rel-19 | TR | FS_AmbientIoT

## Slide 54: 4) Documents for Information and Approval (4/4)
TSs/TRs for Information
TSG SA# | Title | Release | TR/TS | WI Code

## Slide 55: Contents
1) General aspects (events since SA#106, statistics, next meetings)
2) SA Work Report
  2.1) Rel-16 and before Maintenance
  2.2) Rel-17 Work and Maintenance
  2.3) Rel-18 Work and Maintenance
  2.4) Rel-19 Work and Maintenance
  2.5) Rel-20 Work and Maintenance
  2.6) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 56: 5) Collected Items requiring action from SA
Decisions for TRs for information/approval
Approval of new/revised WIDs
Other
  SA should discuss whether User Identities and Authentication discussion can start
  When can the Rel-20 AmbientIoT item be discussed by SA2

## Slide 57: Thank You !
Andrew Bennett
Chair of 3GPP SA2
a.bennett@Samsung.com
www.3gpp.org