## Slide 1: Discussion on Loop Protection
Huawei, HiSilicon

## Slide 2: Background
S2-2505919 New WID on Industrial Networks Loop Prevention
  This is a new WID proposed and discussed in SA2, with the following objective:
    Study how to provide loop prevention functionality (i.e. MSTP/RSTP) such that the 5GS logical bridge’s behavior meets the Bridge component requirements for MSTP/RSTP specified in IEC/IEEE 60802.
  This WID is noted due to no agreement at SA2#169 meeting.
  In this contribution, Huawei provides the following observations and proposes a way forward.

## Slide 3: Loop Protection is a General Issue for Ethernet type Communication, and STP is not appropriate for TSN
Observation 1: Loop Protection is a general Issue for Ethernet type Communication
  Loop Problem is an intrinsic universal challenge to Ethernet Network due to its broadcast nature and the need for multipath redundancy.
  Ethernet type Communication in 3GPP inherently faces Loop Problems since Rel-15, the first release that defines the Ethernet type Communication.
  Rel-15 speciation states that Loop Problem is avoided by network deployment and implementation. And this Loop Problem lasts for Rel-16, Rel-17, Rel-18, Rel-19
Observation 2: STP is one of the solutions for Loop Protection, but not appropriate for TSN
  TSN (IEEE 802.1Q series), emerging in 2012, extends standard Ethernet to provide deterministic low latency and reliability for industrial automation, automotive networks, and other time-critical applications. Rel-16 TSN feature in nature focuses on offering time sensitive periodic deterministic communication, it is defined on top of the Ethernet type Communication with time-sensitive capabilities.
  STP predates TSN. STP (IEEE 802.1D), introduced in 1985, adopted in 1990, was the classic Ethernet protocol for loop prevention. Enhanced versions (e.g., RSTP, MSTP) improves performance, but the key purpose remains for loop elimination in generic Ethernet environments.
  TSN doesn’t mandate support of STP, rather STP may be entirely disabled in TSN deployment, e.g., in the scenarios where TSN is deployed in a dedicated network (e.g., industrial automation). In some TSN deployments, to avoid STP’s limitations, STP is replaced by deterministic routing protocols. In reality, modern TSN networks prefer other deterministic path protocols (e.g., IEEE 802.1Qca, SPB based on IS-IS) over traditional STP, because
    STP’s convergence time (seconds) cannot meet TSN’s real-time requirements (milliseconds/microseconds).
    STP blocks redundant paths, whereas TSN may require multipath transmission for reliability (e.g., FRER, IEEE 802.1CB).

## Slide 4: STP's flaws limit its promotion, and the market widely chooses other ways for Loop Protection
Observation 3: STP is not widely supported in the industry, rather the market chooses other ways for Loop Protection
  Inherent Deficiencies of STP protocol,
    Slow Convergence Speed, 1) Traditional STP (802.1D) requires 30-50 seconds for topology convergence 2) Even improved RSTP (802.1w) still needs 2-5 seconds. Cannot meet millisecond-level fault recovery requirements of modern networks
    Bandwidth/CPU Resource Waste, Passively blocks redundant links, Periodic BPDU transmission and handling for every PDU session
    High Management Complexity, Global configuration coordination (Trusted UE/End Device needed since their misbehavior would bring destroyable impact on the system), Difficult fault troubleshooting
  Implementation Methods in Actual Switches
    MAC Flapping Detection, Monitors rapid MAC address migration between ports, Automatically shuts down abnormal ports when triggered
    Loop Detection Mechanism, Actively sends detection packets, Detects packet loopback, Supports multi-level threshold alarms
    See the links at:
      https://www.cisco.com/c/en/us/td/docs/wireless/asr_901/Configuration/Guide/b_asr901-scg/b_asr901-scg_chapter_01010.html
      https://www.cisco.com/c/en/us/td/docs/switches/lan/catalyst9300/software/release/17-3/configuration_guide/lyr2/b_173_lyr2_9300_cg/configuring_loop_detection_guard.html
      https://www.h3c.com/en/d_201408/838990_294551_0.htm
      https://support.huawei.com/enterprise/en/doc/EDOC1100301696/5cea8faa
  Alternative standardized solutions:
    MLAG (Multi-Chassis Link Aggregation Group): allows two separate physical switches to appear as a single logical switch to downstream devices by combining their links into a single LAG (Link Aggregation Group). This is powerful alternative to STP that provides active-active redundancy, full bandwidth utilization, and simplified network design. It is widely used in data centers, enterprise networks, and high-availability environments where STP’s limitations (slow convergence, blocked links) are unacceptable.

## Slide 5: Loop Protection support in 3GPP is not an easy work
Observation 4: Loop Protection support in 3GPP is not an easy work, and needs more time for investigation, study and evaluation, to make it adaptive to 3GPP Ethernet type communication
  Technical issues to be considered for 3GPP to support loop protection
    Identify Scenarios with Loop Problem,
      PDU session establishment/release, N19 tunnel establishment /release, external Network integration etc.
    Identify functionality enhancement
      Management of the 5GS bridge status (root, leaf etc.)
      Management of the 5GS bridge port status (passive, blocked etc.)
      Management of the link status (weight of the PDU session/N19/N6, release or maintain if loop detected etc.)
      Management of the capability of UEs/end devices (STP capable or not, trusted or not)
      Management of the PBDUs (construction, timer configuration, parse, transmission rule and QoS etc.)
      Management of the e.g., spanning tree structure
    Evaluate Performance and Overhead
  Potential Impacts
    UE/DS-TT, UPF/NW-TT, TSN-AF, TSCTSF, SMF, PCF etc.

## Slide 6: Way forward
Way forward Proposal:
  Either maintain the decision since Rel-15, i.e. leave the loop prevention for network deployment and implementation, or keep this as a SID, as proposed since the beginning of Rel-20 5GA discussion, i.e. remove the STP as only solution from the objective, and revert the objective to the following
    Study whether and how to provide optimization for loop prevention functionality for Ethernet type communication
  Increase the TU for both SID+WID (2.5+2.5 at least)
    Allow more time for investigation, study and evaluation.