## Slide 1
IETF Status Report to TSG CT/SA#109
Peter Schmitt (3GPP Liaison Manager to IETF)
Charles Eckel (IETF Liaison Manager to 3GPP)

## Slide 2: Agenda
3GPP-IETF Coordination
Ongoing Liaison Statements exchanged between IETF and 3GPP
Ongoing IANA action
Status of the 3GPP-IETF dependencies
AoB

## Slide 3: 3GPP-IETF Coordination

## Slide 4: IETF-3GPP Coordination meeting
@IETF#123 (Madrid, Spain)
  2025, July 21
  Remote access was provided
@IETF#124 (Montreal, Canada)
  Planned for 2025, November 03
  Remote access will be provided
@IETF#123 there were 7 side meetings on AI-specific topics, including AI agent protocols, networking for AI, and AI agent applications in 6G network.
  An IETF side meeting is an unofficial gathering held during an IETF meeting where participants gather to discuss topics relevant to IETF but outside the official agenda.

## Slide 5: IETF - 3GPP IAB group
Created in April 2023, similar to the IETF-IEEE IAB group
Group description
  Support coordination between IETF and 3GPP as documented in RFC 3113.
  Led jointly by the 3GPP and IETF liaison managers.
  No fixed membership but participation from relevant IETF Area Directors, IETF WG Chairs, 3GPP WG Chairs, and document authors/editors is encouraged.
  See: https://datatracker.ietf.org/group/ietf3gpp/about/
Action Points:
  Tutorial and technical deep dive (TDD) on 3GPP held at IETF 121
  Update the dependency list tool or create a new one (with IETF support)
  Ongoing update RFC 3113: "3GPP-IETF Standardization Collaboration" (2001) draft version at https://datatracker.ietf.org/doc/draft-kes-rfc3113bis/

## Slide 6: IETF-3GPP Liaison Statements

## Slide 7: TEAS-> SA2, SA3, SA5, RAN3
LS on “IETF Network Slice Application in 3GPP 5G End-to-End Network Slice”(2025/09/12)
  For Action
  the IETF TEAS WG would like to inform 3GPP about the progress of "IETF Network Slice Application in 3GPP 5G End-to-End Network Slice" , an informational document that is almost ready for Working Group Last Call. This document describes the application of the IETF network slice framework in providing 5G end-to-end network slices, including network slice mapping in the management, control, and data planes
  The TEAS WG would like to request 3GPP to review the document and verify if the description of the 3GPP 5G End-to-End Network Slice is accurate, and if not, to kindly provide suggested clarifications.
LS to be scheduled at next SA2, SA3, SA5, RAN3 Meeting

## Slide 8: GREEN> RAN1, RAN4, SA2, SA3, SA4, SA5, CT1, CT4
LS on the creation of the Getting Ready for Energy-Efficient Networking Working Group in the IETF (2025/04/28)
  For Information
  We are glad to inform you that a new Working Group (WG) Getting Ready for Energy-Efficient Networking (GREEN), is created by the IETF. The WG held its first meeting in November 2024, in Dublin, during IETF 121. The GREEN WG is chartered to explore use cases, derive requirements, and provide solutions for identifying and characterizing energy efficiency metrics, methods related to energy consumption of network devices, and optimizing energy efficiency across the network.
LS is on the agenda for the RAN1, RAN4, SA2, SA3, SA4, SA5, CT1, CT4 in May
  Noted in RAN4 in August
  Noted in SA3. Interested in metrics and energy usage of various crypto algorithms.
  Noted in RAN1, SA2, SA4, SA5, CT1, CT4

## Slide 9: 6MAN-> RAN2, SA2, CT1, CT3, CT4
LS on draft-ietf-6man-deprecate-router-alert, “Deprecation of the IPv6 Router Alert Option for New Protocols” (2025/04/28)
  For Information
  The IETF is progressing a document that will deprecate the use of IPv6 Router Alert. Protocols that use the Router Alert Option may continue to do so, even in future versions. However, new protocols that are standardized in the future must not use the Router Alert Option.
LS is on the agenda for the RAN2, SA2, CT1, CT3, CT4 in May
  Noted in SA2, CT1, CT3, CT4
  Shown as ”Available” in RAN2

## Slide 10: SA5 -> NETMOD
LS on need for modeling isInvariant and SystemCreated in YANG (2023/03/09)
3GPP Requirements
  Solution to represent isInvariant and SystemCreated properties in YANG statements
  View draft-ma-netmod-immutable-flag as a potential solution
Discussed in NETMOD at IETF 117 – IETF 122
  WG adoption poll for draft-ma-netmod-immutable-flag-08 completed with mixed opinions
  Hence the "immutable-flag" draft [3] defines a metadata attribute called "immutable" that can be used by a system to declare which configuration nodes it deems immutable
  draft-ietf-netmod-immutable-flag, -04 posted 2025-05, addressing WGLC comments
  The system datastore defined in [2] provides a similar, but slightly different solution to the problem described by SystemCreated Classes in SA5 LS.
  System-defined Configuration, -12 posted 2025-02
Reply LS on need for modeling isInvariant and SystemCreated in YANG (2025/06/06)
  To be on agenda for SA5 meeting in October

## Slide 11: SA3 and RAN3 -> TSVWG
Reply LS on DTLS for SCTP (2023/08/21) from SA3
Reply LS on DTLS for SCTP next steps and request for input (2023/08/30) from RAN 3
  Both in response to DTLS for SCTP next steps and request for input (2023/08/04)
  SA3 and RAN3 confirmed TSVWG’s interpretation of requirements
Previously, TSVWG design team reached agreement on design goals and security requirements but could not reach consensus on a solution
At IETF 123
  Design team, slides-123-tsvwg-design-team-report-on-dtls-for-sctp-00
  Two drafts were adopted by the WG to provide a solution:
    https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/ adopted as https://datatracker.ietf.org/doc/draft-ietf-tsvwg-sctp-dtls-chunk/
    https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-dtls-chunk-key-management/ adopted as https://datatracker.ietf.org/doc/draft-ietf-tsvwg-dtls-chunk-key-management/
  An LS is expected to be sent to communicate this result

## Slide 12: Tracking requests to IANA

## Slide 13: IANA assignment request handling
Overview:
  A lot of IANA assignment requests have been done
  Any IANA assignment request must be indicated to the IETF liaison and Specification Manager
  Template for IANA assignment request as an Appendix included in the 3GPP specifications requiring the assignment
  Diameter application identifier request needs to be added/covered.
  The requests are tracked by MCC on the 3GPP web page under Delegates Corner: IANA registration requests tracking (3gpp.org)

## Slide 14: IETF Dependencies

## Slide 15: New Published RFCs

## Slide 16: Published RFCs
Deterministic Networking (DetNet) YANG Model RFC 9633
  Published 11/24
  Next step:
    CRs to 23.501 and 23.503
Instant Message Disposition Notification (IMDN) RFC 5438
  Published 02/09
  Next step:
    CR to 23.204 draft-ietf-simple-imdn is referenced in the TS, clause 2 is OK

## Slide 17: Published RFCs
PASSporT Extension for Rich Call RFC 9795
  Published 07/25 was draft-ietf-stir-passport-rcd-26
  Next step:
    SA2 CR to 23.228, SA3 CRs to 33.127, 33.128 and 33.203 , CT1 CR to 24.229
SIP Call-Info Parameters for Rich Call Data RFC 9796
  Published 07/25 was draft-ietf-sipcore-callinfo-rcd
  Next steps: SA2 CR to 23.228, CT1 CR to 24.229, CT4 CR to 29.571

## Slide 18: IETF reference updates
None

## Slide 19: Drafts in RFC Editor queue

## Slide 20: Drafts in RFC Editor queue
draft-ietf-opsawg-teas-attachment-circuit
  Title: YANG Data Models for 'Attachment Circuits'-as-a-Service (ACaaS)
  Status: draft-boro-opsawg-teas-attachment-circuit adopted by WG as draft-ietf-opsawg-teas-attachment-circuit, draft-ietf-opsawg-teas-attachment-circuit-20 posted 01/25, awaiting final approval from authors.
  Next steps: RFC publication, SA5 CR to 28.541
draft-ietf-tsvwg-udp-options
  Title:Transport Options for UDP
  Status: draft-ietf-tsvwg-udp-options-45 posted 03/25.
  Next steps: RFC publication, SA2 CRs to 23.501, 23.502, CT3 CR to 29.561, CT4 CR to 29.244

## Slide 21: Drafts in RFC Editor queue
draft-sipcore-rfc7976bis
  Title: Update to P-Visited-Network-ID in SIP Requests and Responses
  Was draft-jesske-update-p-visited-network
  Agreement to handle within SIPCORE at IETF 116 coordination meeting, Additional WGLC held
  draft-sipcore-rfc7976bis-03 posted 07/2024 addressing comments
  Renamed to draft-ietf-sipcore-rfc7976bis-00, posted 08/2024
  Revised to draft-ietf-sipcore-rfc7976bis-04, posted 08/2025
  Next steps: RFC publication, CT1 CR to 24.229

## Slide 22: Drafts under IESG review

## Slide 23: Drafts under IESG review
None

## Slide 24: Active WG documents

## Slide 25: Active WG document
draft-ietf-masque-quic-proxy
  Title: QUIC-Aware Proxying Using HTTP
  Status: WG Document, draft-ietf-masque-quic-proxy-06 posted 07/2025 Next step: IESG review, IESG review, RFC publication, SA2 CR to 23.501, 23.502, CT3 CR to 29.561, CT4 CR to 29.244
draft-ietf-moq-transport
  Title: Media over QUIC Transport
  Status: WG document, draft-ietf-moq-transport-14 posted 09/2025,
  Next step: IESG review, IESG review, RFC publication, SA2 CR to 23.501, 23.503, CT3 CR to 29.561, CT4 CR to 29.244, 29.571

## Slide 26: Active WG document
draft-ietf-quic-multipath
  Title: Multipath Extension for QUIC
  Status: draft-ietf-quic-multipath-16 posted 08/2025 addressing comments from WG last call Next step: IESG review, IESG review, RFC publication, SA2 CR to 23.501, CT1 CR to 24.193, SA3 CR to 33.501, SA4 CR to 26.501
draft-ietf-mimi-content
  Title: More Instant Messaging Interoperability (MIMI) message content
  Status: WG document, draft-ietf-mimi-content-07 posted 07/2025,
  Next step: IESG review, IESG review, RFC publication, SA4 CR to 26.143

## Slide 27: Active WG documents
draft-ietf-masque-connect-ethernet
  Title: Proxying Ethernet in HTTP
  Like IP proxying in HTTP, but for Layer 2 instead of Layer 3
  Status: WG last call, draft-ietf-masque-connect-ethernet-07 posted 07/2025
  Next steps: IESG review, RFC publication, SA2 CR to 23.501, CT1 CR to 24.193, CT4 CR to 23.003
draft-ietf-opsawg-pcap
  Title: PCAP Capture File Format
  Status: WG last call, draft-ietf-opsawg-pcap-06 posted 09/2025
  Next steps: IESG review, RFC publication, SA5 CR to 28.560

## Slide 28: Expired drafts

## Slide 29: Expired drafts
none new, see also Backup

## Slide 30: Obsoleted RFCs

## Slide 31: Obsoleted RFCs
RFC 6712: Internet X.509 Public Key Infrastructure - HTTP Transfer for the Certificate Management Protocol (CMP) obsoleted by RFC 9811 referenced by TS 33.310
RFC 4210: Internet X.509 Public Key Infrastructure - Certificate Management Protocol (CMP) obsoleted by RFC 9810 referenced by TS 33.310, 28.314
RFC 3810 “Multicast Listener Discovery Version 2 (MLDv2) for IPv6” obsoleted by RFC 9777 referenced by 23.401 24.008
RFC 3376 “Internet Group Management Protocol, Version 3” obsoleted by RFC 9776 referenced by 23.401, 24.008, 29.244
RFC 2460: "Internet Protocol, Version 6 (IPv6) Specification“ obsoleted by RFC 8200 updated by RFC 9763 referenced by TS 29.274, 33.128, 29.244, 29.281
RFC 6750 “The OAuth 2.0 Authorization Framework” obsoleted by RFC 9700 referenced by 29.500, 33.380
RFC 4122: “A Universally Unique IDentifier (UUID) URN Namespace ” Obsoleted by: RFC 9562 referenced by 33.310,
RFC 7230: "Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing“ Obsoleted by: 9110, 9112 referenced by 29.244
RFC 3315 and RFC 3736 both are obsoleted by RFC 8415 “Dynamic Host Configuration Protocol for IPv6 (DHCPv6) ” used by 24.229, 34.229
RFC 4282: "The Network Access Identifier“ Obsoleted by: RFC 7542 referenced by 29.061, 29.273, 29.244, 33.128, 23.228

## Slide 32: Individual submissions

## Slide 33: Individual submissions
none

## Slide 34: Any Other Business

## Slide 35
Reminder
  To allow tracing of all IETF drafts referenced in 3GPP specifications
  IETF dependencies newly introduced in a 3GPP specification should be reported to the workplan manager by the 3GPP WG chairs.
  IETF Coordinator will trace the progress of the IETF draft
  The workplan manager will add a line to the workplan for each IETF draft.
  The workplan manager will mark the task as completed once the IETF draft becomes an RFC and the RFC is referenced in the 3GPP TS

## Slide 36: Thank You!
Charles Eckel
IETF Liaison Manager to 3GPP
eckelcu@cisco.com
Peter Schmitt
TSG CT Chair
CCSA
peter.schmitt@huawei.com

## Slide 37: Backup Referenced expired drafts which are out of track

## Slide 38: Referenced Expired drafts (1/3)
draft-newton-json-content-rules-09
  Title: A Language for Rules Describing JSON Content
  Status: Last version published in 09/2017
  Expired internet draft, CT3 referenced in TS 29.155, 29.250, 29.251
draft-kelly-json-hal-11 (ietf.org)
  Title: JSON Hypertext Application Language
  Status: Last version published in 11/2023
  Expired internet draft, CT4 referenced in TS 29.501

## Slide 39: Referenced Expired drafts (2/3)
draft-bhutton-json-schema-01
  Title: JSON Schema: A Media Type for Describing JSON Documents
  Status: Last version published in 06/2022
  Expired internet draft, SA4 and SA5 referenced older versions in TS 26.346, TS 26.348, TS 32.158 and TS 32.160
Note: The JSON Schema TSC ( https://json-schema.org/slack ),it is open if a new draft will be provided to IETF. The latest versions of JSON Schema can be found here: https://json-schema.org/specification Copyrights do not allow 3GPP to reference. 3GPP need to reference the expired draft version on IETF server.

## Slide 40: Referenced Expired drafts (3/3)
draft-bhutton-json-schema-validation
  Title: JSON Schema Validation: A Vocabulary for Structural Validation of JSON
  Status: Last version published 06/2022
  Expired internet draft, SA4 referenced in TS 26.510 and TS 26.512 , SA5 referenced older versions in TS 32.158 and TS 32.160
draft-handrews-json-schema-hyperschema
  Title: JSON Hyper-Schema: A Vocabulary for Hypermedia Annotation of JSON
  Status: Last version published in 09/2019
  Expired internet draft, SA5 referenced older versions in TS 32.158 and TS 32.160