## Slide 1
Gilles Teniou (SA4 Chair, Tencent)
SA WG4 Status Report to
TSG SA#110
SP-251428
AI# 4.4
3GPP TSG SA Meeting #110
09 – 12 Dec 2025, Baltimore, USA

## Slide 2: Contents
1) General aspects (WG officials, WG meetings, statistics, progress highlights)
2) SA4 Work Report
  2.1) CRs to Rel-18 and earlier
  2.2) CRs to Rel-19 features under exception
  2.3) CRs to Completed Rel-19 features
  2.4) Rel-19 Work Items
  2.5) Rel-20 5G-A Work Items
  2.6) Rel-20 Study Items
  2.6) New Work & Study Items
3) SA4 Work Planning
4) External SDOs interaction (including IETF dependencies)
5) Collected Items requiring action from SA
6) Documents for Information and Approval

## Slide 3: 1) General Aspects – SA4 Officials
SA4 officials:
  Chair: Gilles Teniou (Tencent, CCSA)
  Vice Chairs:
    Mary-Luc Champel (Xiaomi, CCSA)
    Tomas Toftgård (Ericsson LM, ETSI) (New)
  Secretary: Andrijana Brekalo (MCC Support)
Sub Working Groups and their leaders
SA4 SWG reports:
  SA4 Audio SWG reports: SP-251541
  SA4 MBS SWG reports: SP-251541
  SA4 Video SWG reports: SP-251541
  SA4 RTC SWG reports: SP-251541
Audio SWG | Multicast-Broadcast-Streaming (MBS) SWG | Real Time Communications (RTC) SWG | Video SWG
Chair: Tomas Toftgård (Ericsson LM, ETSI) Vice-Chair: Stéphane Ragot (Orange, ETSI) | Frédéric Gabin (Dolby France SAS, ETSI) | Saba Ahsan (Nokia corporation, ETSI) | Gilles Teniou (Tencent, CCSA)

## Slide 4: 1) General Aspects – SA4 Meetings (1/2)
SA4 meetings held since SA#109
AH conference calls (1 to 2 hours each)
  Audio SWG: 15 Sep., 16 Oct., 23 Oct., 27 Oct.(x2)
  MBS SWG: 23 Oct.
  Video SWG: none.
  RTC SWG: 24 Sep., 22 Oct.
SWG AH Face-to-face meetings
  Audio SWG: 23-25 Sept. Erlangen (GE), host Fraunhofer IIS
Meetings in 2025 | Dates | Venue and Host
SA4#134 | F2F: 17-21 Nov. 2025 | Host: ATIS, Venue: Dallas, Texas, USA

## Slide 5: 1) General Aspects – SA4 Meetings (2/2)
SA4 plenary meetings (2026): 3 F2F and 2 e-meetings
October date not used
Meetings in 2026 | Dates | Venue and Host
SA4#135 | F2F: 9-13 Feb. 2026 | Host: TSDSI, Venue: Goa (IN)
SA4#135e-bis | E-meeting: 13-17 Apr. 2026 | Host: MCC, Electronic meeting
SA4#136 | F2F: 11-15 May 2026 | Host: Interdigital, Venue: Montreal (CA)
SA4#137e | E-meeting: 24-28 Aug. 2026 | Host: MCC, Electronic meeting
SA4#138 | F2F: 16-20 Nov. 2026 | Host: ATIS, Venue: Calgary (CA)
SA4 plenary meetings (2027): 4 F2F and 1 e-meeting
October date not used
Meetings in 2027 | Dates | Venue and Host
SA4#139 | F2F: 22-26 Feb. 2027 | Host: TBD, Venue: Korea
SA4#139e-bis | E-meeting: 19-23 Apr. 2027 | Host: MCC, Electronic meeting
SA4#140 | F2F: 24-28 May 2027 | Host: CCSA, Venue: China
SA4#141 | F2F: 30 Aug. - 3 Sep. 2027 | Host: ETSI, Venue: EU
SA4#142 | F2F: 15-19 Nov. 2027 | Host: ATIS, Venue: North America

## Slide 6: 1) General Aspects – SA4 Statistics
Statistics at SA4#134 (17-21 November 2025, Dallas, US)
  217 delegates ‘attended’ (checked-in) at SA4#134 45 registered for the on-line broadcast
  11 Tdocs not treated due to lack of time
  36% of agreed/approved/endorsed tdocs overall
Note 1: the number of F2F participants at SA4#131 (85) is representative of a regular standalone SA4 F2F meeting.
Note 2: the number of Tdocs (542) per meeting at SA4#134 (NEW) was at a record high
466 Subscribers registered on the SA WG4 e-mail reflector on 17 Nov. 2025

## Slide 7: 1) General Aspects – SA4 Progress highlights (1)
Release-19
  CRs to Rel-19 completed features on AMD-ARCH-MED, MeME-MED, IVAS_Codec_Ph2, 5G_RTP_Ph2, AMD_PRO-MED, AvCall-MED, FS_5G_RTP_Ph2, ATIAS_Ph2 and VOPS
  CRs to TEI19 (GA4RTAR and 5G_MEDIA_MTSI-ext)
  2 Work Items completed:
    Video Operating Points - Harmonization and Stereo MV-HEVC (VOPS)
    Stage 3 for Advanced Media Delivery (AMD_PRO-MED)
  2 Work Items under an exception are completed:
    EVS Codec Extension for Immersive Voice and Audio Services, Phase 2 (IVAS_Codec_Ph2)
      TS 26.251 sent for approval.
    Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 2 (ATIAS_Ph2)
  Completed 2 listening labs’ test reports and the global analysis lab report of IVAS fixed-point encoder delivery, sent for approval for final payment of the contracts with ETSI.
Release-12
  Correction on the EVS specification of a wrong clause referenced, does not introduce backwards compatibility issue on implementations (just a specification issue)
Release-17
  Correction on missing parameters for MBS service announcement (5MBUSA)
Release-18
  Corrections on IVAS_Codec

## Slide 8: 1) General Aspects – SA4 Progress highlights (2)
Release 20
  1 work item Diverse audio Capturing System for UEs (DaCAS) progressed as planned
  1 work item AI/ML for IMS services (AIML_IMS-MED) progressed slower than expected
  5 studies Media Energy Consumption Exposure and Evaluation Framework phase 2 (FS_Energy_Ph2-MED), Usage of Dynamically Changing Traffic Characteristics and Enhanced QoS support in Media Applications and Services (FS_DCTC_eQOS_MED), Advanced Video Formats and Operation Points (FS_AVFOPS_MED), 3D Gaussian splats (FS_3DGS_MED), Advanced Media Delivery Phase 2 (FS_AMD_Ph2) progressed as planned
  1 study on Audio Codec APIs completion was delayed by 2 plenary meeting cycles.
2nd package of Rel-20 topics for approval
  1 New work item (5G-A)
    Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 3 (ATIAS_Ph3-MED)
  5 New study items (5G-A)
    Study on IMS DC Enhancements (FS_DCE_MED)
    Study on QUIC-based Media Delivery for Real-time Communication (FS_Q4RTC_MED)
    Study on evaluation of QUIC-based protocols for on-demand and live video services (FS_Qstream_MED)
    Study on Avatar communication Phase 2 (FS_Avatar_Ph2_MED)
    Study on advanced image formats (FS_AIF_MED)
  1 New study item (6G)
    Study on Media Aspects for 6G System (FS_6G_MED)
Any other business
  SA4 discussed updates to its Terms of Reference and request guidance from SA on the scope of AI/ML

## Slide 9: 2.1) CRs to Rel-18 and earlier
Tdoc | Title | Source | Type | For | Agenda Item | Agenda Item description | Release
SP-251429 | CR Pack on EVS_Codec-SA4 | SA WG4 | CR pack | Approval | 12 | Rel-12 CRs | Rel-12
SP-251430 | CR Pack on 5MBUSA | SA WG4 | CR pack | Approval | 17 | Rel-17 CRs | Rel-17
SP-251431 | CR Pack on IVAS_Codec | SA WG4 | CR pack | Approval | 18.4 | SA WG4 Rel-18 CRs | Rel-18

## Slide 10: 2.2) CRs to Rel-19 features under exception
Tdoc | Title | Source | Type | For | Agenda Item | Agenda Item description | Release
SP-251435 | CR Pack on IVAS_Codec_Ph2 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251442 | CR Pack on ATIAS_Ph2 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19

## Slide 11: 2.3) CRs to Completed Rel-19 features
Tdoc | Title | Source | Type | For | Agenda Item | Agenda Item description | Release
SP-251432 | CR Pack on GA4RTAR, TEI19 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251433 | CR Pack on AMD-ARCH-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251434 | CR Pack on MeME-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251436 | CR Pack on 5G_RTP_Ph2, AMD_PRO-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251437 | CR Pack on AvCall-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251438 | CR Pack on FS_5G_RTP_Ph2 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251439 | CR Pack on 5G_MEDIA_MTSI_ext, TEI19 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251440 | CR Pack on 5G_RTP_Ph2 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251441 | CR Pack on VOPS | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251443 | CR Pack on AMD_PRO-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19

## Slide 12: 2.4) Rel-19 Work Items: Overview
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1030002 | Video Operating Points - Harmonization and Stereo MV-HEVC | VOPS | 12/12/2025 | 95% | SP-250818 | 100% | Stage 3 complete in SA#109 Work on conformance complete
1040021 | EVS Codec Extension for Immersive Voice and Audio Services, Phase 2 | IVAS_Codec_Ph2 | 9/9/2025-> 12/12/2025 | 80% | SP-250262 | 100% | Exception requested in SA#109 Complete
1050113 | Terminal Audio quality performance and Test methods for Immersive Audio Services | ATIAS_Ph2 | 9/9/2025-> 12/12/2025 | 75% | SP-241314 | 100% | Exception requested in SA#109 Complete
1070057 | Stage 3 for Advanced Media Delivery | AMD_PRO-MED | 9/9/2025 | 85% | SP-250265 | 100% | Stage 3 complete in SA#109 Work on OpenAPI complete

## Slide 13: 2.4) Rel-19 Work Items: Video Operating Points - Harmonization and Stereo MV-HEVC (VOPS) – Complete!
Purpose
  Harmonize and include as needed all the SA4 video operating points into a new specification that will be home to all such video operating points and upgrade HEVC-based levels based on industry practices.
  Define the MV-HEVC capability in this new specification.
  Then add and harmonize stereoscopic MV-HEVC operating points and capabilities for TS 26.511, TS 26.119 and TS 26.143
Progress in the last quarter
  Several essential corrections were agreed to TS 26.265, resulting in overall better structuring and removal of issues that were misaligned with deployments.
  The required conformance assets in scope of VOPS WI were gathered. It was agreed to add these to Annex B of TS 26.265. This Annex also documents the key related 3GPP forge repositories.
Next steps
  Work complete!
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1020069 | Study on (Stage 2 of) Phase 3 for UAS, UAV and UAM | FS_UAS_Ph3 | 09/09/2024 | 100% | SP-231801 | 100% | 
TDoc | Title | Source | Type | For | Agenda item | Agenda item description | Release
SP-251441 | CR Pack on WI VOPS | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19

## Slide 14: 2.4) Rel-19 Work Items: EVS Codec Extension for Immersive Voice and Audio Services, Phase 2 (IVAS_Codec_Ph2) – Complete!
Purpose
  The overall objective of this work item is to provide an improved set of IVAS specifications with a fixed-point C-code to be part of TS 26.251; characterization of the IVAS codec based on the floating-point and fixed-point C-codes, and documentation of characterization results into TR 26.997; Enhancements to codec conformance test procedures and criteria; definition of relevant tiers of functionality to be implementable on a wide range of UEs with different capabilities, balancing user experience and implementation complexity/cost; enhancements to the RTP payload format and SDP negotiation, including split rendering operation; update relevant system and service specifications.
Progress in the last quarter
  Corrections provided for the IVAS algorithmic description and the IVAS-related SDP aspects. The IVAS characterization test plan was agreed, Material collection report, Host Lab report, 12 listening lab reports and the Global Analysis Lab were agreed, the IVAS characterization results was agreed. The draft TS 26.251 with IVAS fixed-point code was finalized and addition of test sequences for fixed-point and non-bit-exact conformance for floating-point was agreed
Next steps
  Work complete!
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1040021 | EVS Codec Extension for Immersive Voice and Audio Services, Phase 2 | IVAS_Codec_Ph2 | 9/9/2025-> 12/12/2025 | 80% | SP-250262 | 100% | Exception requested in SA#109 Complete
TDoc | Title | Source | Type | For | Agenda item | Agenda item description | Release
SP-251435 | CR Pack on WI IVAS_Codec_Ph2 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251447 | MESAQIN.com Listening Lab Report - IVAS Characterization Phase | SA WG4 | report | Approval | 4.4 | SA WG4 reporting | 
SP-251448 | FORCE Technology Listening Lab Report - IVAS Characterization Phase | SA WG4 | report | Approval | 4.4 | SA WG4 reporting | 
SP-251449 | IVAS Characterization Tests - Global Analysis Lab Report | SA WG4 | report | Approval | 4.4 | SA WG4 reporting | 
SP-251444 | Draft TS 26.251 v2.0.0 | SA WG4 | draft TS | Approval | 7.2.4 | SA WG4 Specifications for Approval | Rel-19

## Slide 15: 2.4) Rel-19 Work Items: Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 2 (ATIAS_Ph2) – Complete!
Purpose
  Consider additional requirements corresponding to the test methods in TS 26.260 and/or update requirements marked as TBD for sending and receiving characteristics of terminals in TS 26.261. Define new test methods and performance requirements/objectives, for the assessment of capture and playback of complex sound scenes. Define new test methods and performance requirements/objectives for the assessment of acoustic echo control. Define test methods and performance requirements/objectives for the assessment of binaural rendering in receive direction, including headtracking and motion-to-sound latency.
Progress in the last quarter
  Introduction of new objective test methods and setups, and additional performance requirements and objectives for UEs supporting immersive services based on IVAS codec
Next steps
  Work complete!
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1050113 | Terminal Audio quality performance and Test methods for Immersive Audio Services | ATIAS_Ph2 | 9/9/2025-> 12/12/2025 | 75% | SP-241314 | 100% | Exception requested in SA#109 Complete
TDoc | Title | Source | Type | For | Agenda item | Agenda item description | Release
SP-251442 | CR Pack on ATIAS_Ph2 | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19

## Slide 16: 2.4) Rel-19 Work Items: Stage 3 for Advanced Media Delivery (AMD_PRO-MED) – Complete!
Purpose
  Main objective: Address recommendations from FS_AMD and FS_MS_NS_Ph2 studies in TS 26.510, TS 26.512, and TS 26.517
  MBS Protocol Extensions: In-session unicast repair for MBS Object Distribution; Time synchronization…
  5G Media Streaming Protocol Updates: Common Media Client Data (CMCD); multi-access media delivery; media delivery from multiple service locations
  Content Protection & Distribution: Support for network and client-side interoperability for DRM and Content Protection (reference CPIX & DASH-IF) QoS Improvements: Integrate ECN marking for L4S; Add QoS monitoring features; Network Slicing Support…
  Define APIs and OpenAPI YAML specifications: Collaborate with organizations like SVTA, CTA WAVE, ISO/IEC; API and Protocol Development
Progress in the last quarter
  Provided some XML schema corrections, fixed security procedures and metrics reporting at M3, corrected the M3 data models, corrections of ContentHostingConfiguration and ContentContributionConfiguration OPenAPI schema, agreed OpenAPI YAML updates for in-session repair and updated normative CMMF content preparation template and media player entry references
Next steps
  Work complete!
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1070057 | Stage 3 for Advanced Media Delivery | AMD_PRO-MED | 9/9/2025 | 85% | SP-250265 | 100% | Stage 3 complete in SA#109 Work on OpenAPI complete
TDoc | Title | Source | Type | For | Agenda item | Agenda item description | Release
SP-251443 | CR Pack on AMD_PRO-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19
SP-251436 | CR Pack on 5G_RTP_Ph2, AMD_PRO-MED | SA WG4 | CR pack | Approval | 19.4 | SA WG4 Rel-19 CRs | Rel-19

## Slide 17: 2.5) Rel-20 5G-A Work Items: Overview
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1080049 | Media aspects for AI/ML in IMS services | AIML_IMS-MED | 3/3/2026 | 0% | SP-250878 | 20% | Progress slower then expected
1060022 | Diverse audio CApturing System for UEs | DaCAS | 6/6/2026 | 55% | SP-241962 | 60% | 

## Slide 18: 2.5) Rel-20 5G-A Work Items: AI/ML for IMS services (AIML_IMS-MED)
Purpose
  The AI_IMS-MED work item will focus solely on enabling AI/ML media processing as part of IMS-based services (including audio, video and AR calls) and has the following objectives in Rel-20:
    Extend TS 26.114 and TS 26.264 specifications to support AI/ML data delivery and AI/ML media processing in IMS services.
    Specify support for AI/ML data signaling and negotiation, including support for split inferencing.
    Select interoperable formats for AI/ML model and intermediate data.
    Define the support of the configuration, delivery, compression, and processing of AI/ML data as identified in TR 26.927 clause 6, as needed, along with relevant optional metadata, as identified in TR 26.927 clause 6.6.
Progress in the last quarter
  Agreed, as a basis for further work, a high-level common call flow for device, split and network inferencing. Details include DC app selection, AI task selection as well as related app requirements, UE/MF capabilities and app negotiations. A neutral skeleton CR document was also agreed as basis for further work (target TS still under discussion). WI likely to be extended by at least one meeting.
Next steps
  Progress work on bootstrap and app DC negotiation procedures for AI/ML model delivery; signalling for discovery and configuration of AI/ML; media processing; MF profile for AI/ML processing; Extending UE client Terminal Architecture to support AI/ML processing; Signalling for negotiation and configuration for split inferencing, supporting split and sequential AI/ML processing applications; Specifying interoperable formats and mechanisms for AI/ML model data delivery; Specifying format protocols and signalling of AI/ML intermediate data, including compression where necessary
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1080049 | Media aspects for AI/ML in IMS services | AIML_IMS-MED | 3/3/2026 | 0% | SP-250878 | 20% | Progress slower then expected

## Slide 19: 2.5) Rel-20 5G-A Work Items: Diverse audio Capturing System for UEs (DaCAS)
Purpose
  The overall objective of this work item is to define minimum performance criteria suitable for immersive audio capture. Furthermore, example solutions that meet the minimum performance requirements/objectives are developed. To enable the execution of the work item and evaluation of solutions for immersive audio capture in a transparent manner, a representative set of target devices will be defined, and sufficient test signals are generated based on the devices.
Progress in the last quarter
  Progress on DaCAS-1 (Target devices and databases).
  2 new recording scenarios for object-based audio capturing documented into DaCAS-2 (Test methodologies and requirements) reflecting agreements from previous AH telcos and new proposals (multi-source evaluation for ISM capturing, requirements for raw microphone signals, documentation of microphone signal compensation, referencing of initial test script)
  No update on DaCAS-3 (deliverables for DaCAS)
  Discussions on complexity evaluation, source code, and deliverable.
Next steps
  Continue work on Common database for the target devices and Deliverables of example solutions for the target devices.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1060022 | Diverse audio CApturing System for UEs | DaCAS | 6/6/2026 | 55% | SP-241962 | 60% | 

## Slide 20: 2.6) Rel-20 5G-A Study Items: Overview
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1030009 | Study on Audio Codec APIs | FS_ACAPI | 12/12/2025 -> 6/6/2026 | 49% | SP-240480 | 60% | New completion date
1070055 | Study on Ultra Low Bitrate Speech Codec | FS_ULBC | 6/6/2026 | 15% | SP-250635 | 27% | Progress slower then expected
1080050 | Study on Media energy consumption exposure and evaluation framework Phase 2 | FS_Energy_Ph2_MED | 3/3/2026 | 0% | SP-250636 | 30% | 
1090041 | Study on Usage of Dynamically Changing Traffic Characteristics and Enhanced QoS support in Media Applications and Services | FS_DCTC_eQOS_MED | 9/9/2026 | 0% | SP-250937 | 10% | 
1090042 | Study on Advanced Video Formats and Operation Points | FS_AVFOPS_MED | 6/6/2026 | 0% | SP-250938 | 10% | 
1090043 | Study on 3D Gaussian splats | FS_3DGS_MED | 3/3/2027 | 0% | SP-251190 | 10% | 
1090046 | Study on Advanced Media Delivery Phase 2 | FS_AMD_Ph2 | 6/6/2026 | 0% | SP-251265 | 10% | 

## Slide 21: 2.6) Rel-20 5G-A Study Items: Study on Audio Codec APIs (FS_ACAPI)
Purpose
  The overall objective of this study item is to study APIs to provide support for 3GPP's speech and audio codecs in TS 26.114 and TS 26.117 for enhanced Web-based applications over 3GPP networks.
Progress in the last quarter
  The draft TR 26.858 was updated with agreements related to editorial improvements and considerations to the registration of 3GPP communication codecs as WebCodecs. An LS was sent to W3C accordingly. The completion date is delayed to June 2026.
Next steps
  Continue to identify relevant interfaces on hardware/firmware platforms to the (supported) relevant codecs defined in TS 26.114 and TS 26.117 and other common pre- and postprocessing blocks, including capture front end and renderer, and characterize signal (including control signal and metadata) flows on these interfaces.
  Continue to identify potential gaps in the 3GPP and W3C specifications to enable and simplify the use of the codecs in TS 26.114 and TS 26.117 in WebCodecs and WebRTC
  Continue to identify common APIs for the relevant codecs defined in TS 26.114 and TS 26.117 and other common pre- and postprocessing blocks, including capture front end and renderer, that are useable to expose the identified interfaces.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1030009 | Study on Audio Codec APIs | FS_ACAPI | 12/12/2025 -> 6/6/2026 | 49% | SP-240480 | 60% | New completion date

## Slide 22: 2.6) Rel-20 5G-A Study Items: Study on Ultra Low Bitrate Speech Codec (FS_ULBC)
Purpose
  This study aims to develop recommendations for an ultra-low bitrate voice codec with primary application for GEO (Geostationary Earth Orbit) communications. The main objectives include:
    Application scenarios for ultra-low bitrate communication services; GEO channel characteristics and their service dependencies; design constraints; performance requirements and test methods for speech quality; objective measures for design constraints; reference codecs for comparison; Coordinating with other 3GPP groups.
Progress in the last quarter
  Limited progress due to Release-19 exceptions prioritization. Agreement on the NTN-TDL-C 10° and 50° channel model and NB-IoT NTN system and design parameters.
  11 contributions could not be treated due to lack of time during SA4#134 and will be given priority during the next FS_ULBC AH call.
Next steps
  Finalize study of GEO channel characteristics and derivation of service-related dependencies, e.g. bitrates, mouth-to-ear delay or loss/delay/jitter profiles.
  Progress work on:
    Document existing technologies and feasibility evidence.
    Identify the relevant design constraints.
    Define performance requirements and identify appropriate test methodologies.
    Document Application Scenarios if time permits.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1070055 | Study on Ultra Low Bitrate Speech Codec | FS_ULBC | 6/6/2026 | 15% | SP-250635 | 27% | Progress slower then expected

## Slide 23: 2.6) Rel-20 5G-A Study Items: Study on Media Energy Consumption Exposure and Evaluation Framework phase 2 (FS_Energy_Ph2-MED )
Purpose
  Address, in the context of media delivery, the new Release 20 requirements in TS 22.261 on:
    Energy-related information as a service criterion, including Energy-related info exposure to UEs and authorized third parties over specific time periods, including energy consumption by the serving network
  Update or develop existing potential solutions and proposed normative work associated with the Key Issue on energy-related information exposure in media consumption context
  Propose new potential solutions to phase 1 Key Issues on energy-related monitoring and measurement during media consumption,
  Describe new Key Issues identified during phase 1 about Energy-related configuration by the media Application Service Provider / AS energy management / Client energy management
Progress in the last quarter
  Progress made on the following key issues agreed as basis for further work: KI1:Collecting and reporting an Energy of Service Metric to authorized 3rd parties, KI4:Energy-related configuration by the Application Service Provider for media delivery services, KI5: Media Application Server Energy management, KI6: Client-driven management of media delivery service energy optimization as well as Energy aware streaming.
Next steps
  Update or develop potential solutions on existing key issues.
  Progress work on new potential solutions addressing new key issues.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1080050 | Study on Media energy consumption exposure and evaluation framework Phase 2 | FS_Energy_Ph2_MED | 3/3/2026 | 0% | SP-250636 | 30% | 

## Slide 24: 2.6) Rel-20 5G-A Study Items: Usage on Dynamically Changing Traffic Characteristics and Enhanced QoS support in Media Applications and Services (FS_DCTC_eQOS_MED)
Purpose
  Document popular media applications and service scenarios that may exhibit dynamically changing traffic characteristics.
  For a relevant subset of the media applications/service scenarios defined above do the following:
    Develop observation tests to evaluate these scenarios. Execute the tests and collect relevant information to what extent the reference applications exhibit dynamically changing traffic characteristics. Document possible benefits of applying QoS features
  Based on the findings in the tests from 2 do the following:
    Document and describe observed dynamic traffic characteristics in media applications and services. Document potential improvements when applying different QoS features, for uplink, downlink and with dependent UL/DL flows. Map the reference scenarios to end-to-end procedures
  Based on the findings in 3, do one or more of the following
    Document guidelines on how to identify and characterize dynamic traffic characteristics in media applications and services. Refine call flows and typical workflows involving QoS usage and dynamically changing traffic characteristics usage in typical scenarios using characteristics.
Progress in the last quarter
  Study initiated. Agreed skeleton for draft TR 26.823 and 7 use cases including conversational, short form video, live streaming, video on demand and upstream/downstream AI inferencing.
Next steps
  Continue Document popular media applications and service scenarios that may exhibit dynamically changing traffic characteristics and Develop observation tests to evaluate these scenarios
  Agree on the terminology
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1090041 | Study on Usage of Dynamically Changing Traffic Characteristics and Enhanced QoS support in Media Applications and Services | FS_DCTC_eQOS_MED | 9/9/2026 | 0% | SP-250937 | 10% | 

## Slide 25: 2.6) Rel-20 5G-A Study Items: Study on Advanced Video Formats and Operation Points (FS_AVFOPS_MED)
Purpose
  Identify relevant new representation formats not yet documented in TS 26.265 and provide their benefits in terms of user experience. The analysis includes potential format specificities for capture at interoperability point 2 and for rendering at interoperability point 4. Candidate representations include support for alpha, depth together with stereo, and additional colour subsampling 4:2:2 or 4:4:4.
  Study the feasibility of generating the video signals corresponding to the hypothetical optical system
  Identify compression options for the representation formats based on video codecs supported in 3GPP specifications, with HEVC as priority.
  Identify the opportunities and needs to integrate the representation formats into different transport systems, including messaging, real-time communication, split rendering and streaming formats.
  Define the expected traffic characteristics for new representation formats to meet certain quality thresholds.
  Further develop the bitstream conformance environment, including hosting, tooling and process, as well as collecting sample
  Identify gaps in the following specifications:
    In 3GPP specifications, especially on operation points, and provide guidance for potential normative work.
    In specifications defined by other SDOs (e.g. MPEG) and coordinate possible actions with the relevant SDOs.
Progress in the last quarter
  Study initiated at the last SA4 meeting. Collected 2 new scenarios which are changeable video background and refocusable video. Transferred the Permanent Document on conformance from VOPS to FS_AVFOPS_MED. Established 3GPP Forge project to carry out the conformance work on video operation points
Next steps
  Continue work on the feasibility of generating video signals corresponding to the hypothetical optical system and the associated compression options
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1090042 | Study on Advanced Video Formats and Operation Points | FS_AVFOPS_MED | 6/6/2026 | 0% | SP-250938 | 10% | 

## Slide 26: 2.6) Rel-20 5G-A Study Items: Study on Advanced Video Formats and Operation Points (FS_AVFOPS_MED)
Purpose
  Identify use cases for mobile devices that demonstrate the practical applications of 3DGS representation formats. Based on feasibility, a potential subset of the collected use cases will be prioritized, and the remainder of the study will focus on this selected subset.
  Analyse state-of the-art 3DGS representation formats,
  Study and document content generation aspects and rendering workflow aspects
  Map the relevant workflows to 3GPP services (such as messaging) and identify the media requirements to support the scenario.
  Identify the target bitrates and potential traffic characteristics of 3DGS representations for the selected scenarios and investigate the associated compression aspects.
  Identify needs and requirements for a potentially suitable standardization process, including data sets, training models, test data, etc. for 3DGS representations.
  In parallel to the above objectives: Develop an end-to-end reference implementation for content delivery, covering the entire pipeline from content creation on a server or on the UE and, through compression, transmission, to rendering on a mobile device platform. This work could serve as a basis for future developments and be used in the evaluations carried out during this study.
Progress in the last quarter
  Study initiated at the last SA4 meeting. Definition of the use cases that will be addressed by the study (On-device capture and sharing of a static 3DGS scene, Exploration of a large 3DGS environment, Dynamic 3DGS content, and 3DGS Avatar communication)
  Agreed initial description of the 3DGS process and workflow (3DGS representation format, Static 3DGS content creation, 3DGS rendering)
  Description of the quality factors that impact the 3DGS experience
Next steps
  Complete the identification of use cases for mobile devices that demonstrate the practical applications of 3DGS contents
  Continue the analysis of the 3DGS representation format, Rendering workflow
  Initiate the development an end-to-end reference implementation (mobile renderer)
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1090043 | Study on 3D Gaussian splats | FS_3DGS_MED | 3/3/2027 | 0% | SP-251190 | 10% | 

## Slide 27: 2.6) Rel-20 5G-A Study Items: Study on Advanced Media Delivery Phase 2 (FS_AMD_Ph2)
Purpose
  Document the following additional Key Issues in more detail, in particular how they relate to the 3GPP Media Delivery architecture and/or the MBS User Service architecture:
    WT#1: Common Client Metadata phase 2; WT#2: Server and Network-assisted media streaming; WT#3: Multiple service locations phase 2; WT#4: Combined Unicast-Multicast-Broadcast; WT#5: 5G System-independent Media Streaming; WT#6: Latency Measurements and Control; WT#7: Network Slicing phase 3; WT#8: Multi-access media delivery phase 2
  Study collaboration scenarios between the Application Service Provider and the 5G System and for each of the key topics.
  Based on existing architectures, develop one or more deployment architectures that address the key topics and the collaboration models.
  Map the key topics to basic functions and develop high-level call flows.
  Identify the issues that need to be resolved.
  Provide candidate solutions including call flows, protocols and APIs for each of the identified issues.
Progress in the last quarter
  Study initiated with initial versions of working tasks (agreed as basis for further work): WT1: Comment Client Metadata phase2; WT2a: Comment server and network assisted streaming; WT4: Combined Unicast-Multicast-Broadcast; WT5: 5G system-independent media streaming; and WT6: Latency measurement and control
Next steps
  Complete evaluation of candidate solutions including call flows, protocols and APIs for each of the identified work topics.
  Complete identifying gaps and recommend potential normative work for stage-2 for relevant work topics.
  Agree CRs addressing potential normative work for stage-2 for relevant work topics
  Progress candidate solutions including call flows, protocols and APIs for each of the identified issues.
  Progress identifying gaps for stage-3 for relevant work topics and progress relevant for potential issues related to stage-3
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1090046 | Study on Advanced Media Delivery Phase 2 | FS_AMD_Ph2 | 6/6/2026 | 0% | SP-251265 | 10% | 

## Slide 28: 2.7) New Work & Study Items: Overview
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100004 | Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 3 | ATIAS_Ph3-MED | 3/3/2027 |  | SP-251352 |  | 5GA
1100005 | Study on evaluation of QUIC-based protocols for on-demand and live video services | FS_QStream_MED | 3/3/2027 |  | SP-251353 |  | 5GA
1100006 | Study on IMS DC Enhancements | FS_DCE_MED | 6/6/2026 |  | SP-251354 |  | 5GA
1100007 | Study on QUIC-based Media Delivery for Real-time Communication | FS_Q4RTC_MED | 3/3/2027 |  | SP-251355 |  | 5GA
1100008 | Study on advanced image formats | FS_AIF_MED | 9/9/2026 |  | SP-251356 |  | 5GA
1100009 | Study on Avatar communication Phase 2 | FS_Avatar_Ph2_MED | 9/9/2026 |  | SP-251357 |  | 5GA
1100010 | Study on Media Aspects for 6G System | FS_6G_MED | 3/3/2027 |  | SP-251358 |  | 6G

## Slide 29: 2.7) New Work & Study Items: New work on Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 3 (ATIAS_Ph3-MED)
Purpose
  Define new and consolidate existing requirements for sending and receiving characteristics of immersive UEs.
  Review test methods and requirements on acoustic echo control (AEC) and possibly extend these clauses in TS 26.260/261 for double talk scenarios.
  Extend test methods for the assessment of complex sound scenes that are captured, processed and transmitted by the UE.
  Develop new test methods adapt existing transparency test methods to be adapted to noise suppression algorithms including possible degradations in speech quality
  Refine and extend test methods for binaural rendering at the acoustical interface, with better distinction between headtracking performance and motion-to-sound latency.
    Note: As in previous phases, the definition of requirements and test methods shall balance technical complexity with practical feasibility and industry acceptance.
  Review and possibly update existing test methods and requirements, ideally supported by measurement results originated from e.g., simulations, prototypes and/or even first) commercially available devices.
  If applicable
    consider additional aspects of UE audio capture and processing, ensuring alignment with related work items such as DaCAS.
    include additional test methods for clause 4 of 3GPP TS 26.260, which is generically about immersive capturing/playback devices,
  Coordination with committees from certain SDOs (e.g., GSMA TSG, ETSI STQ, ITU-T SG12, etc.) that are known for having aspects of terminal testing in their scope.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100004 | Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 3 | ATIAS_Ph3-MED | 3/3/2027 |  | SP-251352 |  | 5GA

## Slide 30: 2.7) New Work & Study Items: New study on evaluation of QUIC-based protocols for on-demand and live video services (FS_QStream_MED)
Purpose
  Identify application scenarios and their (uplink and downlink) delivery characteristics of segmented media delivery services and applications.
  Identify existing and emerging segmented media streaming technologies such as QUIC-based streaming technologies based on those identified in TR 26.804,
  Define an evaluation framework for media delivery protocols in the context of 5G Media Streaming downlink as defined in TS 26.501 and TS 26.512 to evaluate emerging technologies:
    Determine the set of existing metrics to be collected that are reflecting QoE, and if needed, their respective QoS metrics.
    Document potential impact of deploying QUIC-based streaming technologies on 5GMS architecture, delivery protocols, and codecs and formats
    Design a test framework for collecting the selected metrics for evaluating the baseline with identified technologies.
  Evaluate selected technologies, by collecting the QoE metrics, using the framework developed, for the selected use cases identified under 3GPP network conditions. Develop the network simulation setup and select the network traces for the identified relevant application scenarios.
  If sufficient evidence of benefits are identified :
      Study the integration into 5G Media streaming and identify potential gaps in the 5GSM architecture, protocols and codecs and formats
      Identify corresponding potential normative work
  Communicate the progress of this study to relevant SDOs such as the IETF MoQ Working Groups and solicit collaboration with organizations conducting similar work such as SVTA.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100005 | Study on evaluation of QUIC-based protocols for on-demand and live video services | FS_QStream_MED | 3/3/2027 |  | SP-251353 |  | 5GA

## Slide 31: 2.7) New Work & Study Items: New study on IMS DC Enhancements (FS_DCE_MED)
Purpose
  KI#1: Analyze multiplexing edge‑cases (per TS 23.228 AC.7.10)
    Study multi‑application multiplexing when an m‑line combines several a=3gpp-req-app with mixed endpoint types (…-UE and …-Server).
    Document examples aligning with stage‑2 procedures.
  KI#2: Interworking facilitation with MTSI
    Study signaling aspects for associating a DC application stream to MF‑anchored RTP legs when interworking is invoked per TS 23.228 AC.7.9.
    Document informative examples consistent with TS 23.228 AC.7.9 flows.
  KI#3: Clarifications to HTTP protocol usage on DC
    Study and recommend solutions for the handling of external resources.
    Document guidelines on the DC application behavior for the HTTP subprotocol.
  KI#4: Consolidate Rel‑19 stage 3 implications from NG_RTC_Ph2 and address identified ambiguities, if applicable, and features from other 3GPP WGs and SDOs, such as GSMA (e.g. their LS on Automatic Resumption), and any future incoming LSs.
  KI#5: Identify inconsistencies and ambiguities, if any, between TS 23.228 and TS 26.114, TS 26.264 and TS 26.567and document alignment and clarification actions, if needed.
  KI#6 Document any new media use cases and identify any gaps and potential solutions, if needed, for IMS DC based on SA1 requirements.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100006 | Study on IMS DC Enhancements | FS_DCE_MED | 6/6/2026 |  | SP-251354 |  | 5GA

## Slide 32: 2.7) New Work & Study Items: New study on QUIC-based Media Delivery for Real-time Communication (FS_Q4RTC_MED)
Purpose
  Identify existing and emerging QUIC-based media delivery protocols suitable for real-time communication and document their features, benefits, limitations and current applications.
  Define an evaluation framework for QUIC-based media delivery protocols in the context of the RTC System as defined in TS 26.506 and TS 26.113.
    Define application scenarios for which the evaluation of QUIC-based media delivery protocols is carried out
    For the identified application scenarios, define appropriate performance metrics, requirements and evaluate the performance of the QUIC-based media delivery protocols against existing architectures and protocols as defined in TS 26.506 and TS 26.113
    Document potential impact of deploying QUIC-based technologies on the delivery architecture defined in TS 26.506
  If sufficient evidence of benefits for the selected QUIC-based media delivery protocols in the context of RTC are identified
    Study integration into the RTC System.
    Identify gaps and potential normative work on the architecture and procedures of the RTC System as well as on its protocols and APIs.
  Coordinate work with other 3GPP groups and the IETF as needed.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100007 | Study on QUIC-based Media Delivery for Real-time Communication | FS_Q4RTC_MED | 3/3/2027 |  | SP-251355 |  | 5GA

## Slide 33: 2.7) New Work & Study Items: New study on advanced image formats (FS_AIF_MED)
Purpose
  Identify currently widely employed use cases of still images on mobile devices:
    Sharing of images using messaging services including 3GPP and 3rd party services.
    Traditional photo taking for uploading to and sharing via cloud, social networking, as well as device-to-device sharing.
    Taking, processing, and sharing of screen captures.
    HDR processing, visualization, and rendering aspects.
  Identify already widely employed and 3GPP relevant imaging formats in the market for each of these use cases. When video coding tools are used for images, the study would primarily focus on HEVC as an existing 3GPP codec.
  Document image capturing formats for traditional photography.
  Based on the identified image formats, identify key operating points suitable for interoperability for these image formats.
  In the cases where interoperability is not the primary focus, a list of guidelines may be provided for mobile devices, based on other criteria such as screen capabilities and computational resource consumption. These use cases are:
    use of tiling for editing and random access of large images.
    HDR gain map metadata processing capabilities in relation to device support of SDR only/HLG/PQ.
  Investigate the development of conformance material to support interoperable generation and consumption of still images in 3GPP relevant messages and services.
  Provide recommendations for potential subsequent normative work.
  Liaise with ISO/IEC JTC1/SC29 (MPEG), ISO/IEC TC 42, and GSMA RCSG on this topic as needed.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100008 | Study on advanced image formats | FS_AIF_MED | 9/9/2026 |  | SP-251356 |  | 5GA

## Slide 34: 2.7) New Work & Study Items: New study on Avatar communication Phase 2 (FS_Avatar_Ph2_MED)
Purpose
  Document additional Avatar-based real-time communication use cases, such as the integration of Avatars and network-based media processing (e.g., AI/ML processing) for real time services (within IMS and non-IMS), and multiparty Avatar call using common scene
  Define Quality of Experience (QoE) metrics and Quality of Service (QoS) requirements specific to Avatar communication services and evaluate Avatar formats in this context.
  Develop evaluation criteria and provide evaluations for animating techniques to enhance realism and user interactivity. Coordinate with relevant SDOs (e.g., MPEG) and utilize existing evaluations where needed.
  Evaluate communication techniques to meet animation quality as identified in Objective (3).
  Study and document Avatar creation process.
  In collaboration with SA3, study security implications, focusing on identification, authentication (including schemes for Avatar related APIs), privacy preservation, content protection (e.g. watermarking and DRM), and secure distribution mechanisms for Avatar data,
  Document existing compression methods for static Avatar data and animation streams and identify suitable solutions for 3GPP.
  Evaluate mechanisms to support more realistic and natural animation of some dynamic components (accessories, hair, clothes, etc.) of an Avatar.
  Coordinate with MPEG and other SDO’s as needed and for any gaps that are identified.
  Study Architectural gaps and potential enhancements and align with other related 3GPP group: including those identified in TS 26.264 and non-IMS scenarios.
  Identify gaps in existing specifications for potential normative work.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100009 | Study on Avatar communication Phase 2 | FS_Avatar_Ph2_MED | 9/9/2026 |  | SP-251357 |  | 5GA

## Slide 35: 2.7) New Work & Study Items: New study on New Media Aspects for 6G System (FS_6G_MED)
Purpose
  Document the work topics introduced above in more detail, in particular how they relate to media delivery and taking into account the progress in other working groups:
    WT#1: Media Delivery Architecture
    WT#2: 6G Media
    WT#3: Media Aspects related to SA2 topics
    WT#4: Media for ubiquitous access
    WT#5: Trusted and private media communication
  Identify the dependencies of the issue to other working groups and collect information on relevant developments within 3GPP and externally.
    NOTE: Topics potentially requiring input into other WG studies or those creating dependencies on other work topics will be prioritized.
  Based on existing media delivery architectures and functionalities, as well as the development in SA2 architectures, and design concepts with respect to 6G, map the work topics to basic functions and develop high-level call flows, if appropriate.
  Identify potential gaps and opportunities that may need solutions and either
    recommend potential further study or normative work for stage-2 and stage-3, including which existing specifications would be impacted and/or if any new specifications would preferably be developed.
    provide candidate solutions that may address the issues
  Coordinate work with other 3GPP groups e.g. SA2, SA3, SA5, SA6 and others as needed.
  Coordinate work with external organizations such as SVTA, CTA WAVE, ISO/IEC JTC1 SC 29, 5G-MAG, Metaverse Standards Forum, Khronos or IETF, as needed.
UID | Name | Acronym | Target (dd/mm/yyyy) | Old % | WID | New % | Change or comment
1100010 | Study on Media Aspects for 6G System | FS_6G_MED | 3/3/2027 |  | SP-251358 |  | 6G
During the study, the progress and results of 3GPP TR 22.870 (SA1 study), TR 38.960 (RAN study), TR 23.801-01 (SA2 study) and possibly other working groups will be taken into account.
Specific work topics may be concluded earlier than the envisaged timeline below and may then be progressed in a dedicated study in a newly defined timeframe. In such a case this study will refer to the dedicated study where relevant.

## Slide 36: 3) SA4 Work Planning: General
SA4 working assumptions in the Rel-20 definition
  It is anticipated that 5G Advanced topics may be proposed as a follow-up of Release19 activities or as a request to implement stage 3 from other 3GPP WGs (or any new topic).
  There is a wish to not only initiate 6G studies but also to build up a global vision on what 6G means in terms of media experience.
  On the requested work split from SA, it is foreseen to start Release 20 with 90% of 5GA and 10% of 6G.
Requested information for new work and study
  Any Release 20 study or work item proposal is requested to be accompanied with the following information:
    Preliminary work plan
    Anticipated normative work (e.g., same release or the following one, on which specs…)
    Any intent to provide corresponding implementations: test vectors, APIs, reference implementation (internally developed by 3GPP, supported externally e.g., by MRP…)
    Expected SA approval date (package 1 or 2).
    Indication of 5GA or 6G topic
    Expected SWG(s) to host the proposal (may be joint).

## Slide 37: 3) SA4 Work Planning: General
SA4 agreed to work on 2 packages
  Package 1 delivered in Sept. 2025
  Package 2 delivered in Dec. 2025
SA4#132 - May 25: 1st round of Rel-20 topics reviewed with a few ideas presented for information and triggering discussions.
  FS_Energy_Ph2_MED and AIML_IMS-MED agreed due to stage 2 aspects.
SA4 AH call - 10th Jul. 25: Dedicated SA4 AhG call reviewing around 12 proposals presented with more details (see next slide)
SA4#133e - Jul. 25: 1st decisions made with the selection of the first topics and the identification of strong candidates for the 2nd package
  3 Package 1 proposals were agreed : FS_AVFOPS_MED, FS_3DGS_6G_MED & FS_DCTC_eQOS_MED. Other proposals are deferred to package 2.
SA4#134 – November 25: Review of package 2 candidates to be submitted to SA#110 in Dec. 25

## Slide 38: 3) SA4 Work Planning:

## Slide 39: 4) External SDOs interaction (including IETF dependencies)
Incoming LS
  Received during SA4#134 from ITU-T SG12, ITU-T JCA-IMT2020, ITU-T SPAIAS, ISO/IEC/JTC1/SC29(MPEG), 5G-MAG
  More details here: https://www.3gpp.org/Liaisons/Incoming_LSs/S4-meeting.htm
Outgoing LS
  Approved during SA4134 to ISO/IEC/JTC1/SC29(MPEG), W3C
  Approved reply LS to GSMA sent to SA#110 for consolidation
  More details here: https://www.3gpp.org/Liaisons/Outgoing_LSs/S4-meeting.htm
IETF dependencies
  No new dependency introduced
  No new dependency removed
TDoc | Title | Source
SP-251301 | LS from SA WG4: LS reply on External Resource Handling in IMS Data Channel | SA WG4

## Slide 40: 5) Collected Items requiring action from SA
Action items from SA4 to SA#110:
  Approve the Rel-12 and all Rel-17 to Rel-19 SA4 agreed CRs
  Approve the 3GPP TS 26.251 - Codec for Immersive Voice and Audio Services (IVAS); C code (fixed-point)
  Approve the Listening Labs and Global analysis report on the verification of IVAS fixed-point Encoder
  Approve the New Rel-20 Work Item Description on Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 3 (ATIAS_ph3-MED)
  Approve the New Rel-20 Study Item Description on IMS DC Enhancements (FS_DCE_MED)
  Approve the New Rel-20 Study Item Description on QUIC-based Media Delivery for Real-time Communication (FS_Q4RTC_MED)
  Approve the New Rel-20 Study Item Description on evaluation of QUIC-based protocols for on-demand and live video services (FS_QStream_MED)
  Approve the New Rel-20 Study Item Description on Avatar communication Phase 2 (FS_Avatar_Ph2_MED)
  Approve the New Rel-20 Study Item Description on advanced image formats (FS_AIF_MED)
  Approve the New 6G Rel-20 Study Item Description on Media Aspects for 6G System (FS_6G_MED)
  Provide guidance to SA4 on how to address the AI/ML topic within SA4 as part of its efforts to update the ToRs
  Consider the SA4 reply LS to GSMA NG UPG sent to SA for consolidation.

## Slide 41: 6) Documents for Information and Approval
New SID/WID for Approval
TSG SA TDoc# | Type | Title | Acronym
SP-251352 | WID | Terminal Audio quality performance and Test methods for Immersive Audio Services, Phase 3 | ATIAS_Ph3-MED
SP-251353 | SID | Study on evaluation of QUIC-based protocols for on-demand and live video services | FS_QStream_MED
SP-251354 | SID | Study on IMS DC Enhancements | FS_DCE_MED
SP-251355 | SID | Study on QUIC-based Media Delivery for Real-time Communication | FS_Q4RTC_MED
SP-251356 | SID | Study on advanced image formats | FS_AIF_MED
SP-251357 | SID | Study on Avatar communication Phase 2 | FS_Avatar_Ph2_MED
SP-251358 | SID | Study on Media Aspects for 6G System | FS_6G_MED

## Slide 42: 6) Documents for Information and Approval
TSs/TRs for Approval
TSG SA TDoc# | Title | Release | TR/TS | WI Acronym
SP-251444 | Draft TS 26.251 v2.0.0 | Rel-19 | 26.251 | IVAS_Codec_Ph2

## Slide 43: Thank You !