## Slide 1
Puneet Jain
SA2 Chairman, Intel
Maurice Pope
SA2 Secretary, MCC
SA2 Status Report to
TSG SA#85

## Slide 2: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Work and Maintenance
  2.3) Rel-16 Work and Maintenance
  2.4) Rel-17 Work
  2.5) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA

## Slide 3: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Work and Maintenance
  2.3) Rel-16 Work and Maintenance
  2.4) Rel-17 Work
  2.5) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 4: 1) General Aspects (1/7)
SA2 meetings held since SA#84
  SA2#134: 24 – 28 June 2019, Sapporo, Japan
Future SA2 meetings
  SA2#135: 14 – 18 Oct 2019, Split, Croatia
  SA2#136: 18 – 22 Nov 2019, Reno, NV, USA

## Slide 5: 1) General Aspects (2/7)
SA2 WG leadership
  Chairman: Puneet Jain (Intel)
  Vice Chairmen: Tao Sun (CMCC), Andrew Bennett (Samsung)
  Secretary: Maurice Pope (MCC)
Parallel sessions held in the last plenary cycle
  SA2 has one main session and 2 parallel sessions for most part.
  Many thanks to Maurice Pope and parallel session chairs, Andrew Bennett, Tao Sun, and LaeYoung Kim for their outstanding support!

## Slide 6: 1) General Aspects (3/7)
Statistics at SA WG2 #134:
229 delegates ‘attended’ (checked-in) SA WG2 #134
  1625 documents, 1370 Tdocs handled (including revisions), including
    1252 CRs (including revisions)
    48 Incoming LSs, of which 7 were postponed
    27 Outgoing LSs Approved
  255 Tdocs postponed / not handled
Total CRs agreed: 299 (of which, 2 conditionally approved)
656 people registered on the SA WG2 e-mail reflector on 02 September 2019

## Slide 7: 1) General Aspects (4/7)
Chart: SA WG2 meeting attendance
| 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 113AH | 114 | 115 | 116 | 116bis | 117 | 118 | 118bis | 119 | 120 | 121 | 122 | 122bis | 123 | 124 | 125 | 126 | 127 | 127bis | 128 | 128bis | 129 | 129bis | 130 | 131 | 132 | 133 | 134
attended | 157 | 139 | 133 | 162 | 135 | 142 | 139 | 173 | 181 | 165 | 158 | 153 | 189 | 146 | 133 | 145 | 142 | 144 | 195 | 159 | 175 | 182 | 113 | 137 | 200 | 137 | 107 | 157 | 168 | 169 | 143 | 157 | 233 | 182 | 175 | 191 | 188 | 156 | 154 | 156 | 222 | 196 | 174 | 149 | 140 | 152 | 149 | 165 | 191 | 153 | 178 | 279 | 280 | 229

## Slide 8: 1) General Aspects (5/7) Resource usage
SA2 meetings
Number of Sessions
Chart: 
| #118bis Jan | #119 Feb | #121 May | #122 Jun | #122bis Aug | #123 Oct | #124 Nov | #125 Jan | #126 Feb | #127 Apr | #127bis May | #128 Jul | #128bis Aug | #129 Oct | #129bis Nov | #130 Jan | #131 Feb | #132 Apr | #133 May | #134 Jun
maintenance | 5 | 6 | 6.5 | 6 | 3.4 | 5 | 3 | 4.5 | 3.8 | 4 | 4 | 1.5 | 1.2 | 3 | 1.5 | 0.9 | 0.9 | 2 | 0.9 | 3.5
Rel-15 5GS / maintenance | 18 | 23 | 27 | 31 | 32.5 | 36 | 37 | 24 | 25 | 19 | 19 | 15 | 15 | 13.7 | 11.5 | 9 | 9.3 | 8.2 | 7.2 | 6
Rel-15 other | 2.5 | 8.5 | 11.5 | 8.3 | 6.3 | 4 | 3
Rel-16 work | 3.7 | 13.5 | 12 | 19.5 | 20 | 26.4 | 28.6 | 31.2 | 34.9 | 34.9 | 34.4 | 35.3 | 37.7 | 33
Rel-15 exceptions | 1 | 1.3 | 1 | 0.2

## Slide 9: 1) General Aspects (6/7) Document Handling / Meeting
Number of Tdocs
Rel-12
Rel-11
Rel-14
Rel-13
Rel-15
Rel-16
Rel-17
Chart: 

## Slide 10: 1) General Aspects (7/7) SA2 Agreed CRs by Release / Meeting
Rel-12
Rel-11
Rel-14
Number of CRs
Rel-13
Rel-15
Rel-16
Rel-17
Chart: 
| 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107+E | 108 | 109 | 110 | 110AH | 111 | 112 | 113 | 113AH | 114 | 115 | 116 | 116bis | 117 | 118 | 118bis | 119 | 120 | 121 | 122 | 122bis | 122e | 123 | 124 | 125 | 126 | 127 | 127bis | 128 | 128bis | 129 | 129bis | 130 | 131 | 132 | 133 | 134
Rel-10 CR | 130 | 52 | 41 | 54 | 38 | 38 | 21 | 21 | 17 | 3 | 3 | 9 | 1 | 6 | 2 | 3 | 3 | 4 | 0 | 0 | 2 | 3 | 6 | 3 | 1 | 3 | 1 | 0 | 1 | 1 | 1
Rel-11 CR | 0 | 2 | 3 | 12 | 16 | 7 | 31 | 26 | 23 | 105 | 71 | 53 | 45 | 18 | 27 | 20 | 20 | 19 | 17 | 10 | 7 | 4 | 5 | 5 | 0 | 6 | 3 | 1 | 1 | 1
Rel-12 CR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 4 | 11 | 8 | 19 | 21 | 35 | 50 | 38 | 64 | 55 | 39 | 35 | 34 | 21 | 11 | 10 | 9 | 1 | 9 | 3 | 3 | 3 | 1
Rel-13 CR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 10 | 19 | 13 | 14 | 6 | 9 | 56 | 25 | 58 | 73 | 41 | 11 | 35 | 29 | 25 | 25 | 9 | 11 | 2 | 5 | 2 | 4 | 2 | 5 | 3 | 1 | 1 | 1 | 1
Rel-14 CR | 4 | 21 | 69 | 81 | 33 | 56 | 23 | 13 | 17 | 18 | 20 | 10 | 8 | 10 | 8 | 1 | 7 | 2 | 1 | 2 | 5 | 1
Rel-15 PCR/draftCR | 63 | 126 | 117 | 121 | 171 | 214 | 62 | 287 | 328 | 182 | 4
Rel-15 CR | 19 | 19 | 27 | 27 | 12 | 351 | 201 | 213 | 119 | 159 | 100 | 102 | 78 | 74 | 50 | 40 | 17
Rel-16 PCR/draftCR | 43 | 80 | 170 | 147 | 181 | 171 | 207 | 250 | 88 | 87 | 71 | 103 | 26
Rel-16 CR | 2 | 3 | 66 | 133 | 117 | 233 | 279

## Slide 11: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-15 Work and Maintenance
  2.3) Rel-16 Work and Maintenance
  2.4) Rel-17 Work
  2.5) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 12: 2.1) Rel-14 and before Maintenance (1/1)
Work Progress on Corrections (Category A CRs are not counted)
  R12: none
  R13: none
  R14: none

## Slide 13: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2 Rel-15 Work and Maintenance
  2.3) Rel-16 Work and Maintenance
  2.4) Rel-17 Work
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 14: 2.2) Rel-15 Work and Maintenance (1/2)
WI | Work Item | WP | CRs approved
VoWLAN | Complementary Features for Voice services over WLAN | 100% | 
ProSe_WLAN_DD_Stage2 | Inclusion of WLAN direct discovery technologies as an alternative for ProSe direct discovery | 100% | 
NAPS | Northbound APIs for SCEF – SCS/AS Interworking | 100% | 2
eVoLP | enhanced VoLTE performance | 100% | 
USOS | Unlicensed spectrum offloading system enhancements | 100% | 
EDCE5 | EPC enhancements to support 5G New Radio via Dual Connectivity | 100% | 4
PS_Data_Off_Phase2 | PS Data Off Feature Phase 2 | 100% | 
EPS_URLLC | EPC support for E-UTRAN Ultra Reliable Low Latency Comm. | 100% | 
TEI15 | Maintenance for pre-Rel-15 features in Rel-15 |  | 1
TEI15 | Rel-15 Cat B/C alignments with other WGs or specifically required |  | 

## Slide 15: 2.2) Rel-15 Work and Maintenance (2/2)
Progress since SA#84:
  CRs agreed for TS 23.501 (93 CRs), TS 23.502 (101 CRs), TS 23.503 (19 CRs)
  12 CRs agreed for TS 23.401
Next steps:
  FASMO corrections
  Further aligning with the work from other WGs
WI Code | Work Item Title | WP | Target Date | WID#
5GS_Ph1 | 5G System – Phase 1 | 100% | Dec, 17 | SP-160958

## Slide 16: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Work and Maintenance
  2.3) Rel-16 Work and Maintenance
  2.4) Rel-17 Work
  2.5) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 17: 2.3) Rel-16 Work and Maintenance (1/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_PARLOS_SA2 | Study on System enhancements for Provision of Access to Restricted Local Operator Services by Unauthenticated UEs | 100 > 100% | Sep, 18 | SP-180501
PARLOS | System enhancements for Provision of Access to Restricted Local Operator Services by Unauthenticated UEs | 100 > 100% | Mar, 19 | SP-180738
Progress since SA#84:
  1 CR agreed at SA2 on alignment with CT1 on Emergency service for RLOS attached UE.
  RAN impacts or dependencies:
  RLOS indicator in RRC (solved at last plenary)
Next steps:
  Maintenance

## Slide 18: 2.3) Rel-16 Work and Maintenance (2/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_5WWC | Study on the Wireless and Wireline Convergence for the 5G system architecture | 100 > 100% | Dec, 18 | SP-170380
5WWC | Wireless and Wireline Convergence for the 5G system architecture | 85 > 100% | Jun, 19 | SP-181117
Progress since SA#84:
  Exception requested at SA#84 were completed.
  Procedures for the Non-3GPP device not supporting NAS connected to a Trusted Non-3GPP Access Network.
  for 5G-RG the specification related to Policy management as defined in TS 23.503
  Complete support of FN-RG
  Completed definition of support of IPTV
  RAN impacts or dependencies:
  specification of N2 (NGAP) extension
Next steps:
  Maintenance

## Slide 19: 2.3) Rel-16 Work and Maintenance (3/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_ATSSS | Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture | 100 > 100% | Dec, 18 | SP-180732
ATSSS | Access Traffic Steering, Switch and Splitting support in the 5G system architecture | 85 > 100% | Jun,19 | SP-181124
Progress since SA#84:
  The following two exceptions requested at SA#84 were completed
    EPC Interworking for MA-PDU Session
    How the network can request the re-activation of user-plane resources for the Non-3GPP access of the MA PDU Session
  RAN impacts and dependencies:
  None identified
Next steps:
  Maintenance

## Slide 20: 2.3) Rel-16 Work and Maintenance (4/19)
Progress since SA#84:
  Normative work progressed under the exception.
  New TS 23.287 progressed and is provided for approval.
  CRs to TS 23.501/502/503 and CR to TS 23.285 agreed.
  CR to TS 23.288 (with eNA & eV2XARC WI code) agreed.
RAN impacts or dependencies:
  RAN: NR PC5 unicast/groupcast/broadcast (e.g. PC5 QoS details, PC5 Signalling for unicast), Enhancements to QoS handling for Uu communication – One LS ask RAN2/3 for feedback
  SA3: PC5 unicast and groupcast security protection
Next steps:
  Maintenance and aligning with the work from other WGs.
WI Code | Work Item Title | WP | Target Date | WID#
FS_eV2XARC | Study on architecture enhancements for 3GPP support of advanced V2X services (FS_eV2XARC) | 100 > 100% | Dec, 18 | SP-180733
eV2XARC | Architecture enhancements for 3GPP support of advanced V2X services (eV2XARC) | 75 > 90% | Jun, 19 | SP-181121

## Slide 21: 2.3) Rel-16 Work and Maintenance (5/19)
Progress since SA#84:
  Clarification about Service experience/Abnormal behavior related network data analytics
  Make progress in resolving open issues
RAN impacts or dependences:
  Feedback from RAN3 on input data on Performance Measurements relevant to determine User Data Congestion Analytics
Next steps:
  Finalise normative work by resolving the open issues, which are mostly related to alignment between SA2 and SA5/RAN3
  Maintenance
WI Code | Work Item Title | WP | Target Date | WID#
FS_eNA | Study of enablers for Network Automation for 5G | 94 > 100% | Dec, 18 | SP-180792
eNA | Enablers for Network Automation for 5G | 85 > 92% | Jun, 19 | SP-181123

## Slide 22: 2.3) Rel-16 Work and Maintenance (6/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_CIoT_5G | Study on Cellular IoT support and evolution for the 5G System | 95 > 100% | Dec, 18 | SP-180614
5G_CIoT | Cellular IoT support and evolution for the 5G System | 95 > 98% | Jun, 19 | SP-181118
Progress since SA#84:
  Items on Exception requested at SA#84 were completed.
  Corrections and outstanding issues addressed for almost all 5G CIoT sub-features
  RAN impacts or dependencies:
  Support of NB-IoT/eMTC connected to 5GC, impacts due to Data over NAS and UP optimisation, MO/MT EDT, eDRX, Inter-UE QoS for CP Optimisation, Enhanced Coverage, Expected UE behavior signaling to RAN, signaling of CIoT feature support, LTE-M identification.
Next steps:
  Maintenance
  Complete outstanding issues related to RAN alignment:
    Subscribing to availability after downlink data delivery failure if buffering in the UPF is used
    EDT for 5GS UP optimization
    Support of LTE-M identification (SA2 was awaiting RAN2 feedback; expected to be received by next SA2 meeting)

## Slide 23: 2.3) Rel-16 Work and Maintenance (7/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_ETSUN | Study on Enhancing Topology of SMF and UPF in 5G Networks | 100 > 100% | Dec, 18 | SP-180731
ETSUN | Enhancing Topology of SMF and UPF in 5G Networks | 90 > 100% | Jun, 19 | SP-181116
Progress since SA#84:
  8 CR(s) agreed at SA2
  RAN impacts and dependencies:
  None identified
Next steps:
  Maintenance

## Slide 24: 2.3) Rel-16 Work and Maintenance (8/19)
Progress since SA#84:
  Items listed in the Exception Sheet have been completed
  Some Maintenance CRs approved
RAN impacts or dependencies:
  LS from RAN WG2 on “broadcast assistance data delivery” handled and replied, solution similar to LTE has been specified for broadcast assistance data delivery in 5GS.
Next steps:
  Maintenance
WI Code | Work Item Title | WP | Target Date | WID#
FS_eLCS | Study on Enhancement to Service Based Architecture for Location Services | 100 > 100% | Mar, 19 | SP-180734
5G_eLCS | Enhancement to Service Based Architecture for Location Services | 85 > 100% | Jun, 19 | SP-181119

## Slide 25: 2.3) Rel-16 Work and Maintenance (9/19)
Progress since SA#84:
  Outstanding issues on exception request completed except from UCMF restoration that was preferred to be addressed in CT4
  CRs to TS 23.501, TS 23.401 and TS 23.502 approved by SA2 document all RACS functionality and procedures for 5GS and EPS
RAN impacts or dependencies:
  As per SA2 agreed CRs
Next steps:
  Maintenance
WI Code | Work Item Title | WP | Target Date | WID#
FS_RACS | Study on optimisations on UE radio capability signalling | 100 > 100% | Dec, 18 | SP-180599
RACS | Optimisations on UE radio capability signalling | 90 > 100% | Jun, 19 | SP-190180

## Slide 26: 2.3) Rel-16 Work and Maintenance (10/19)
Progress since SA#84:
  5G-LAN (100%) – Corrections and clarifications related to group management and N19 tunnel management. Open on 5G VN group – one SMF vs. multiple SMF(s).
  NPN (100%) - Progress on access to NPN/PLMN services, CAG and NID related maintenance aspects. Use of GUAMI with shared PLMN ID also clarified i.e. by using NID in the RRC/N2 message.
  TSC (97%) – Exception granted at SA#84 completed (including bridge management, TSCAI derivation, procedure, policy updates etc). Open related to IEEE TSN specification (for which SA2 sent an LS to IEEE), and LLDP and bridge management will be resolved at next meeting.
RAN impacts or dependencies:
  Potential corrections, alignment of TSC (TSCAI related) and NPN aspects (NID, CAG related) based on discussions in RAN2, RAN3 meetings.
Next steps:
  Maintenance. Response and resolution to potential LS from SA3, CT1, RAN2/3, IEEE on NPN and TSC aspects, maintenance and alignment work expected.
WI Code | Work Item Title | WP | Target Date | WID#
FS_Vertical_LAN | Study on 5GS Enhanced support of Vertical and LAN Services | 92 > 100% | Dec, 18 | SP-180507
Vertical_LAN | 5GS Enhanced support of Vertical and LAN Services | 90 > 97% | Jun, 19 | SP-181120

## Slide 27: 2.3) Rel-16 Work and Maintenance (11/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_5G_URLLC | Study on enhancement of URLLC supporting in 5GC | 95 > 100% | Jun, 19 | SP-180118
5G_URLLC | Enhancement of URLLC supporting in 5GC | 80 > 100% | Jun, 19 | SP-181122
Progress since SA#84:
  Progressed normative work by endorsing/refining solutions for the concluded key issues to TSs 23.501/23.502/23.503.
  Key issue #7 (Automatic GBR Service Recovery) was discussed but no consensus was achieved on the conclusion.
RAN impacts and dependencies:
  None identified
Next steps:
  Maintenance

## Slide 28: 2.3) Rel-16 Work and Maintenance (12/19)
Progress since SA#84:
  SMF Delegated Discovery and Selection in HR and specific SMF Service Areas scenarios
  Context transfer update
  Completion of the PCF Group
RAN impacts or dependencies:
  None identified
Next steps:
  Maintenance
WI Code | Work Item Title | WP | Target Date | WID#
FS_eSBA | Study on Enhancements to the Service-Based 5G System Architecture | 100 > 100% | Dec, 18 | SP-180231
5G_eSBA | Enhancements to the Service-Based 5G System Architecture | 80 > 100% | Jun, 19 | SP-181125

## Slide 29: 2.3) Rel-16 Work and Maintenance (13/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_eNS | Study on Enhancement of Network Slicing | 100 > 100% | Dec. 18 | SP-180503
eNS | Enhancement of Network Slicing | 100 > 100% | Jun. 19 | SP-181232
Progress since SA#84:
  The slice specific security support and eNS interworking support between 5GS and EPS were concluded
  RAN impacts and dependencies:
  None
Next steps:
  Maintenance
  Resolve EN e.g. based on feedback from SA3

## Slide 30: 2.3) Rel-16 Work and Maintenance (14/19)
Progress since SA#84:
  Study Work: 1 CR on TR 23.973 clean up agreed.
  Normative Work: No activity in the quarter
RAN impacts or dependencies:
  None identified
Next steps:
  Maintenance
WI Code | Work Item Title | WP | Target Date | WID#
FS_UDICoM | Study on User data interworking, Coexistence and Migration | 75 > 100% | Jun, 19 | SP-190148
UDICoM | User data interworking, Coexistence and Migration | 100 > 100% | Jun, 19 | SP-190182

## Slide 31: 2.3) Rel-16 Work and Maintenance (15/19)
Progress since SA#84:
  9 P-CRs on updating key issues, solutions and evaluations
  TR 23.737 sent for Information
RAN impacts or dependencies:
  Possible impacts identified for the normalization phase on Satellite RAN Identifiers.
Next steps:
  Finalize the solution to different Key issues by removing the existing and new EN added at last SA2 meeting
  Complete solution evaluation and conclusion(s) for each KI
  Send TR for approval to SA plenary in Dec
WI Code | Work Item Title | WP | Target Date | WID#
FS_5GSAT_ARCH | Study on architecture aspects for using satellite access in 5G | 50 > 70% | Dec, 19 | SP-181253

## Slide 32: 2.3) Rel-16 Work and Maintenance (16/19)
Progress since SA#84:
  2 CRs to TS 23.502 and 1 CRs to TS 23.503 agreed.
RAN impacts or dependencies:
  None identified
Next steps:
  maintenance
WI Code | Work Item Title | WP | Target Date | WID#
xBDT | 5GS Transfer of Policies for Background Data Transfer | 0 > 100% | Dec, 19 | SP-180509

## Slide 33: 2.3) Rel-16 Work and Maintenance (17/19)
WI Code | Work Item Title | WP | Target Date | WID#
FS_eIMS5G | Study on Enhanced IMS to 5GC Integration | 70 > 70% | Jun, 19 | SP-180736
eIMS5G_SBA | SBA aspects of enhanced IMS to 5GC integration | 100 > 100% | Jun, 19 | SP-190181
Progress since SA#84:
  Editor’s Note on whether to use new or existing service of UDR to expose HSS Group ID mapping not resolved, LS sent to CT4 to request more context on UDR service and assist resolving issue.
  Maintenance CR’s agreed to clarify HSS service description, consider UPF location for P-CSCF selection, align with eSBA on Group ID mapping by SCP, and remove no longer needed EN.
  RAN impacts and dependencies:
  None.
Next steps:
  Maintenance. Based on Feedback from CT4 address UDR service used for HSS Group ID mapping.

## Slide 34: 2.3) Rel-16 Work and Maintenance (18/19)
WI Code | Work Item Title | WP | Target Date | WID#
IABARC | Architecture enhancements for the support of Integrated access and backhaul (IAB) | 0 > 33% | Dec, 19 | SP-190627
Progress since SA#84:
  General IAB architecture description added to TS 23.501
  Identified list of 5G system enhancements for the support of IAB
  New Rel-16 WID: “Architecture enhancements for the support of Integrated access and backhaul (IABARC)”agreed. Submitted for approval at SA#85 (see SP-190627).
  RAN impacts and dependencies:
  Indication of the IAB capability at RRC layer
  Mobility support for IAB operation
Next steps:
  Close open issues in architecture assumptions
  Create necessary procedure updates for 5GS based on RAN WG agreements
  Create corresponding changes for EPS for the support of IAB according to RAN WG agreements

## Slide 35: 2.3) Rel-16 Work and Maintenance (19/19)
WI | Work Item | WP | CRs approved
TEI16 | Maintenance for pre-Rel-16 features in Rel-16 specs only |  | 46
TEI16 | Rel-16 Cat B/C for alignments with other WG’s work |  | 60

## Slide 36: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Work and Maintenance
  2.3) Rel-16 Work and Maintenance
  2.4) Rel-17 Work
  2.5) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 37: 2.4) Rel-17 Work (1/3)
WI Code | Title | Doc# | Target Date
FS_5GSAT_ARCH | Study on architecture aspects for using satellite access in 5G | SP-181253 | Dec-19
FS_AAI_LTE_NR | Study on Application Awareness Interworking between LTE and NR | SP-190543 | Dec-19
FS_NG_RTC | Study on system architecture for next gen real time communication services | SP-190444 | Mar-20
FS_ID_UAS-SA2 | Study on supporting UAS Connectivity, Identification, and Tracking | SP-181114 | Mar-20
FS_MUSIM | Study on system enablers for multi-USIM devices | SP-190248 | Mar-20
FS_enh_EC | Study on enhancement of support for Edge Computing in 5GC | SP-190185 | Mar-20
FS_SB_SMS | Study on service-based support for SMS in 5GC | SP-190184 | Dec-19
FS_5G_ProSe | Study on system enhancement for Proximity based Services in 5GS | SP-190443 | Jun-20
FS_UPCAS | Study on UPF enhancement for control and SBA | SP-190187 | Mar-20
FS_UUI5 | Study on the Usage of User Identifiers in the 5G System | SP-190450 | Jun-20
FS_eUEPO | Study on enhancement of 5G UE Policy | SP-190449 | Mar-20
Rel-17 Study Items approved at SA#82/83/84:

## Slide 38: 2.4) Rel-17 Work (2/3)
WI Code | Title | Doc# | Target Date
FS_eNA_ph2 | Study on Enablers for Network Automation for 5G - phase 2 | SP-190557 | Mar-20
FS_eNPN | Study on enhanced support of Non-Public Networks | SP-190453 | Mar-20
FS_eATSSS | Study Extended Access Traffic Steering, Switch and Splitting | SP-190558 | Jun-20
FS_eLCS_ph2 | Study on Enhancement to the 5GC LoCation Services - Phase 2 | SP-190452 | Mar-20
FS_5WWC_enh | Study on enhancement of support for 5WWC | SP-190562 | Jun-20
FS_eIMS5G | Study on Enhanced IMS to 5GC Integration | SP-190440 | Mar-20
Rel-17 Study Items approved at SA#82/83/84:
Code | Title | Doc# | Target Date
FLADN | Supporting Flexible Local Area Data Network | SP-190563 | Dec-19
5G_AIS | 5G System Enhancement for Advanced Interactive Services | SP-190564 | Mar-20
Rel-17 Work Items approved at SA#82/83/84:

## Slide 39: 2.4) Rel-17 Work (3/3)
WI Code | Title | Doc# | Target Date
FS_eNS_ph2 | Study on Enhancement of Network Slicing Phase 2 | SP-190628 | Mar-20
FS_MPS | Study on Multimedia Priority Service (MPS) Phase 2, Stage 2 | SP-190629 | Jun-20
FS_IIoT | Study on enhanced support of Industrial IoT - TSC/URLLC enhancements (NOTE 1) | SP-190630 | Mar-20
FS_eV2XARC_ph2 | Study on 3GPP support of advanced V2X services - Phase 2 | SP-190631 | Jun-20
New Rel-17 Study Items for Approval at SA#85:
WI Code | Title | Doc# | Target Date
FS_5MBS | Study on Architectural enhancements for 5G multicast-broadcast services | SP-190625 | Jun-20
FS_5GLAN_enh | Study on enhancement of support for 5G LAN-type service (NOTE 2) | SP-190626 | Mar-20
Revised Rel-17 Study Items for Approval at SA#85:
NOTE 1 : Approved in SA2 with an objection from China Mobile
NOTE 2 : Approved in SA2 with an objection from Qualcomm

## Slide 40: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF and External SDO Normative Reference Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 41: 2.5) IETF and External SDO Normative Reference Update (1/1)
None identified

## Slide 42: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF Dependency Update
3) SA2 Work Planning
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 43: 3) SA2 Work Planning (1/2)
SA2 endorsed work plan proposals (for more details please refer to S2-1908418)
  SA2 Jan 2020 ad-hoc meeting was confirmed as per current schedule (i.e. Jan 13 - 17, 2020)
    Jan 2020 ad-hoc meeting will have full approval power
    Agenda will be published later
  Scheduling constraints makes it difficult to schedule items in parallel
    It was agreed to keep 3 parallel stream but some session with 2 parallel stream
    SA2 work plan will be based on maximum 38 TU/meeting
    3 TU will be reserved as buffer

## Slide 44: 3) SA2 Work Planning (2/3)
Post F2F SA2#134 meeting, an e-mail discussion was held, 9 - 16 July 2019, to finalize the Work Tasks (WT)
  In order to keep WT email discussion manageable only 6 big Rel-17 study items were selected for WT email discussion (i.e. FS_5G_Prose, FS_5MBS, FS_5WWC_Ph2, FS_eNA_Ph2, FS_enh-EC, FS_UUI5).
  Similar WT exercise for other Rel-17 study items is not precluded and may be undertaken at future SA2 meeting.
The following documents were produced at the end of the process -
SA2-TD | Title | TUs estimated as part of SA2 work Plan | Revised TU estimates based on WT exercise
S2-1908637 | Work Tasks for FS_5G_Prose | 17 | 20
S2-1908638 | Work Tasks for FS_5MBS | 16 | 16
S2-1908639 | Work Tasks for FS_5WWC_Ph2 | 10 | 10
S2-1908640 | Work Tasks for FS_eNA_Ph2 | 11 | 14
S2-1908641 | Work Tasks for FS_enh_EC | 10 | 10
S2-1908642 | Work Tasks for FS_UUI5 | 11 | 11

## Slide 45: 3) SA2 Work Planning (3/3)
SA2 work plan was endorsed (for more details please refer to S2-1908590).
Following observation can be made from SA2 Work Plan
  Considerable high Rel-15/Rel-16 maintenance work in Q4, 2019 and Q1, 2020.
  25 Rel-17 study items agreed doesn’t fit in budget.
  Prioritization needed for Rel-17 study items.
Action to SA#85:
  SA#85 is requested to provide SA2 with list of Rel-17 study/work items to be prioritized in Rel-17 timeframe, taking SA2 endorsed work plan into consideration.

## Slide 46: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 47: 4) Documents for Information and Approval (1/3)
TR/TS presentation for Information
  TR 23.737 " Study on architecture aspects for using satellite access in 5G"
TR/TS presentation for Approval
  TS 23.287 "Architecture enhancements for 5G System (5GS) to support Vehicle-to-Everything (V2X) services"

## Slide 48: 4) Documents for Information and Approval (2/3)
Rel-16 WID(s) for Approval
SA-TD | Type | WI Code | Title
SP-190627 | WID NEW | IABARC | Architecture enhancement for the support of IAB

## Slide 49: 4) Documents for Information and Approval (3/3)
Rel-17 WID(s) for Approval
SA-TD | Type | WI Code | Title
SP-190625 | SID REVISED | FS_5MBS | Study on Architectural enhancements for 5G multicast-broadcast services
SP-190626 | SID REVISED | FS_5GLAN_enh | Study on enhancement of support for 5G LAN-type service
SP-190628 | SID NEW | FS_eNS_Ph2 | Study on Enhancement of Network Slicing Phase 2
SP-190629 | SID NEW | FS_MPS2_St2 | Study on Multimedia Priority Service (MPS) Phase 2, Stage 2
SP-190630 | SID NEW | FS_IIoT | Study on enhanced support of Industrial IoT - TSC/URLLC enhancements
SP-190631 | SID NEW | FS_eV2XARC_Ph2 | Study on architecture enhancements for 3GPP support of advanced V2X services - Phase 2

## Slide 50: Contents
1) General aspects (events since SA#84, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 51: 5) Collected Items requiring action from SA
1) Approval of provided TR/TSs (please see slide 47)
2) Approval of new/revised WIDs (please see slide 48, 49)
3) Provide SA2 with list of Rel-17 study/work items to be prioritized in Rel-17 timeframe, taking SA2 endorsed work plan into consideration (please see slide 45)

## Slide 52
Thank You!