## Slide 1: Motivation of Passive IoT
China Mobile, Spreadtrum Communications, Huawei
Notes: 1

## Slide 2
Two Categories of Use Cases for Passive IoT
Pre-stored data report (e.g., Automated asset management)
Small size, ultra-low cost, and batteryless device is required in most cases for automated real-time inventory and tracking of objects for asset management. Typical industries include:
Manufacturing
Logistics and warehousing
Current practice: Barcode on paper for inventory and tracking
    Passive IoT tag
    Automatic remote reading
    Hundred times faster reading
Printer
Printed barcode on various parcels
    Barcode
    Handheld LOS scanning (labor intensive)
    Slow one-by-one scanning (time consuming)
Battery-operated
Cost for batteries and replacement
Device size impacted by battery
Infrequent transmissions for battery life
Environmental issue (Lithium, lead, etc.)
An industrial wireless sensor network in a cement factory
Real-time data report (e.g., Sustainable sensor network)
Wireless sensor without battery during lifetime is required for remote environment and object status monitoring. Typical industries include:
Manufacturing
Agriculture and livestock farming
Energy-harvesting
Self-sustainability
Miniaturized device
No limits on transmission period
Eco-friendly (Ambient energy)
Batteryless device during lifetime is the essential requirement.

## Slide 3
Use Cases #1: Automated Asset Management in Factories
We have considered RFID technology, but RFID is not good.
Bad performance: Based on our test, RFID can only read labels in case the labels are not blocked. On the other words, in case the label attached on the bin is blocked, e.g. by another metal bin, RFID always fail to read it.
High Cost: The transmission distance for RFID readers is short, about 8 meters based on test. We need to deploy a lot of RFID readers to cover the whole warehouse(about 5000m2) and the network cost is very high.
Bin management at the Gate of the warehouse
Identify which bins move in or out of the warehouse, at the Gate of the warehouse.
Bin management inside the warehouse
RWS-210350 Requirements to URLLC, positioning and perception for automotive industry, China Mobile & BMW Brilliance Automotive, 3GPP R18 WS
Key requirements :
low cost batteryless device
sufficient link budget for appropriate deployment
unique identify the bins for logistic management.
Currently, bins are manually managed via scanning the barcode attached on each bin.
Problem：
High OPEX: OPEX of warehouse management is very high for us
Manual error: Manual work often cause errors and many bins lost
We are considering Automatic bin Management in the warehouse with a quite low cost.
Current Practice
Potential RFID technology

## Slide 4
Use Cases #2: Automated Asset Management in Outdoor Warehouse
Key requirements:
1. low cost batteryless device to avoid high-voltage breakdown
2. sufficient link budget for outdoor deployment
Currently, RFID tags are pasted on each equipment and cable for asset management
Problem： Inventory is done by scanning the RFID tags one by one within short range
High OPEX: OPEX is high for manual scanning is needed
Not realtime: it takes long time to scanning the tags one by one. Additionally, as real time inventory is unable to be reached, asset lose cannot be warned in time
Current Practice
Equipment/Cables management outdoor
Identify the equipment/cables in outdoor warehouse
For power grid companies, there are plenty of equipment and cables stored in their outdoor warehouses (usually a few thousand square meters)

## Slide 5
Use Cases #3: Sustainable Sensor Network for Agriculture
Sensors are widely deployed in digital farm to monitor environments, crops state, and equipment state
  Environments
    light intensity, CO2 concentration, soil acidity
  Crops state
    size of fruit, temperature, humidity
  Equipment state
    working ours, power consumption
Real time information is important to adjust planting mode in time
  Existing cellular IoT devices will suffer from battery life of no larger than one year with reporting period of a few minutes
  It is not realistic to replace batteries of thousands of sensors scattered throughout farms every year
  No battery is preferred
Key requirements for Passive IoT:
low cost batteryless device
sufficient link budget for outdoor deployment

## Slide 6
Existing batteryless technology-RFID
[1] A -21.2dBm Dual-Channel UHF Passive CMOS RFID Tag Design
Reader
RFID APP Server
RFID Tag
RF Energy harvesting
Based on the order from RFID APP Server, a Reader wirelessly interacts with the RFID Tag to inventory/read/write the tag and return the information.
General architecture of RFID
How RFID works batteryless?
RFID tag is capable of harvesting energy for communication from RF(Radio Frequency) emitted by Reader
Coverage of a commercial RFID reader is only around or less than 10 meters in practical
Problem of RFID
  Some of the reasons:
  Power restriction: according to the regulations of specific UHF band for RFID, EIRP of downlink signals should not exceed 36dBm
  Interference between readers: reduces the coverage of each reader significantly [1]
[1] INTERFERENCE ANALYSIS OF UHF RFID SYSTEMS, Progress In Electromagnetics Research B, Vol. 4, 2008

## Slide 7
Requirements on Passive IoT for the Target Use Cases
Ultra low power device
  Power consumption low enough to work with energy harvesting (1~100uW)
  Harvest energy from Radio frequency or Solar.
Ultra low cost device
  For automated asset management, cost no significant increase compared with barcode printed on heat sensitive paper (~0.01$)
  For sustainable sensor network, cost comparable with sensor (~0.5$)
Coverage and networking match the deployed cellular network
  Indoor deployment: small cell with distance of 20~30 meters between neighboring pico remote radio units
  Outdoor deployment: micro cell with distance of 200~300 meters between neighboring base stations
  Interference management for adaptive networking
  Network Architecture to manage the Passive IoT tags
LPWAN
Passive IoT
Power
Cost
0.01~0.5$
>1$
1~100uW
>10mW
Requirements on device
Passive IoT targets at new IoT markets lower-end than all the existing cellular technologies, which require batteryless device for low maintenance cost
Energy source | Size | Availability | Power density | Conversion efficiency
Solar | Good | Fair | 15~100mW/cm2 | 10~20%
Artificial Light |  |  | 10~100uW/cm2 | 
Airflow | Poor | Good | 100mW/cm2 | -
Motion | Fair | Fair | 200uW/cm2 | ~10%
Thermal | Good | Poor | ~50uW/cm2 | 3%
Radio frequency | Fair | Good | 1~10uW/cm2 | < 20%
Typical energy sources for energy harvesting [1][2]
[1] Internet of Hybrid Energy Harvesting Things, IEEE INTERNET OF THINGS JOURNAL, VOL. 5, NO. 2, 2018
[2] Energy Harvesting Sensor Nodes - Survey and Implications, IEEE COMMUNICATIONS SURVEYS & TUTORIALS, VOL. 13, NO. 3, 2011

## Slide 8
Passive IoT Tag
5GC
Passive IoT Server
NR
RAN Group
Motivation: develop the air technology to support the batteryless IoT device.
Work scope:
Downlink coding and modulation
Uplink coding and modulation scheme supporting backscatter transmission
Frame structure and synchronization scheme
Minimized protocol stack
Coexistence with existing cellular technologies in licensed spectrum
SA2 Group
Motivation: develop the network architecture to support batteryless IoT device and enable the business.
Work scope:
-Study the general architecture for supporting Passive IoT in 5G system.
  Note 1: Passive IoT device connecting to the NG-RAN or UE can be considered.
-Study how to manage the Passive IoT device, including, e.g.:
Whether and how Passive IoT device registered to 5GC;
Whether and how to manage the CM states for the Passive IoT device;
Policy enhancement to manage the Passive IoT device.
-Study how to manage the connectivity for the Passive IoT device, including, e.g.:
Establish the connectivity for the Passive IoT device for data transmission;
QoS handling for the Passive IoT device data transmission;
Policy enhancement to manage the connectivity for Passive IoT device.
-Study how to support the mobility for Passive IoT device.
  Note 2: Gap analysis with the existing 5G system should be studied.
  Note 3: This SA2 study item has dependency to RAN and will start the study in case that the related RAN study is approved in RAN.
Standard work on Passive IoT

## Slide 9
Thanks!