## Slide 1: On the SA6 study item proposal on Service Function Chaining (SP-211559)
3GPP
SP-211565

## Slide 2: Background
Based on SA1 requirement on Service Function Chaining (SFC), SA2 has approved the SA2 SID (S2-2108160) that is subject to prioritization in SA#94-e.
A companion SA6 SID proposal (S6-212737) was objected from one company on the ground that there is “lack of requirements”.
In the subsequent slides, we illustrate that the SA1 requirements for SFC can be approached with two different architecture models that can be considered both in SA2 and SA6.

## Slide 3: About SFC status
SA1 Requirements (TS 22.261 Sec. 6.35.2/3)
  Service function chaining shall support deployments where the Hosted Services are provided by the operator and deployments where the Hosted Services are provided by a third party.
  The service function management shall be able to manage service function chaining for deployments where the Hosted Services are provided by the operator and for deployments where the Hosted Services are provided by a third party.
Excerpts form SA2 SID (S2-2108160)
  Consider different SFC deployments for the 5G network (in Edge Hosting Environment and central location on N6) and investigate the potential required coordination for SFC processing in these SFC deployments.
  NOTE: This study considers only traffic handled over N6 by PSA UPF(s) in 5G network.
Excerpts from proposed SA6 SID (S6-212737)
  The feasibility of using one or more EAS(es) as a chain of service functions,
  The new interfaces, APIs, and/or enhancement of Edge Enabling Layer for handling the chain of service functions for an application at EDN,
The following slides illustrate two different SFC architecture approaches that can be considered by SA2 and SA6 respectively.

## Slide 4
Edge Application
Server (EAS)
SF1
SF2
SFC in
5GC network
SFP1
SFP2
3GPP
Network
Edge Data Network
Edge Enabler
Server (EES)
N6*
N33
SF1
SF2
SF3
SF4
SF5
SFC
Controller
SFP-1
SFP-2
Traffic Classifier
N33
SA2 Scope: SFC in 5GC

## Slide 5
Edge Application
Server (EAS)
SF1
SF2
SFC in
Edge network
SFP1
SFP2
EDGE-X
3GPP
Network
Edge Data Network
EDGE-Y
Edge Enabler
Server (EES)
EDGE-7
EDGE-2
EDGE-7
Edge SFC Enabler
SF1
SF2
SF3
SF4
SF5
SFC
Controller
SFP-1
SFP-2
Traffic Classifier
EDGE-X
EDGE-Y
SA6 Scope: SFC in EDN

## Slide 6: Proposal
Based on the discussion in the previous slides, it is proposed to approve the SA6 SID proposal SP-211559

## Slide 8: SA6 SFC study (SP-211559/S6-212737) objectives
Study and identify the application architecture requirements to enable the support of service functions and service function chains in the Edge Data Network and Cloud Data Network.
Analyze requirements as identified in (1) and study whether that places requirements on existing EDGEAPP architecture and EEL. For example:
  the feasibility of using one or more EAS(es) as a chain of service functions,
  the new interfaces, APIs, and/or enhancement of Edge Enabling Layer for handling the chain of service functions for an application at EDN,
  the handling of SFC at an EDN for an application of a hosting UE when the UE moves with the change of EDN operated by the same or different operators,
  Identify key issues and solutions in the EDGEAPP architecture and/or EEL.
Coordinate with SA2 WG related to the potential new north bound APIs over N33 for providing information, e.g., to steer the traffic of an application towards the required SFC at EDN or cloud data network.
Note: Further coordination may be required to avoid any overlap between SA2 and SA6.