## Slide 1: Philips (health vertical) views on release 19
Walter Dees
Philips International B.V.

## Slide 2: Outline
Wide range of features in 5G and 5G advanced of interest to health domain.

## Slide 3: Overall View on Rel-19 Content
NO | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Integrated Sensing & Communications (See slide 7 for more details) | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment using NR RF signals. Key Work Tasks include defining: Architecture and function enhancement to support new sensing service within 5GS. E2E procedures for sensing service exposure, discovery, selection and coordination of the sensing entities, authorization, sensing control parameter generation and provisioning, handling and processing of sensing data, service continuity, additional privacy control. Integration with location services for combined and more accurate position estimation. | Yes, TR 22.837 | SA2 | Yes, Major | SA3 for security, SA5 for charging
2 | Ambient IoT (See slide 8 for more details) | 5G system support for Ambient IoT, i.e. IoT devices powered by energy harvesting, being either battery-less or with limited energy storage capability. An ambient IoT device has low complexity, small size and lower capabilities and lower power consumption than previously defined 3GPP IoT devices. Key Work Tasks include defining: Architecture and function enhancement for supporting Ambient IoT within 5GS. E2E procedures for device identification, connection management (incl. connectionless communication, triggering), service exposure, managing and controlling a UE or a RAN node for communication with Ambient IoT device(s), authorization and policy control, QoS, mobility management, positioning of Ambient IoT devices. Simplified protocol stack and simplified procedures and features for Ambient IoT device(s). | Yes, TR 22.840 | SA2 | Yes, Major | SA3 for security, SA5 for charging

## Slide 4: Overall View on Rel-19 Content
NO | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Mobile metaverse services and other XR/IMS related enhancements (See slide 9 for more details) | 5G system support for mobile metaverse services and other enhanced XR/IMS related capabilities. NOTE: whether or not this is done in a single SI/WI or split over multiple (e.g. phase 2 of XRM and NG_RTC) is to be decided. Key Work Tasks include defining: Architecture and function enhancement to support Metaverse services E2E procedures for IMS communication enhancements for Metaverse, such as synchronization of multiple streams from multiple (remote and local) UEs, digital asset and avatar representation in IMS communication, support for transcoding of different avatar representations, distributed rendering enhancements E2E procedures for general XR related enhancements, such as digital identity/asset management and authorization, control of avatar representation for metaverse services, end-to-end QoS control, enhanced support for multi-modality services. | Yes, TR 22.856 | SA2 | Yes, Minor | SA3 for security
4 | Ranging phase 2 (See slide 10 for more details) | 5G system support for enhanced ranging/sidelink positioning. Key Work Tasks include defining: Defining architecture, function and procedure enhancements to enable: NI-LR procedure and related IMS updates for accurate positioning during emergency calls using ranging (e.g. for ProSe Remote UEs). NPN support for ranging (NOTE: may depend on further ProSe enhancements (see next slide)) Inter-PLMN ranging. Support for restricted discovery (using DDNMF). Enhanced privacy profile handling for ranging (if not done in release 18). | See TS 22.261 | SA2 | Yes, Minor | SA3 for security

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | 5G ProSe phase 3 (See slide 10 for more details) | 5G system support for further enhanced 5G ProSe services. Key Work Tasks include defining: Defining architecture, function and procedure enhancements to enable: NPN support for ProSe Multi-path via different U2N relays Multi-hop U2N relay Group mobility for U2N relay Non-3GPP support for ProSe Precise clock synchronization/TSN for ProSe Sidelink for Industrial Communication | See TS 22.261 | SA2 | Yes, Major | SA3 for security
6 | Enhancement of user identifiers in the 5G System and improved integration of non-3GPP devices (See slide 11 for more details) | 5G system support for enhanced usage of user identifiers in the 5G system, e.g. to identify individual human users on a shared UE or to identify an individual non-3GPP device (without SUPI) behind a gateway. Key Work Tasks include defining: Architecture and function enhancement to support enhanced usage of user identifiers E2E procedures for linking user identifiers with 3GPP subscriptions, improved identification and authentication of individual users and of individual non-3GPP devices behind gateway, improved QoS and policy control for individual users and for individual non-3GPP devices behind gateway. NOTE: identifying non-3GPP devices may overlap with 5WWC work identified for R19. | TR 22.904 TS 22.101 (clause 26a) TS 22.115 (clause 5.2.17) | SA2 | No | SA2 for security, SA5 for charging.

## Slide 6: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
7 | Miscellaneous | Various other small improvements to the 5G system mentioned in work tasks of various study/work items or that are unmet in release 17 and 18. Key Work Tasks include defining: Further enhancements for NTN IoT communication (e.g. store and forward) 3GPP RAT based positioning using NTN Dual steer connectivity via PLMN and SNPN Interconnect of SNPNs Control Plane-based provisioning of NPN credentials Finegrained geofencing for accessing localized networks Enabling timing delivery as a service for NB-IoT and eMTC Lightweight Access Aggregation and Steering of Wi-Fi in 5GC | TS 22.261 | SA2 | Depends | SA3 for security

## Slide 7: 5GS support for wireless sensing
Unobtrusive way to perform e.g. activity monitoring & fall detection of elderly, incl. cases when people don’t carry a UE.
Wider coverage area than Wi-Fi sensing, incl. service continuity outside of home.
Improved location estimation by combining UE location and sensing.
Requires handling and processing of sensing data in 5G System, coordination and handovers between sensing transmitters and receivers, additional authorization and privacy control, exposure to 3rd parties, etc.

## Slide 8: 5GS support for ambient IoT
Ambient IoT = Ultra low power IoT  NB-IoT and LTE-M still too high energy consumption and peak power requirements.
Very useful for body-worn sensors, asset/patient tracking and inventory management, given the limited space for a good battery and (logistical) difficulties for recharging.
Requires 5GS to support irregular traffic patterns, connection less communication, device triggering and identification, reduced complexity protocols and possibly new positioning methods.

## Slide 9: 5GS support for metaverse services
Enables new ways of communication and new levels of immersiveness.
AR/VR Telepresence: improves collaboration and enables remote consultation and remote intervention.
Requires 5GS to support synchronization of multiple streams from multiple remote and local UEs, digital asset and avatar representation in IMS communication, support for transcoding of different avatar representations, distributed rendering enhancements, end-to-end QoS control, enhanced support for multi-modality services, etc.
Whether or not this is done in a single SI/WI or split over multiple (e.g. phase 2 of XRM and NG_RTC) is to be decided.

## Slide 10: Ranging phase 2
Ranging important enabler for more accurate positioning and for positioning in challenging coverage situations.
Important features not yet supported:
  NI-LR procedure for ranging during emergency call (e.g. for positioning of Remote UE making emergency call).
  NPN support for ranging (NOTE: may depend on further ProSe enhancements (see next slide)).
  Inter-PLMN ranging.
  Support for restricted discovery (using DDNMF).
  Enhanced privacy profile handling for ranging (if not done in release 18).
Accurate cellular positioning with ranging
Location Service
3rd party app
ranging
Indoor / out-of-coverage wayfinding

## Slide 11: 5G ProSe phase 3
5G ProSe important enabler for providing communication in challenging coverage situations.
Important features not yet supported:
  NPN support for 5G ProSe
  Non-3GPP support for 5G ProSe
  Multi-path via different U2N relays
  Multi-hop U2N relay
  Group mobility for U2N relay
  Precise clock synchronization/TSN
  Sidelink for Industrial Communication

## Slide 12: Enhancement of user identifiers in the 5G System and improved integration of non-3GPP devices
Granularity of using UE identifiers as identification of users and devices is insufficient. Multiple users may share same UE. Also, not all devices may have SUPI (e.g. non-3GPP devices connected to a gateway UE). Important to address this.
5GC could act as user identity provider to external services. SA1 has studied and created requirements for this (e.g. TR 22.904, TS 22.101 (clause 26a), TS 22.115 (clause 5.2.17)), but SA2 has not yet picked this up.
Requires 5GS architecture, function and procedure enhancements for linking user identifiers with 3GPP subscriptions, improved identification, authentication, QoS and policy control of individual users and individual non-3GPP devices behind gateway, rather than doing this only per UE.
NOTE: identifying non-3GPP devices behind gateway may overlap with potential 5WWC work identified for release 19.
Mapping users to devices
5GC

## Slide 13: Summary
As Philips, we think it is important in release 19 to work on:
Integrated sensing and communication
Ambient IoT
Mobile metaverse services and other XR/IMS related enhancements
Ranging phase 2
5G ProSe phase 3
Enhancement of user identifiers in the 5G System and improved integration of non-3GPP devices
Several other miscellaneous enhancements:
  Further enhancements for NTN IoT communication (e.g. store and forward)
  3GPP RAT based positioning using NTN
  Dual steer connectivity via PLMN and SNPN
  Interconnect of SNPNs
  Control Plane-based provisioning of NPN credentials
  Finegrained geofencing for accessing localized networks
  Enabling timing delivery as a service for NB-IoT and eMTC
  Lightweight Access Aggregation and Steering of Wi-Fi in 5GC