## Slide 1: Discussion on KPI consolidation
Huawei
S1-231195

## Slide 2: Use cases for FS_Sensing
Clause | use cases | KPI table
5.1 | Use case of intruder detection in smart home | Yes
5.2 | Use case on pedestrian/animal intrusion detection on a highway | Yes
5.3 | Use case on rainfall monitoring | Yes
5.4 | Use Case on Transparent Sensing Use Case | No
5.5 | Use case on sensing for flooding in smart cities | Yes
5.6 | Use case on intruder detection in surroundings of smart home | Yes
5.7 | Use case on sensing for railway intrusion detection | Yes
5.8 | Use Case on Sensing Assisted Automotive Maneuvering and Navigation | No
5.9 | Use case on AGV detection and tracking in factories | The KPIs for this use case are FFS.
5.10 | Use case on UAV flight trajectory tracing | Yes
5.11 | Use case on sensing at crossroads with/without obstacle | Yes
5.12 | Network assisted sensing to avoid UAV collision | Yes
5.13. | Use case on sensing for UAV intrusion detection | Yes
5.14 | Use case on sensing for tourist spot traffic management | Yes
5.15 | Use case on contactless sleep monitoring service | Yes
5.16 | Use case on Protection of Sensing Information | No
5.17 | Use case on health monitoring at home | No
5.18 | Use case on service continuity of unobtrusive health monitoring. | No
5.19 | Use case on Sensor Groups | No
5.20 | Use case of Sensing for Parking Space Determination | Yes
5.21 | Use case of Seamless XR streaming | No
5.22 | Use case of UAVs/vehicles/pedestrians detection near Smart Grid equipment | Yes
5.23 | AMR collision avoidance in smart factories | Yes
5.24 | Use case on roaming for sensing service of sports monitoring | Yes
5.25 | Use Case on immersive experience based on sensing | Yes
5.26 | Use case on accurate sensing for automotive maneuvering and navigation service | No
5.27 | Use case public safety search and rescue or apprehend | Yes
5.28 | Use case on Vehicles Sensing for ADAS | Yes
5.29 | Use case on Gesture Recognition for Application Navigation and Immersive Interaction | Yes
5.30 | Use case on sensing for automotive maneuvering and navigation service when not served by RAN | No
5.31 | Use case on blind spot detection | No
5.32 | Use case of integrated sensing and positioning in factory hall | Yes

## Slide 3: Discussion on KPI consolidation
Option#1: a single KPI table which lists all the KPI values of use cases.
  It is a very straight forward way to consolidate the KPI.
  The KPI values in the table may be very range.
Option#2: several separate KPI tables. Each table is for each category of the vertical market, such like smart transportation, smart city.
  It would become efficient to consolidate the KPI table within each category.
  This document provides a initial proposal of methodology of how to consolidate existing sensing KPI.
It is up to SA1 team which option is preferred. This DP just provides a overview.

## Slide 4: Option 1: KPI consolidation
Scenario | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
Intruder detection in smart home | Indoor | 95 | ≤10 | ≤10 | N/A | N/A | N/A | N/A | <1000 | < 1 | < 5 | < 2
Pedestrian/animal intrusion detection on a highway | Outdoor (Highway) | 95 | ≤1 | N/A | N/A | N/A | N/A | N/A | ≤5000 | ≤ 0.1 | ≤5 | ≤5
Rainfall monitoring | outdoor | 95 | [1mm/h] | N/A | N/A | N/A | N/A | N/A | N/A | 1 min | 10min, application configurable | 5
sensing for flooding in smart cities | Outdoor | 95 | ≤10 | [≤0.2] | N/A | N/A | N/A | N/A | ≤ 1min | < 1min | < 0.1 | < 3
intruder detection in surroundings of smart home | Outdoor | 95 | ≤2 | N/A | N/A | N/A | N/A | N/A | ≤1000 | < 1 | < 0.1 | < 5
Intrusion detection on a railway | Outdoor (Along railway) | 95 | ≤1.5 | N/A | N/A | N/A | N/A | N/A | ˂1500 | ≤ 0.1 | 2 | 2
UAV flight trajectory tracing | Outdoor | N/A | N/A | N/A | N/A | N/A | 1m x 1m ~10m x 10m | 1m/s x 1m/s ~ 10m/s x 10m/s | 100~1000 | 1Hz | 5 | 5
Sensing at crossroads with/without obstacle | Outdoor | 95 | ≤1 | N/A | N/A | N/A | N/A | N/A | ≤100 | ≤ 0.1 | ≤5 | ≤5
Network assisted sensing to avoid UAV collision | Outdoor | [99] | 1 | N/A | 1 | N/A | <1 | 1 | 500 | 0.5 | N/A | N/A
……. | ……. | ……. | ……. | ……. | ……. | ……. | ……. | ……. | ……. | ……. | ……. | …….
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  | 
Note: not all KPI values are included in the above table due to limited space. .
5.1
5.2
5.3
5.5
5.6
5.7
5.10
5.11
5.12

## Slide 5: Option2: Categories of use cases with KPI table
Smart transportation
Low-altitude UAV
5.12 Network assisted sensing to avoid UAV collision
5.13 Use case on sensing for UAV intrusion detection
5.2 Use case on pedestrian/animal intrusion detection on a highway
5.7 Use case on sensing for railway intrusion detection
5.11 Use case on sensing at crossroads with/without obstacle
5.14 Use case on sensing for tourist spot traffic management
5.20 Use case of Sensing for Parking Space Determination
5.28 Use case on Vehicles Sensing for ADAS
Smart life
Smart factory
5.1 Use case of intruder detection in smart home
5.6 Use case on intruder detection in surroundings of smart home
5.15 Use case on contactless sleep monitoring service
5.24 Use case on roaming for sensing service of sports monitoring
5.25 Use Case on immersive experience based on sensing
5.29 Use case on Gesture Recognition for Application Navigation and Immersive Interaction
5.3 Use case on rainfall monitoring
5.5 Use case on sensing for flooding in smart cities
5.22 Use case of UAVs/vehicles/pedestrians detection near Smart Grid equipment
5.27 Use case public safety search and rescue or apprehend
Smart city
5.23 AMR collision avoidance in smart factories
5.32 Use case of integrated sensing and positioning in factory hall
Indoor
Outdoor

## Slide 6: Sensing KPI for smart transportation
Scenario | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
Pedestrian/animal intrusion detection on a highway | Outdoor (Highway) | 95 | ≤1 | N/A | N/A | N/A | N/A | N/A | ≤5000 | ≤ 0.1 | ≤5 | ≤5
Intrusion detection on a railway | Outdoor (Along railway) | 95 | ≤1.5 | N/A | N/A | N/A | N/A | N/A | ˂1500 | ≤ 0.1 | 2 | 2
Sensing at crossroads with/without obstacle | Outdoor | 95 | ≤1 | N/A | N/A | N/A | N/A | N/A | ≤100 | ≤ 0.1 | ≤5 | ≤5
Tourist spot traffic management | Outdoor | 95 | [≤2] | N/A | N/A | N/A | [1] | [1] | [≤5000] | [≤0.2] | ≤5 | ≤5
Parking space determination | Indoor/ outdoor | 95 | 0.5 | 0.5 | 0.1 | N/A | 2.5m perpendicular to the parking space 5m parallel to the parking space | N/A | 1000 | 1 | 1 | 5
ADAS [long range Radar] | TBD | [95] | ~[0.1]-[1.3] | TBD | [±0.03] -[±0.12] m/s | N/A | [0.4] | [0.1] –[0.6] | [50] | [0.05] -[0.2] | [1-10]% | [<1]%
ADAS [Short range Radar] | TBD | [95] | ~[0.02]-[2.6] | TBD | [±0.03] -[±0.12] m/s | N/A | [0.4] | [0.1] –[0.6] | [20] | [0.02] –[0.05] | [1-10]% | [<1]%
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Sensing KPI for low-altitude UAV
Scenario |  | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
Network assisted sensing to avoid UAV collision |  | Outdoor | [99] | 1 | N/A | 1 (NOTE 2) | N/A | <1 | 1 | 500 | 0.5 | N/A | N/A
UAV intrusion detection | Level 1 | Outdoor | 95 | ≤10 | ≤10 | N/A | N/A | 10 | [5] | [≤1000] | [≤1] | ≤5 | ≤5
 | Levle2 | Outdoor | 95 | ≤5 | ≤5 | N/A | N/A | 10 | [5] | [≤1000] | [≤1] | ≤5 | ≤5
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: Sensing KPI for smart home
Scenario | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
Intruder detection in smart home | Indoor | 95 | ≤10 | ≤10 | N/A | N/A | N/A | N/A | <1000 | < 1 | < 5 | < 2
intruder detection in surroundings of smart home | Outdoor | 95 | ≤2 | N/A | N/A | N/A | N/A | N/A | ≤1000 | < 1 | < 0.1 | < 5
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: Sensing KPI for smart life
Scenario | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
Sleep monitoring | Outdoor (bedroom) | 95 | 2 times/min [0.033Hz] (NOTE 2) | N/A | N/A | N/A | N/A | N/A | N/A | 60s | 60 | 5 (NOTE3)
Sports monitoring | Indoor (living room) | 95 | 3 times/min [0.05Hz] (NOTE 2) 4 times/min [0.07Hz] (NOTE 3) | N/A | N/A | N/A | N/A | N/A | N/A | 60s | 1min | N/A
Immersiveexperience | Indoor | 95 | 0.5 | 0.5 | 0.1 | N/A | 0.5 | N/A | 250 (granularity of field is 1.5m x 1.5m) | 0.25 | 5 | 5
Gesture recognition | Indoor | N/A | N/A | FFS | FFS | 0.1 | 0.1 | FFS | [0.3] | FFS | ≤0.1 | FFS
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Sensing KPI for smart city
Scenario | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
Rainfall monitoring | outdoor | 95 | [1mm/h] NOTE 2 | N/A | N/A | N/A | N/A | N/A | N/A | 1 min | 10min, application configurable | 5
sensing for flooding in smart cities | Outdoor | 95 | ≤10 | [≤0.2] NOTE 2 | N/A | N/A | N/A | N/A | ≤ 1min NOTE 3 | < 1min NOTE 3 | < 0.1 | < 3
Sensing for the use case in Smart Grid (NOTE 2) | Outdoor | 95 | ≤0.7 | N/A | UAV: ≤25 Pedestrian: ≤1.5 Vehicle: ≤15 | N/A | N/A | N/A | ≤5s | ≥10Hz | [≤5] | [≤5]
Search and Rescue/Apprehend | Outdoor/Indoor | 99 | ≤ 0.5 | ≤ 1.0 | Pedestrian: ≤1.5 | Pedestrian: ≤1.5 | 3 | Horiz: 5 Vert: 5 | ≤1s | ≥10Hz | [≤3] | [≤3]
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: Sensing KPI for smart factory
Scenario | Sensing service area | Confidence level [%] | Accuracy of positioning estimate by sensing (for a target confidence level) |  | Accuracy of velocity estimate by sensing (for a target confidence level) |  | Sensing resolution |  | Max sensing service latency [ms] | Refreshing rate [s] | Missed detection [%] | False alarm [%]
 |  |  | Horizontal [m] | Vertical [m] | Horizontal [m/s] | Vertical [m/s] | Range resolution [m] | Velocity resolution (horizontal/ vertical) [m/s x m/s] |  |  |  | 
AMR collision avoidance in smart factories | 100m | 99 | ≤1 | N/A | 1 | N/A | 1 | 10 | ˂500 | ≥20Hz | N/A | 5
Indoor Factory | 100 m2 | 99 | [≤0.5] | N/A | 0.5 | N/A | [0.5] | [0.5] | ≤100 | 0.1 | N/A | N/A
NOTE: FFS |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 12
Thank you