## Slide 1: SA1 pre#110 call – AI Agent session
Answers to posed Questions on AI Agents in 6G
Xiaomi
S1-252038

## Slide 2: 4 questions were provided ahead of the call
  What is meant by "intent" , how does it relate to "AI agent" and what's the difference compare to SA5 definition?
  What service AI agent could provide within 3GPP network?
  What's the impact on network if AI agent is introduced?
  Which new type of service /use case can be performed by an AI Agent compared with traditional AI model/algorithm e.g. in the NWDAF

## Slide 3
What is meant by "intent" , how does it relate to "AI agent" and what's the difference compare to SA5 definition?
In this case (and in general for TR22.870) the requirement in 6.5.6 for a 6G network to be able to “expose its services … by intent” is unclear and potentially inaccurate based on industry definition of terms.
The “Intent” step in AI processing is the interpretation of the original user query, after feature extraction for use in routing the query and potentially final formatting of the Feature Extraction before inputting to the appropriate AI Model for the query.
Additionally, AI services including AI Agents may be connected together in order to provide solutions and manage processes through collaboration or combination (e.g. in various architectures) via inter connecting nodes or through use of dedicated protocols such as A2A or MCP. As such the message structure for data transferred between AI services or AI Agents is standardised as are the services offered by the destination AI Agents.
In the context of the exposure of services it is simply clearer to remove reference of intent.
SA5 makes reference to “intent” in use by management services to select AI/ML models with suitable capabilities to fulfil the “intent”. [TS 28.105] This is consistent with the above
https://developers.googleblog.com/en/a2a-a-new-era-of-agent-interoperability/
https://www.anthropic.com/news/model-context-protocol
What service AI agent could provide within 3GPP network?
AI Agents represent one way of providing AI services. Agentic AI and AI Agents are alternatives of autonomous AI solutions but other dedicated AI service flows can also be considered to deliver AI services.
AI Agents offer particular advantages through autonomy, and ability to learn and adapt over time and through interaction with other systems/tools, use of local memory such as short term or long term memory
AI Agents are gaining wide industry adoption and enhancements for interconnection and discovery to other tools and AI Agent through new protocols e.g. MCP and A2A. Which equipped with reliable and secure protocols can enable higher degrees of collaboration and scalability between AI Agents and tools.
AI Agents can by way of engineered AI Agent teams be used inside of 3GPP networks (e.g. a specialized domain) to manage particular services or simply to enable access through use of secure protocols e.g. MCP to network data to authorized third parties. Implementations adopting teams of AI Agents can facilitate structured management and control on data utilization e.g. policy and access control, QoS control, service reliability.
E.g. AI Agents acting as security verification services within a network enabling access to other databases or data repositories within a network, or AI Agents enabling network operators to utilise third party providers to supply authorized optimisation operation strategies or AI Agents to provide enhanced routing schemes e.g. enhanced computing resource management, or AI Agents to parse data to recognised/required regulatory requirements through interaction with regulatory AI Agents.

## Slide 4
What's the impact on network if AI agent is introduced?
Optimised data management and control of access. AI specific (not only for AI Agents) protocol client/server implementations and new AI Agent management and coordination function may be necessary e.g. potentially conforming to industry standard open interfaces. (e.g. supporting O-RAN)
When designed and implemented correctly and integrated with necessary security protocols (e.g. within AI protocols such as MCP and A2A) risk can be controlled and managed.
Which new type of service /use case can be performed by an AI Agent compared with traditional AI model/algorithm e.g. in the NWDAF
Potentially most existing functions can be supported
Since AI Agents offer another way for AI services and functions to be adopted which enable faster updates based on learning from existing tasks.
Note AI Agents may not always be the optimal solution since they have inherent memory and latency aspects that may impact performance targets. However through good AI service implementation and AI architecture and workflows there can be some mitigation of these impacts. E.g. aspects such as message error handling may not be best enhanced by AI Agents.
Use of AI Agents with small specific tasks, teams of AI Agents can be supported in larger teams or “swarms” to collaborate and implement specific tasks. E.g. architectures and AI Agents with specific functionalities to maintain security, monitoring of activity, regulatory compliance, etc. can be supported
Implementation of AI Agent teams does not exclude the requirement for human intervention, which can be programmed in to specific AI Agents based on specific triggers. Continuous monitoring and audit recording can also be supported.
New services and functions that AI Agents can facilitate include structured AI Agent related management and control and enhanced data handling e.g. group management including for new AI Agent services offered by networks, policy and access control, QoS control, service reliability.
AI Agents may also act as security verification services within a network enabling access to other databases or data repositories within a network. Additionally AI Agents could be used to parse data to recognised/required regulatory requirements or enable authorized 3rd party AI Agents to provide optimized services including network operation.