## Slide 1: Discussion on Core Network Type Selection based on the Subscription Information
NTT DOCOMO
Vodafone?
Telecom Italia?
China Mobile?
Verizon?
Deutsche Telekom?
S2-133909
TSG SA WG2 #100
San Francisco, USA, 11-15 November 2013

## Slide 2: Motivation
Strong merits to divide networks into a conventional and specific types of networks (in long-term), such as roaming users accommodation, MTC network separation, etc.
  There is little influence on normal users if the overload is caused in other type of network.
  It is possible to construct a simple network appropriate to service characteristics with low cost.
Also useful for Pre-Rel-10 UEs which do NOT support LAPI for routing them to an appropriate networks.
  It is quite inefficient to add new functions to existing UEs because they have already been in widespread use.
A solution, which relies on a new subscription information to perform a network selection, is required for specific groups of UEs to distinguish conventional and specific type of network to attach.

## Slide 3: Solution Requirement
No impact on UEs.
  Should work with existing pre-Release 10 UEs.
  Should work also with Rel-10 UEs

## Slide 4: Problems to be Solved
Problem #1: How is the CN network type indication stored in the subscription?
Problem #2: How to direct the UE to MME of the appropriate overlay network?

## Slide 5: Solution for Problem #1: Indication of CN Overlay Network
Problem #1: How is the CN network type indication stored in the subscription?

## Slide 6: Indication of CN Overlay
PLMN-ID Solution will not work for Docomo.
  Hence, #2 or #3 based solution is needed to be developed.
Alternatives |  | Description | Pros Cons
1 | PLMN ID | Multiple PLMN-IDs are used. Each PLMN-ID indicates a particular CN Overlay network. This solution reuses network sharing concept (MOCN) | Reuse existing procedures, CN sharing Operators in some countries cannot obtain new PLMN-ID, due to regulation. Managing of IMSIs per CN overlay network is operational headache.
2 | APN | APN indicates CN Overlay Network. In subscription information the default APN is the CN overlay network. OPEN ISSUES: Problems with Multiple APNs in subscription? UE only provides APN in attach, but not in TAU, so how is MME selection at TAU supported? | No new indication in Subscription Still need to solve the re-direction of UE to right MME.
3 | New CN Type Indication | New parameter in Subscription that indicates the CN Overlay type | Cleaner solution with a new feature supported by new indication Need to solve the re-direction of UE to right MME
We need to choose slide 6 or 7

## Slide 7: Indication of CN Overlay
Alternatives |  | Description | Pros Cons
1 | PLMN ID | Multiple PLMN-IDs are used. Each PLMN-ID indicates a particular CN Overlay network. This solution reuses network sharing concept (MOCN) | Reuse existing procedures, CN sharing Operators in some countries cannot obtain new PLMN-ID, due to regulation. Managing of IMSIs per CN overlay network is operational headache.
2 | APN | APN indicates CN Overlay Network. In subscription information the default APN is the CN overlay network. | No new indication in Subscription Still need to solve the re-direction of UE to right MME. Problems with Multiple APNs in subscription. Problems with right MME selection at TAU.
3 | New CN Type Indication | New parameter in Subscription that indicates the CN Overlay type | Cleaner solution with a new feature supported by new indication Need to solve the re-direction of UE to right MME
We need to choose slide 6 or 7

## Slide 8: Solution for Problem #2
Problem #2: How to direct the UE to MME of the appropriate overlay network?
NOTE: Solution in following slides is based on a new CN Type indication in the subscription.

## Slide 9: Original Proposal at SA2#99 - Reroute Command -
UE
HSS
MME
Overlay
S/PGW
eNB
Overlay
MME
S/PGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter to indicate that UE can select “Core Network Type” in the Subscription Data.
2. Reroute Command
(NAS, Core Network Type)
3. Attach Request
Problem: Once NAS security between first MME and UE has been established, Overlay MME cannot communicate with UE.

## Slide 10: Issues Identified
We must find the solution to avoid the security problem of IMSI Attach as described in the previous slide.
We should define the behavior of roaming network which does not support a certain value of “Core Network Type”.

## Slide 11: Security Problem of IMSI Attach

## Slide 12: Alternatives of IMSI Attach 1. Security Key Inheriting
IMSI Attach is converted into GUTI Attach, and eNB select the right pool and pick one of the overlay MMEs according to “Core Network Type”.
eNB
Overlay
MME
UE
HSS
MME
Overlay
S/PGW
S/PGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter to indicate that UE can select “Core Network Type” in the Subscription Data.
2. Reroute Command
(NAS, Core Network Type, GUTI)
4. Identification Req/Resp
(Security Context)
3. Attach Request
(GUTI)
5. (Optional) NAS Security Mode Command between Overlay MME and UE, and continue Attach procedure.
It is possible for Overlay MME to communicate with UE by using first MME’s Security Key.
6. Bearer estb.
7. ULR/ULA

## Slide 13: Alternatives of IMSI Attach 2. Containing “Core Network Type” in AIA
Overlay MME
Reroute Command
(Attach Request Message, Core Network Type)
Attach Request
“Core Network Type” is contained
Authentication Information Request
Authentication Information Response

## Slide 14: Alternatives of IMSI Attach 3. specific GUTI + non-broadcast TAI (ZTE proposal)
eNB
Overlay
MME
UE
HSS
MME
Overlay
S/PGW
SGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter to indicate that UE can select “Core Network Type” in the Subscription Data.
2. Attach Accept
MME allocates specific GUTI (including MMEGI-B) with a non-broadcast TAI if “Core Network Type” is contained in the Subscription Data.
MMEGIs are pre-configured.
MMEGI-A -> of blue MME
MMEGI-B -> of overlay MME
3. TAU Request (w/ MMEGI-B)
A non-broadcast TAI (e.g. 0000, FFFF) drives UE to perform TAU procedure.
Overlay MME trys to get context information from blue MME due to the configuration of MMEGI-B
MMEGIs are pre-configured.
MMEGI-A -> redirect to blue MME
MMEGI-B -> redirect to overlay MME
MMEGIs are pre-configured.
MMEGI-A -> of blue MME
MMEGI-B -> of blue MME
4. Identification Req/Resp
2. Bearer estb.
(PGW would be Overlay PGW)
5. Bearer estb.
6. ULR/ULA

## Slide 15: Evaluation of Alternatives
We think alt.1 is the best solution.
Alternatives |  | Solves the security problem @SA2#99? | Pros Cons
1 | Security Key Inheriting | Yes | - Reuse existing procedures - Faster (Bearer establishment is needed only 1 time) - Takes longer than alt.2
2 | Containing “Core Network Type” in AIA | Yes | - Fastest (ULR/ULA with 1st MME can be omitted) - Bigger HSS impact expected - Security authorization would delay than usual
3 | specific GUTI + non-broadcast TAI | Yes | - Reuse existing procedures - No impacts on eNB - All MMEs must store the list of GUTI for each MME in the overlay network MME pool. - All MMEs and eNBs must have complex pre-configurations about GUTIs (MMEGIs). -> This may lead to exhaustion of MMEGIs in network. - May not be simple to apply this to 2G/3G where the NNI field structure is not well defined.

## Slide 16: ANNEX: Rerouting at Identification Req/Resp procedure
GUTI Attach procedures (once IMSI Attach has been completed)
Overlay MME
“Core Network Type” is contained
Reroute Command
(Attach Request Message, Core Network Type)
Attach Request

## Slide 17: ANNEX: Rerouting at Context Req/Resp procedure
No need to perform
“Core Network Type” is contained
Indicating failure due to the mismatch of “Core Network Type”
Reroute Command
(TAU Request Message, Core Network Type)
Overlay MME
TAU Request

## Slide 18: Roaming Compatibility

## Slide 19: If roaming NW does not support a certain value of “Core Network Type”
VPLMN
HPLMN
HSS
MME
HSS
MME
eNB
eNB
Core Network Type=10
10 : M2M network
10 : not supported
roaming
MME
(for M2M)
MME
(for M2M)
How does it work?
M2M device @ VPLMN

## Slide 20: If roaming NW does not support a certain value of “Core Network Type”
eNB
MME
HSS
MME (for M2M)
VPLMN
HPLMN
eNB
MME
HSS
MME (for M2M)
UE
If indicated “Core Network Type” is not supported in VPLMN, the MME should continue to perform normal Attach procedure and make UE camp on the conventional network.
Attach Request
Perform AIR/ULR to aquire “Core Network Type”
Send “Core Network Type” in AIA/ULA
- For example : IMSI Attach case -
Attach Accept
MME ignores the indicated “Core Network Type” if the VPLMN does not support its value.

## Slide 21: Well-known values of Core Network Type
To avoid the inconsistent use of values of “Core Network Type” between operators, it may be important to define some of the well-known values of “Core Network Type” for the roaming or other interworks between operators.
We suggest the well-known values as follows;
Values | Purpose | Domain
0 | Conventional Network | between operators # appropriate (roaming) agreements are necessary
1-7 | Standardized overlay network values (e.g. MTC devices) | 
8-15 | Reserved/Proprietary |