## Slide 1: SA2 Work Status: Network Slicing
China Mobile, Nokia
(Rapporteurs)

## Slide 2: 1 Network Slicing Definition
Network Slice (NS): is composed of all the NFs that are required to provide the required Telecommunication Services and Network Capabilities, and the resources to run these NFs.
  NOTE 4: In this document a Network Slice is equivalent to a Network Slice Instance.
  Editor’s Note: It is for the RAN WG to determine how the Network slicing applies to RAN. It is FFS whether some aspects of level of isolation/separation should be part of the NS definition.
  NOTE 5: The PLMN may consist of one or more network slices. The special case of just one Network Slice is equivalent to an operator’s single, common, general-purpose network, which serves all UEs and provides all Telecommunication Services and Network Capabilities that the operator wants to offer.

## Slide 3: 2.1 Possible Scenarios Considered
Dedicated Network slices includes the interpretation that the UE obtains services from different network slices and different CN instances, aiming at logical separation/isolation between the CN instances. This group is characterised by independent subscription management/mobility management for each network slice handling the UE.
Editor’s note: Whether it is worthwhile to allow a UE to simultaneously access multiple network slices is FFS.

## Slide 4: 2.2 Possible Scenarios Considered
2. Network slices with some shared components (e.g. MM function) and dedicated components (e.g. UP functions) – In this case, UE can camp in multiple network slices provided there is a single MM function for a given UE

## Slide 5: 3. Work Tasks of Identified Network Slicing
ID | Work Task(s) | Work Task Description
WT_#1 | Network Slice Instance Selection and Association | Initial network slice instance selection to support UE’s service establishment and re-selection to support UE mobility and other scenarios that are TBD, Network slice instance identification, Service authorization for UE association with network slice instance Network assistance information support for UE network slice instance association with corresponding PLMN
WT_#2 | Network Slicing Isolation | Security isolation Resource isolation OAM support isolation (e.g. Usage and Fault isolation etc.)
WT_#3 | Network Function Determination | Identifying what are the network functions comprise of a network slice for particular network services
WT_#4 | Network Function Sharing support | Identifying network function(s) that need to be shared between network slice instances Defining what needs to be done for enabling the NFs identified above under 1) for supporting the sharing
WT_#5 | Enable operators to use the network slicing concept to efficiently support multiple 3rd parties (e.g. enterprises, service providers, content providers, etc.) that require similar network characteristics. | Handling of UE’s subscription between MNO and its 3rd parties to enable MNO to leverage the network slicing solution to efficiently utilize system resources to support multiple 3rd parties’ network services with adequate QoS, mobility, service continuity etc. support
WT_#6 | UE Simultaneous Association with Multiple Network Slice Instances | Coordination on security, MM and SM support, if any, and any other required operations.
WT_#7 | Network Slicing Roaming support | Determination what visiting and home Network Function(s) are required to support roaming.
WT_#8 | Network Slicing terminology & definitions | If Network Slice Instance is agreed to apply E2E system, then, we should consider new terminology for Access slice instance and Core slice instances.

## Slide 6: 4 Proposed Way Forward
It is suggested RAN groups takes into account the slicing progress as above
If RAN decides whether slicing applies to RAN, kindly let SA2 know