## Slide 1
SA WG2 Meeting #123 S2-178032
23-27 October 2017, Ljubljana, Slovenia (revision of S2-177224)
Source: Vencore Labs, OEC, AT&T, T-Mobile, Verizon, Sprint, FirstNet
Title: QCI Priority Level Override
Document for: Discussion / Endorsement
Agenda Item: 7.1
Work Item / Release: TEI15 / Rel-15
Abstract of the contribution: Triggered by recent proposals to expand the existing set of standardized QCI values (as specified in TS 23.203), the contribution explores the current SA2 methodology for assigning new standardized QCI values. It identifies several issues and proposes adding a new optional information to overcome the identified issues.

## Slide 2: The Need
Flexibility in configuring relative service priorities based on operator policies and national / regional regulatory requirements
  Not only for admission and retention, but also for scheduling during temporary congestion situation
Expressed by all major US Operators

## Slide 3: Why is it Important
A GBR bearer is admitted and experiences normal traffic situation (T0)
  Packets are handled meeting the PDB and PER
Propagation environment changes (T1)
  The system cannot handle all packets of all admitted GBRs within the allowed PDB (of each GBR bearer)
  Situation may be temporary – so too early to release some bearers based on ARP
The congestion situation persists for an extended period
  Overload control is applied (T2)
  Some bearers are released (based on ARP) to relieve congestion
  Other admitted bearers can be served within specified PDB and PER
How to handle already admitted GBR bearers during (T1 – T2)?
  As per TS 23.203, use QCI Priority Level to determine which bearer to be given priority in meeting PDB
  Use of ARP precluded by TS 23.401. Any use of ARP here is non-standard

## Slide 4: What was Proposed
QCI Priority Level Overide IE
  When present replaces the existing priority level in QCI
  Consistent with usage of QCI in TS 23.203
  Decouples Priority Level from other QoS characteristics
  Gives the necessary flexibility
Supported by all major US Operators

## Slide 5: Comments
GBR once admitted, its QoS requirements are always met
  If so, why is QCI Priority Level (PL) specified for GBR?
    If there is no use for QCI PL for GBR, then remove QCI PL for GBR from the QoS characteristics table
  Why is Notification control parameter added in 5G?
ARP can be used
  Not only for admission and retention, but also for scheduling
  Contradicts TS 23.401
Request new QCIs

## Slide 6: QCI PL vs ARP Debate
If QCI Priority Level influences the treatment of admitted SDF as specified in TS23.203
  A Priority Level Override is recommended to allow flexibility for operators to change the treatment as needed
    Allows QCI Priority Level to be decoupled from other QCI characteristics
    Reduces the need of new QCIs (when only Priority Level is different)
If Priority Level of QCI does not influence / is not used in the treatment of a GBR SDF in any fashion
  Remove Priority Level from the QCI characteristics applicable for GBR Resource types
If ARP PL can be used to influence packet handling
  Remove the restriction placed in TS 23.401 on ARR’s impact on packet handling of established bearers

## Slide 7: Alternatives QCI Priority Level Override
Request new QCI
  Impact to all existing nodes
  Impacts other specification (SRVCC, etc)
  Still does not decuple priority level from other QoS characteristics
  Proliferation of QCIs
Use ARP
  TS 23.401 precludes the use of ARP in scheduling
  Remove the restriction on the use of ARP for scheduling in TS 23.401

## Slide 8: Summary
QCI Priority Level Override is a better approach
Removing the restriction on the use of ARP in packet scheduling in a standardized way – second best option
Choose one of the two options above and allow revision of relevant specifications

## Slide 9: Original Slides

## Slide 10: Objective
Propose adding an optional QCI Priority Level Override IE to QCI to allow flexibility in configuring relative service priorities based on operator policies and national / regional regulatory requirements

## Slide 11: QCI
TS 23.203 defines a set of standardized QCIs and associated QoS characteristics
  Resource type, Packet Error Rate (PER), Packet Delay Budget (PDB) and Priority Level (PL)
  PER and PDB are well understood, but role of PL has been subjective
TS 23.203 states
  If the target set by the PDB can no longer be met for one or more SDF aggregate(s) across all UEs that have sufficient radio channel quality then Priority shall be used as follows: in this case a scheduler shall meet the PDB of an SDF aggregate on Priority level N in preference to meeting the PDB of SDF aggregates on next Priority level greater than N, until the priority N SDF aggregate's GBR (in case of a GBR SDF aggregate) has been satisfied.

## Slide 12: Current SA2 Approach for QCI Assignment and Issues
9 QCI values assigned in Rel-8
More QCI values added for MC-PTT signaling, voice and data, V2X
Additional QCI values proposed for MC Video and Ultra Reliable and Low Latency Communication
  Need to consider impacts to existing services
Issues
  A new QCI that includes a PL which has a higher priority than the existing set impacts the relative order of the services supported by a 3GPP system
  Problematic for national networks where multiple priority services that are subjected to regulatory rules are supported
The 3GPP specification should be flexible to provide operators with the tools to meet national/regional requirements and not dictate or specify relative priority of application services

## Slide 13: A Day in the Life of a GBR Bearer
A GBR bearer is admitted and experiences normal traffic situation (T0)
  Packets are handled meeting the PDB and PER
Propagation environment changes (T1)
  The system cannot handle all packets of all admitted GBRs within the allowed PDB (of each GBR bearer)
  Situation may be temporary – so too early to release some bearers based on ARP
The congestion situation persists for an extended period
  Overload control is applied (T2)
  Some bearers are released (based on ARP) to relieve congestion
  Other admitted bearers can be served within specified PDB and PER
How to handle already admitted GBR bearers during (T1 – T2)?
  As per TS 23.203, use QCI Priority Level to determine which bearer to be given priority in meeting PDB
  Use of ARP precluded by TS 23.401. Any use of ARP here is non-standard

## Slide 14: Need for Flexibility
For a given combination of Resource Type, PDB and PER (for example to support voice), operators require flexibility to assign different relative priorities
  Depending on the specific context it is used (normal voice, emergency, MPS, MC, etc.) or even for different class of users (platinum/gold/silver)
The relative service priorities should be configurable and be based on operator policies and corresponding national / regional regulatory policies
  3GPP specifications should not force specific priorities
5GS overcomes these limitations by allowing custom values for PDB, PER and PL as part of dynamic 5QI assignment
LTE lacks similar flexibility

## Slide 15: QCI Priority Level Override IE
Optional IE in QCI
  [QCI, QCI Priority Level Override (optional)]
  If present the value in the QCI Priority Level Override field will replace the existing QCI Priority Level in the QoS characteristics (Resource Type, Priority Level, PDB, PER) derived from the QCI value
  Provides flexibility in a standardized fashion
  Separates QCI priority level from other intrinsic QoS characteristics (such as PDB and PER)
  Allows easier interworking between 5G and LTE
Impacted specifications
  Two Existing Specifications (TS 23.203 & TS 23.401) requiring CRs submitted under TEI15
  5G interworking impacts to TS 23.501 & TS 23.502 requiring p-CRs submitted under 5GS QoS agenda.
  Stage 3 work in CT1, CT3, CT4, RAN2 and RAN3 would follow

## Slide 16: Recommendation
Endorse adding an optional QCI Priority Level Override IE in QCI in Release 15
Send an LS to appropriate CT and RAN WGs
Agree related SA2 CRs / Allocate time slot at SA2#124 to discuss and agree them

## Slide 17: Backup

## Slide 18: QCI PL vs ARP Debate
If QCI Priority Level influences the treatment of admitted SDF as specified in TS23.203
  A Priority Level Override is recommended to allow flexibility for operators to change the treatment as needed
    Allows QCI Priority Level to be decoupled from other QCI characteristics
    Reduces the need of new QCIs (when only Priority Level is different)
If Priority Level of QCI does not influence / is not used in the treatment of SDF in any fashion
  Remove Priority Level from the QCI characteristics applicable for GBR Resource types
If ARP PL can be used to influence packet handling
  Remove the restriction placed in TS 23.401 on ARR’s impact on packet handling of established bearers

## Slide 19: Role of ARP
During resource limitations, ARP determines which bearer to be admitted (Admission) and ARP determines which bearer to be retained or released (Retention)
Although ARP may be used to support admission and retention decisions concerning particular bearers, TS 23.401 precludes the use of ARP for the scheduling of individual packets