## Slide 1
Handling of QoS flows at 5GS to EPS mobility
Intel
S2-1901758
3GPP TSG SA2#130

## Slide 2: 5GS=>EPS HO with N26: Use cases to consider
Case A: GBR QoS Flow mapped 1:1 to EPS bearer
  QoS rules preserved at HO to EPS
Case B: GBR QoS Flow with no mapping
  QoS rules deleted after HO to EPS; App layer informed about release of dedicated resource
  Traffic implicitly mapped on Default EPS bearer (if it has no assigned TFT)
  Traffic likely to be terminated by application
Case C: Multiple non-GBR QoS Flows mapped to EPS bearer other than Default EPS bearer
  QoS rules preserved at HO to EPS
  How does signalling of TFT work for the subsequent QoS Flow (e.g. “TFT ‘add filter’ operation) while UE is in 5GS?
  Answer: When QoS Flow #4 is created, network also signals mapped EPS bearer configuration, including a TFT (‘create new TFT’), as the flow is mapped to a dedicated EPS bearer. The QoS Flow description for QoS Flow #4 includes a pointer to EPS bearer ID #2. Later when QoS Flow #5 is created, network updates the mapped EPS bearer configuration (‘modify existing EPS bearer’ + ‘add packet filters to existing TFT’). The QoS Flow description for QoS Flow #5 includes a pointer to EPS bearer ID #2.
Case D: Non-GBR QoS Flow with no mapping
  QoS rules deleted at HO to EPS; App layer informed about release of dedicated resource
  Traffic implicitly mapped on Default EPS bearer (if it has no assigned TFT)
  Traffic may be continued or terminated by application
Case E: Multiple non-GBR QoS Flows mapped on the Default EPS bearer
  QoS rules preserved at HO to EPS (as for case C)
  When the Default QoS Flow #1 is created, network also signals mapped EPS bearer configuration, optionally including a TFT (‘create new TFT’). If QoS Flow #1 is associated with a ‘match-all’ packet filter, then the network does not include a TFT. The QoS Flow description for QoS Flow #1 includes a pointer to EPS bearer ID #1. Later when QoS Flow #2 is created, if a TFT exists, network updates the mapped EPS bearer configuration (‘modify existing EPS bearer’ + ‘add packet filters to existing TFT’). The QoS Flow description for QoS Flow #2 includes a pointer to EPS bearer ID #1.

## Slide 3: Conclusion
Handling of GBR and non-GBR flows is the same, although the consequences may be different
  If QoS Flow (GBR or non-GBR) does not have an assigned EBI, the QoS rules and PCC rules are deleted in UE and PGW-C+SMF, respectively
  UE and PGW-C+SMF inform the App layer and PCF, respectively, about the release of a dedicated QoS resource
  The SDFs corresponding to the QoS Flows (GBR or non-GBR) can continue flowing on the default EPS bearer if it does not have assigned TFT
  Any subsequent action (e.g. a QoS request for the downgraded SDFs) needs to be triggered from the app layer

## Slide 4: BACKUP slide: Subsequent EPS=>5GS handback
Case A: GBR QoS Flow mapped 1:1 to EPS bearer
  TFT preserved at HO to 5GS
Case B: GBR QoS Flow with no mapping
  QoS Flow #6 is terminated; re-establishment of QoS flow requires new trigger from application layer when back in 5GS
Case C: Multiple non-GBR QoS Flows mapped to EPS bearer other than Default EPS bearer
  1:N handover to 5GS is possible
  TFT preserved at HO to EPS
  How does signalling of QoS rules works in PCO if EPS bearer #2 is being updated while UE is in EPS?
  Answer: When EPS bearer #2 is created, the network also signals QoS Flow description (‘Create new flow description’) and QoS rules for QoS Flow #4 (‘Create new QoS rule’) in the ePCO IE. The QoS Flow description for QoS Flow #4 includes a pointer back to EPS bearer ID #2. Later when the EPS bearer #2 is modified, the network also signals QoS Flow description (‘Create new flow description’) and QoS rules (‘Create new QoS rule’) for QoS Flow #5. The QoS Flow description for QoS Flow #5 includes a pointer back to EPS bearer ID #2.
Case D: Non-GBR QoS Flow with no mapping
  QoS Flow #3 is terminated, but the corresponding traffic is mapped on the Default QoS Flow
  Re-establishment of QoS flow requires new trigger from application layer in UE or from SMF when back in 5GS
Case E: Multiple non-GBR QoS Flows mapped on the Default EPS bearer
  1:N HO to 5GS is possible
  How does signalling of QoS rules work in PCO if EPS bearer #2 is being updated while UE is in EPS?
  Answer: When the Default EPS bearer #1 is modified while the UE is in EPS, the network also signals QoS Flow description (‘Create new flow description’) and QoS rules (‘Create new QoS rule’) for QoS Flow #2. The QoS Flow description for QoS Flow #2 includes a pointer back to EPS bearer ID #1.