## Slide 1: 3GPP TSG-SA WG2 Meeting #132 S2- 1903172 Xi’an, China, 8 - 12 April, 2019 (revision of S2-19xxxx) Source: Ericsson Title: NF Set and NF service Set clean up Document for: Discussion Agenda Item: 6.19 Work Item / Release: 5G_eSBA /Rel-16
Abstract of the contribution: This contribution motivates clarifications and changes proposed in S2-1903173
Ericsson
2019-03-30

## Slide 2: Set definitions and Editor Note on set identifiers
NF Set: A group of interchangeable NF instances of the same type, supporting the same services and the same Network Slice(s). The NF instances in the same NF Set may be geographically distributed but have access to the same context data.
NF Service Set: A group of interchangeable NF service instances of the same service type within an NF instance. The NF service instances in the same NF Service Set have access to the same context data.
In 6.2.6 NRF in the NF profile it is new added:
  NF Set ID.
  NF Service Set ID of the NF service instance.
  Editor's note: It is FFS whether the NF Service Set ID is unique within the NF instance or NF Set. If former, it is FFS how to correlate the NF Service Set ID values between the NF instances within the NF Set.
Observation 1: The NRF provides to a consumer the necessary information to identify NF instances belonging to a NF Set and Service instances belonging to a NF Service Set
Observation 2: the NF Service set is defined within a NF instance and thus the NF Service Set ID has only significance within the NF instance
Proposal 1: the EN above can be removed.
Editor's note: It is FFS whether the NF Service Set ID is unique within the NF instance or NF Set. If former, it is FFS how to correlate the NF Service Set ID values between the NF instances within the NF Set.

## Slide 3: Set interchangeability (i)
In 6.3.1 it is stated:
  If the end point address provided by a NF service producer points to a specific target NF producer/NF service producer instance within a Set, the NF consumer or SCP may re-select another service instance of the same NF service within the same NF service Set in that same NF instance, or another NF instance in the same NF Set for subsequent transaction, and get the same results as if the original selected NF service instance was used. Re-selecting may be needed if the requester NF fails to contact the original NF service instance
Observation 3: Endpoint Address(es) are also provided to an NF consumer by the NRF. A clarification that the Endpoint Address(es) provided by the NF service producer refers to the address returned in the request response may be beneficial.
Proposal 2: Adjust the text to:
  If the Endpoint address returned by a NF service producer in a response message points to a specific target NF producer/NF service producer instance within a Set, the NF consumer or SCP may re-select another service instance of the same NF service within the same NF service Set in that same NF instance, or another NF instance in the same NF Set for subsequent transaction, and get the same results as if the original selected NF service instance was used. Re-selecting may be needed if the requester NF fails to contact the original NF service instance

## Slide 4: Set interchangeability (ii)
  If the end point address provided by a NF service producer points to a specific target NF producer/NF service producer instance within a Set, the NF consumer or SCP may re-select another service instance of the same NF service within the same NF service Set in that same NF instance, or another NF instance in the same NF Set for subsequent transaction, and get the same results as if the original selected NF service instance was used. Re-selecting may be needed if the requester NF fails to contact the original NF service instance
Observation 4: Reselection in case of failure is addressed in these sentences, however the Rel-15 reselection within an NF instance now is not considered and should be re-introduced. Some improvement in readability are also needed.
Proposal 2: Adjust the text to:
  If the end point address provided by a NF service producer points to a specific target NF producer/NF service producer instance within a Set, the NF consumer or SCP may re-select for a subsequent transaction another service instance of the same NF service either within the same NF service Set in that same NF instance, or in another NF instance in the same NF Set, or in the same NF instance, and get the same results as if the original selected NF service instance was used. Re-selecting may be only needed if the requester NF fails to contact the original NF service instance

## Slide 5: Set interchangeability and use of locality information (i)
Whether locality of the NF instance or NF service instance should be considered by a consumer at reselection within a set, it is not explicitly stated.
Proposal 4: update re-selection text accordingly as follows
  If the end point address provided by a NF service producer points to a specific target NF producer/NF service producer instance within a Set, the NF consumer or SCP may re-select another service instance of the same NF service within the same NF service Set in that same NF instance, or another NF instance in the same NF Set for subsequent transaction, and get the same results as if the original selected NF service instance was used. The consumer should select an alternative instance with the same location. Re-selecting may be needed if the requester NF fails to contact the original NF service instance.

## Slide 6: Locality and reselection (i)
In 6.3.1.1 Location information it is stated:
  A locality parameter describes the location of NF instance (e.g. geographic location, data center). The locality of the NF instance is limited to one location.
  The locality parameter may be used to select the NF service instance or NF instance from a particular network location based on local configuration.
  Editor’s note: It is FFS whether the locality parameter is defined at NF instance level or NF service instance level. If latter, the locality of the NF instance is the union of the locations of its NF service instances. If later, it is FFS how stateful NF services can handle request and process transactions for the same UE.
Observation 8: In order to select an instance from a particular network location, the locality parameter need to be defined at NF instance level or NF service instance level. If defined at NF Service Level , the use of a locality at NF instance level lacks significance for service reselection. However for backward compatibility the locality at NF instance level is needed.
Additionally if locality is expected to be considered at reselection within a set, its significance may need to extend beyond the sole geographical aspects and include at the same time also deployment aspects such as data centers and clusters.
Proposal 4: Remove the EN and adjust the text to:
  A locality parameter describes the location (e.g. one or more of the following: geographic location, data center, cluster) of an NF instance or NF Service instance. The locality may be defined at NF instance level and at NF service instance level. When the locality is defined at NF service instance level, the locality of the NF instance is limited to one location the locality of the NF instance is only used for backwards compatibility..
  The locality parameter may be used to select the NF service instance or NF instance from a particular network location based on local configuration.
  Editor’s note: It is FFS whether the locality parameter is defined at NF instance level or NF service instance level. If latter, the locality of the NF instance is the union of the locations of its NF service instances. If later, it is FFS how stateful NF services can handle request and process transactions for the same UE.

## Slide 7: Summary
The proposed changes are included the CR of 23.501 S2-193173