## Slide 1: Handling of IPv6 addresses for FN-RG
Source: Rapporteour (Huawei)
Document for: Discussion
Agenda Item: 4.1
Work Item / Release: 5WWC

## Slide 2: BBF Request (S2-2003627)
Support for FN-RGs using IPv6oE procedures Current FN-RGs in IPoE supports the specification defined in RFC2464 for Local Link Assigment based on self-assignment from MAC address and there is no means for override such assignment from 5G CN. Proposed solution is to extend NAS in PDU sessno establishment for signaling to SMF the selected LLA
Support for FN-RGs using PPPoE and IPv6CP procedures IETF RFC 5072 NCP negotiation procedures performed between the FN-RG and W-AGF require the AGF to know the SMF’s link local address. Proposed solution to add an information element to the PDU Session Establishment Accept message that provides this information to the W-AGF for use in RFC 5072 negotiation procedures.
The discussion has been postponed from the previous meeting
Options to address the above
To endorse the BBF proposals approving CR for addition of new parameters in NAS SMF Container exchanged in PDU session messages and the SMF behavior related to LLA management when request from FN-RG (S2-2004926)
Do not change 3GPP specifications. Assume that BBF can resolve the issue anyway, e.g. by W-AGF being specified as a layer 3 node and performing interworking between the SMF and an FN-RG for IPv6 procedures/packets”