## Slide 1: Discussion on the update of the AIML SID
Huawei, HiSilicon

## Slide 2: Outline
WTs in Moderator draft SID
Additional WTs

## Slide 3: WTs in Moderator draft SID
WT | Proposal
WT#1: AI/ML cross-domain coordination aspects (Note: SA2 will start the study to investigate the possible architecture options and align with RAN results as necessary once RAN completes its work) WT1.1: 5GC support for UE/air interface AI/ML; WT1.2: Study enhancements to UE data collection framework; WT1.3: Study 5GC support for AI/ML model and information sharing to the UE; WT1.4: Study the Model ID alignment, Lifecycle management (LCM) alignment between SA2 and RAN e.g. in terms of Model performance and Model ID; WT1.5: Study QoS and policy control to support RAN model transfer and delivery (including data collection); WT1.6: Interaction/coordination with RAN to support the AI enabled RAN framework (i.e. AI/ML for NG-RAN in Rel-18). | Suggest to remove this WT: RAN1 use cases are all related to physical layer. There is no benefit for CN to be involved assisting data/model transmission or analytics for physical layer. RAN3 AI R18 already concluded that AI/ML model handling is in gNB or OAM. It is unclear why CN should be involved in the RAN use cases. It is high risk to go no where for this WT as RAN1 can conclude there is no CN impact (i.e. similar as RAN3). Discussing this even without conclusion in the RAN will steal TU budget for other more important WTs/SIDs.

## Slide 4: WTs in Moderator draft SID
WT | Proposal
(FFS) WT2: Study the following potential enhancements to enable 5G system to assist cross-domain (e.g. UE, 5G Core, application, OAM) AI training and inference (so-called “Vertical Federated Learning (VFL)”) (Note: RAN aspects are out of scope) WT2.1: How to support feature determination and alignment across domains when applying the VFL operation; WT2.2: How to identify/select the required NF(s) within the 5G Core domain and the UEs corresponding to the local feature in order to collaborate on the VFL operation (i.e. training or inference); WT2.3: Whether and which policy configurations and enhancement are required in order to support VFL operation (i.e. training or inference); WT2.4: What is the proper transport mechanism to support cross-domain AI model training/inference data transfer. | Suggest to remove this WT: It is unclear what the use case to support the VFL is. Even if there is a use case, why should OAM and UE be involved in the VFL? OAM is within operator’s domain, NWDAF can retrieve data from OAM already. VFL would need complex privacy protection methods to protect local data privacy, it is inefficient to support such mechanism in UE. (For example, the calculation of the data with holomorphic encryption via HElib is almost 1 million times slower than the average speed of non-cipher text.) For the individual UE itself, it is lots of pain and no gain.

## Slide 5: WTs in Moderator draft SID
WT | Proposal
WT3: Study enhancements to support NWDAF-assisted recommendations and address network abnormal behaviors WT3.1: 5GC recommendations; (FFS if in scope based on discussion in workshop, where aspects related to studies of robust and resilient core was deprioritized) WT3.2: Study prediction, detection, prevention, and mitigation of network abnormal behaviors (e.g. signaling storm). The study will analyze the handling of misbehaving NF in terms of abnormal behaviour, performance degradation, operational conflict, etc., and study further information exchange with MDAF, etc. for specific operational use cases. The study will focus primarily on existing enforcement mechanisms when available, and identify new ones when no existing ones can be used. | Suggest to reword this WT: In general support this WT. The network abnormal behaviors needs clear description. The simplest way is updated to “i.e. signaling storm” and remove other terms.

## Slide 6: Additional WTs
The additional WTs proposed by individual company has not been fully discussed. Further discussion is needed before the final decision.
WT a: reinforcement learning(RL)/NF feedback for accuracy
  Detail description: Whether and how to support additional NF feedback related to the NWDAF analytics and model training to improve the correctness.
  This comes from CMCC’s proposal in NWM and S2-2306503. It is related to the discussion on NF feedback for correctness in R18 and should be better be further discussed in R19 to calculate the accuracy for the analytic with NF actions.
  This picture comes from S2-2306503.
WT b:Transfer Learning between NWDAFs
  Detailed Description: Study 5GC extensions to support Transfer Learning between NWDAFs.
  This comes from ETRI and KDDI’s proposal in NWM. It can enable NWDAF to expedite the model training operation by leveraging trained models, and assist the NWDAF in generating models even in small dataset.

## Slide 7: Summary
It is proposed to remove WT1 and WT2 until a valid use case is found.
It is proposed to further discuss the additional WTs.