## Slide 1: Proposed formulation of WT#9 for 5G ProSe Ph3
Philips International B.V., Siemens AG, Lenovo, LG Electronics, Novamint, NICT, Mitsubishi Electric

## Slide 2: Introduction
Based on the SA Plenary Release 19 Workshop in June a list of topics was identified to improve ProSe, one of these topics was called “NPN Enhancements for ProSe”.
During SA2 Moderated E-mail discussions in August, 7 companies indicated support or conditional support for “NPN Enhancements for ProSe”, but at least 5 companies requested additional information to clarify the scope of this topic before they could indicate support. Hence this topics was not yet included by the moderator in the resulting draft release 19 SID for ProSe.
Furthermore, during the Conference Call on the 5G ProSe Phase 3 proposal for Release 19 on September 25, several companies had questions on what exactly would need to be done and how a limited scope can be achieved.
This proposal aims to clarify what is needed and proposes a formulation of WT#9 with limited scope to address the main purpose, i.e. enable ProSe to be deployed in Non-Public Networks.
It is important to consider this topic for inclusion in release 19, given that without NPN support, deployment of ProSe (e.g. in factories) is hampered, and important SA1 use cases identified and requirements for ProSe (e.g. collaborating mobile robots as specified in TS 22.104) cannot be fully supported. As indicated in LS S2-2311029, various whitepapers from 5G-ACIA such as “Using 5G sidelink in industrial factory applications” show the need for 5G sidelink communication to be supported in non-public networks (SNPN, PNI-NPN). It also affects other programs, such as Ranging, i.e. ranging cannot be deployed in NPNs unless NPN support for ProSe is added.

## Slide 3: What needs to be studied and specified?
As explicitly indicated in 23.501 clauses 5.30.2.0 and 5.30.3.1, ProSe is currently not supported for NPNs.
During preliminary discussions in SA2, several gaps were identified that would require some study. The most important of these include:
  Architecture and potential procedure updates for supporting Proximity-based Services within an NPN, such as enabling UEs to access NPNs via a ProSe relay, and enabling direct device communication in NPNs.  Currently the authorization/policy control is only done per PLMN, the Relay Service Codes cannot indicate access to NPN, and the architecture figures in TS 23.304 only provide explicit PLMN support.
  How to convey NPN related identifiers, such as NID, CAG ID during ProSe discovery, to aid in selection of ProSe peer UEs or relay UEs that match the network selection criteria for NPNs.  Currently only PLMN ID can be conveyed during discovery.
  Whether and how CAG is used for access control for ProSe UEs, in particular ProSe Remote UEs and U2N relays.  For example it is not clear if CAG affects which U2N relays can be selected for relay communication.
Also SA3 would probably need to study whether and how authentication/authorization procedures and key management functions need to be updated to support 3rd party credential holders and key generating EAP methods (e.g. EAP-TLS).

## Slide 4: Proposal
Propose to reintroduce WT#9 to the 5G ProSe Ph3 R19 study item proposal with the following formulation:
WT-9: NPN support for ProSe:
    Study architecture and potential procedure updates for supporting Proximity-based Services within an NPN. This includes studying how to support service authorization and provisioning of ProSe services within NPNs, and how to authorize and identify Relay Service Codes for UEs accessing an NPN via ProSe U2N Relay.
    Study how to convey NPN related identifiers, such as NID and CAG ID during ProSe discovery, to aid in selection of ProSe UEs (i.e. peer UEs for direct communication) or ProSe U2N Relays or ProSe U2U Relays that match the network selection criteria for NPNs.
    Study whether and how CAG is used for access control for ProSe U2N Relays and ProSe Remote UEs.
    Study impacts for supporting QoS handling for 5G ProSe Direct Communication within NPNs (e.g. custom QoS profiles).
  NOTE 1: ProSe direct or indirect communication involving UEs from a PLMN and UEs from an SNPN, and communication involving UEs from a PNI-NPN and UEs from an SNPN or from (a PNI-NPN of) a different PLMN is not included for study.
  NOTE 2: Connecting to an Onboarding-SNPN is not included for study.
  NOTE 3: Alignment with SA3 may be needed for potential NPN related authentication and key management updates for ProSe.
Amount of TUs for Study: 1, Normative: 1.