## Slide 1: Triggering VFL model training Possible use cases and Options
Thomas Belling
Nokia

## Slide 2: Use case 1: Model training triggered via internal service logic or configuration (OAM, out of SA2 scope)
Nokia view:
Seems already supported, no standards impacts apart from possibly showing box in flows.
Most likely scenario to trigger model training

## Slide 3: Use case 2: VFL Model training with NWDAF VFL server triggered by ANLF requesting VFL models
Nokia view:
Model provisioning is supported since Rel-17. Aim is that model can be used by other entity for inference than for training. This allows more flexible deployments and load distribution
Nokia would be happy to support this, but majority of companies seems to prefer that models cannot be transferred for VFL in this release
A compromise could be to allow transfer of models between servers in this release, but keep assumption that models cannot be transferred between VFL clients
  Complexity seem limited: Only addition of VFL correlation ID and a vendor container with further VFL info (features, weights, clients etc)

## Slide 4: Use case 3: VFL Model training with NWDAF VFL server controlled by some supervising AnLF not using VFL models (independent of Inference trigger)
Nokia view:
No necessity for this use case, no benefit, but lots of extra complexity
  Supervising AnLF role not backed by any study conclusions but appears to be entirely new role, could only be added by consensus.
If a VFL model is not distributed, VFL server can supervise training itself, or OAM can be used to trigger training.
Many Open questions: How would Supervising AnLF be selected? How would AnLF determine that model training or retraining is required? What would AnLF do with training info? What are appropriate service operations and parameters? How to consider accuracy monitoring? How does AnLF know applied model (e.g if it was recently retrained)? Service operations and parameters?
  Remark: Current proposal try to extend the Nnwdaf_MLModelProvision service to address this flow, but this seems not appropriate as no models are provisioned.
For AnLF as analytics proxy, see use case 7 considerations

## Slide 5: Use case 4: VFL Model training with AF VFL server supervised by AnLF (independent of Inference trigger)
Nokia view:
Possible befits as network might not have extra means to interact with AF (e.g. OAM) to control model training, but extra complexity.
Preference not to support this use case at such a late stage, but can live with majority view
Already agreed that Inference can be triggered by AnLF, so special AnLF to interact with AF already defined
Many Open questions: How would AnLF determines that model training or retraining is required? What would AnLF do with training info? What are appropriate service operations and parameters? How to consider accuracy monitoring? How does AnLF know applied model (e.g if it was recently retrained)? Service operations and parameters?
  Remark: There are proposal to extend the NafVFlModelTraing service to address this flow, but this requires more discussions since entirely different parameters are require and service is intended to be provided by AF VFL Client
  Remark: There seems consensus that no models are transferred from AF to AnLF
For AnLF as inference proxy, see use case 6 considerations

## Slide 6: Use case 4a: VFL Model training with AF VFL server supervised by AnLF not using VFL models (independent of Inference trigger) interacting with AF VFL server via an MTLF (as in endorsed CR)
Nokia view:
This use case is beyond my comprehension despite my best effort. I suspect it somehow relates to use case 7.
See concerns for use case 3.
In addition: Proxy NWDAF(MTLF) seems a new role. How is it discovered?

## Slide 7: Use case 5: Direct Inference request to NWDAF VFL server as trigger for model training
Nokia view:
Seems already supported, no standards extension apart from possibly showing in flows.
In deployment scenarios where an Analytics ID is only supported by VFL, only VFL servers would support it and can directly be discovered by analytics consumer/NEF via NRF without a need to support VFL. Thus very likely Analytics request flow.
But triggering Model Training at time of Analytics subscription is in general debatable, because training might take too long

## Slide 8: Use case 6: Inference request to AF VFL server via NWDAF to trigger training
Existing agreed flow for inference (for possible extensions to trigger model training see next slide)
Nokia view:
Ok to document an easy solution
But triggering Model Training at time of Analytics subscription is in general debatable, because training might take too long

## Slide 9: Use case 6 Solution Option 1 Inference request to AF VFL server via NWDAF to trigger training
Existing agreed flow (for possible extensions to trigger model training see next slide)
Nokia view:
OK to support, No standards effort apart from possible mentioning in flow

## Slide 10: Use case 6 Solution Option 2 Inference request to AF VFL server via NWDAF to trigger training
Nokia view:
Depends on use case 4 support

## Slide 11: Use case 7: Indirect Inference request to NWDAF via AnLF supporting no VFL models (NWDAF can be VFL server or possibly forward request to AnLF as server)
Existing agreed flow for inference (for possible extensions to trigger model training and how AnLF determines its role, see next slide)
Nokia view:
AnLF as analytics request/subscription proxy is a new function introduced for VFL (apart from roaming support)
The need for an AnLF as analytics proxy is very debatable for NWDAF as VFL server: If an analytics ID is to be provided via VFL, only the NWDAF VFL server could indicate the support for that Analytics ID in its NF profile and the Analytics consumer (or NEF) can then directly discover the NWDAF VFL server at the NRF and contact it
Existing agreed flow is thus debatable, but unless there is agreement to remove AnLF as analytics proxy we should make it work
Ok to document an easy solution for VFL training triggering based on inference according to this flow. But triggering Model Training at time of Analytics subscription is in general debatable, because training might take too long
Main concern of some companies seems to be how an AnLF can determine that it needs to acts as analytics proxy
  But as AnLF as analytics proxy is new functionality for VFL, it can be assumed that it is enhanced, and backward compatibility with Rel-18 AnLF is not an issue

## Slide 12: Use case 7: Solution option 1 Indirect Inference request to NWDAF via AnLF supporting no VFL models
Nokia view:
Preferred solution option. No signaling extensions required. Also agreed Info in NRF profile should be sufficient

## Slide 13: Use case 7: Solution option 2 Indirect Inference request to NWDAF via AnLF supporting no VFL models
Nokia view:
Seems either dependent on Use case 3 support (with debatable signaling solution) or on misconception relating to the need of a backward compatible solution.
Not acceptable

## Slide 14: Conclusions
Triggers for VFL training could be configuration, internal service logic (e.g. to supervise accuracy), or inference/analytics requests.
Model provisioning procedure enables an AnLF that needs a ML model to request a model from MTLF and in this manner also to trigger model training and provide related requirements. If a NWDAF VFL server split into AnLF and MTLF and related model transfer is supported, a model provisioning request can thus be an additional trigger for an MTLF to train a VFL server.
However, if AnLF and MTLF are assumed to be collocated in the VFL server NWDAF, there is no need for model provisioning between them, or for another NWDAF to supervise the model training. How would that supervising NWDAF know related requirements (time when model is required, accuracy etc)? A model training supervising NWDAF would be an architectural change not backed by any study conclusions and without any clear benefit.
For VFL inference, the newly introduced “Analytics proxy AnLF” can determine based on the NRF profile of the NWDAF VFL server that it is a VFL server and then forward the analytics request or subscription without retrieving a VFL model; there is no need for a trial-and-error model retrieval attempt.