## Slide 1: NTT DOCOMO's views on 6G study

## Slide 2: Outline
Based on the lessons learned from 5G, the design principles for the 6G System should aim at:
  Simplified architecture: Consolidate network functions (NFs), addressing 5G's excessive fragmentation (30+ NFs) to reduce complexity, costs, and failure risks.
  Streamlined deployments: Minimize standardized deployment options to avoid heterogeneous deployments paths and increased costs.
  Essential interworking: Include only strictly necessary features for 6G and legacy system migration.
  Reduced TCO: Identify solutions to reduce Total Cost of Ownership of the network.
  Innovation enablement: Introduce features supporting novel value-added services, like AI, exposure services, and compute offloading, etc.
  Standardization for a Seamless 6G Future: To ensure seamless interoperability and prevent vendor lock-in, 6G systems must be built upon open and unified standards. This is particularly critical for the AI-native 6G core.
  Sustainability: Enable the mobile industry to achieve its sustainability goals and drastically reduce energy consumption and carbon footprint, aligning with broader industry trends
  Energy efficiency, robustness, and resilience are fundamental requirements integrated into every aspect of 6G architecture design and system procedures throughout the study.
NOTE: The architecture requirements presented in the subsequent slides do not reflect a specific order of priority.

## Slide 3: View on 6G SID Scope Content for Architecture requirements (1/4)
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | 6G Simplified architecture | Simplify architectural framework in comparison with 5G Only standalone architecture Reduced number of NFs Categorize NFs into Mandatory NFs and Optional NFs | Installation, Deployment & Operation: reduce the complexity by reducing signals between NFs and reduced TCO. Resiliency improvement: simplified core leads to lower possibility of communication failures. Reusable Core Functions: Identify the common and basic functions on which all functions or services can be built, so that an operator does not have to change or modify these functions each time a new feature or services are introduced. | RAN and CT WGs
2 | In network compute | Integration of computation and communication capabilities in the mobile network; the 3GPP System: Exposes compute resources to (third party) applications and receives service requirements from application layer. Executes data processing and offloads application workloads within the operator's network. Ensures continuous compute availability during UE mobility. | Providing compute capabilities in addition to communication capabilities may be a key enabling factor for 6G networks to support and enable new revenue streams such as artificial intelligence and XR applications. Target SA1 requirement in TR 22.870 “Subject to privacy considerations and regulatory requirements, the 6G network shall be able to enable compute offloading to operator managed data network for third party applications.” | SA3, SA5
3 | AI native 6G Core | Every network function is empowered by AI/ML to optimize the operation/functionality of the NF. Support efficient data collection and standardized open ML model life-cycle management capabilities to support the AI empowered NFs in multi-vendor deployment Supports advanced AI/ML techniques such as transfer learning, etc. | Optimizing the operation and control of the network by AI/ML is a promising approach as the ingredient part of the 6G which should be supported in multi-vendor deployment via standardized open ML model LCM. | SA5, RAN1/2/3

## Slide 4: View on 6G SID Scope Content for Architecture requirements (2/4)
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4 | Network for AI | Data & Model Training: 6G exposes data (e.g., sensing, network data) for application layer model training, and supports both offloaded and distributed application layer ML model training. Inference & Deployment: 6G enables offloaded, distributed, and federated ML inference for AI/ML-based applications. | AI/ML-based applications are widely used, and 6G as the infrastructure of the future societies should facilitate the applications in data collection, training, deployment and usage steps. | SA5, SA6
5 | Sustainability | Sustainable AI/ML 6G should support sustainable AI/ML deployment 6G should exploit AI/ML as a tool to optimize energy efficiency of the network Reliable energy-related information determination 6G should supports accurate determination of energy-related information which are reliable enough for the charging purposes and credit control. | AI/ML will be integral to 6G, optimizing network operations, including energy efficiency. However, its significant energy consumption necessitates a balanced approach. While 5G provides energy-related estimations, they lack the accuracy for charging purposes. | SA5, RAN WGs
6 | Interworking with 5G | Dual registration: support UE dual registration in 6GC and 5GC network using same subscriber identifier No combo nodes in Control Plane and User Plane shared subscription information between 5G and 6G networks | Decouple 6G architecture from 5G legacy design. Such complete separation of generations, would help to enhance system efficiency, ensure a more simplified approach of network migration, and minimizes the impact when a failure occurs. | RAN3, CT1, CT3, CT4

## Slide 5: View on 6G SID Scope Content for Architecture requirements (3/4)
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
7 | Integrated Sensing and Communication | Mechanisms to support sensing result calculation and processing using In-network computing. Transport mechanisms for result calculation. Integration of sensing and computing. | ISAC's implementation is crucial for achieving lower latency in processed data availability, leading to faster response times. Resource optimization through ISAC improves network efficiency, while its inherent sustainability contributes to environmental goals. Moreover, it unlocks innovative applications such as immersive environments and digital twins. | RAN and CT WGs
8 | Access integrations | NTN System architecture design for Multi-Orbit NTN e.g., mobility management, Roaming, etc. System architecture design for Edge Computing using NTN with real-time processing System architecture design for PWS extension to use NTN and mechanism to support geo-targeted warning notifications. Indoor coverage support The 6G architecture is designed to facilitate millimetre wave coverage, especially indoors. | The proposed initiatives aim to unlock significant technological advancements such as autonomous driving capabilities, connectivity for IoT, remote area coverage, and to provide critical communication infrastructure for search and rescue and disaster relief operations. Indoor coverage small cells should be supported by the design, which is necessary for indoor coverage and utilisation of the millimetre wave spectrum. | SA3, RAN/CT WGs.
9 | IoT | Integrate support for IoT devices in the 6G system from day 1. | Migrating LTE-MTC, NB-IoT and NR (e)RedCap to a new generation enabling IoT use cases in a 6G era. | SA3, CT1

## Slide 6: View on 6G SID Scope Content for Architecture requirements (4/4)
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
10 | Robustness and resiliency | Identify potential architectural principles and study mechanisms to avoid, or lower the risk of, network failures, network modification operation mishandling, and network overload. Study mechanisms to recover from the above-mentioned incidents. | SA1 TR22.870, clause 5.4.1 Zero-Outage Network states, “significant incidents over the last four years […] affecting a vast number of users and causing disruptions in industry applications […]resulting in substantial economic losses. […] The 6G will introduce […] artificial intelligence, digital twins, and sensing, which present new challenges […] it is found that network failures, network modification operations, and network overload are the main causes.” Considering certain architectural principles (e.g., simplified core) may also be beneficial. | CT4 and CT1
11 | Network exposure framework | Study potential enhancement of overall framework to expose network capability and to allow operation from the outside. Study potential enhancement of mechanisms for obtaining necessary authorization and user consent. Study overall framework to expose network big data and to synchronize it with the external situation. Study mechanisms for low latency notification for real-time synchronization. | The network capability exposure has been recognized beneficial during 5G time. It is expected to be enhanced for 6G as well. Big data that are obtained and accumulated in the network can be a source of potential business, if it can be shared in an appropriate manner. Incorporating data of the external situation will enhance the value of the stored data. | SA6, SA3, CT3
12 | Legacy services | Legacy services (e.g. Voice, SMS, Emergency service, Priority service, etc.) | Support existing regulatory requirements in initial 6G specifications. | RAN and CT WGs
13 | RAN-Core Service Based Interface | Study whether to adopt RAN-Core interface to be service-based design. Simplifying the system architecture by combining overlapping functions in RAN and CN (mobility management, paging) | Investigation of the 3GPP-specific legacy protocol (e.g. SCTP) to replace it with virtualisation and cloud-friendly protocols. Simplifying the system architecture by combining overlapping functions; performance enhancements. | RAN3, CT1, CT3, CT4

## Slide 7: Summary
Simplified 6G Architecture: We advocate for a streamlined architecture with reduced complexity and standardized deployment options to enhance cost-effectiveness.
Open, Flexible, and Future-Proof: To maximize flexibility and prevent vendor lock-in, the 6G architecture should target cloud-friendly functionalities, built upon open and unified standards. This is particularly critical for the AI-native 6G core, ensuring seamless interoperability and a robust, vendor-neutral ecosystem.
Innovation through Advanced Services: To foster future innovation, 6G architecture should integrate features supporting novel value-added services, including AI, service exposure capabilities, and compute offloading, etc.