## Slide 1: Discussion on Remote Attestation for 5GS
3GPP TSG SA WG3 #103e
17-28 May 2021, e-meeting
Source: Johns Hopkins University APL, US National Security Agency (NSA),
CISA ECD, InterDigital, Fraunhofer SIT, CableLabs, AT&T, Verizon Wireless, NIST
Title: Discussion on Remote Attestation for 5GS
Document for: Discussion
Agenda Item: 5.16
S3-211465

## Slide 2: Key Issue #1.2 Processing of Tampered Data
5GS using AI/ML-based analytics are subject to attacks involving tampered data.
Threats
  Adversarial examples as inputs leading to severe performance degradation, misclassifications, misinterpretation
  Tampered training data leading to model skewing
  Tampered data leading to information disclosure of proprietary AI/ML algorithms
Security Requirements
  A 5GS analytics function shall be protected from processing unsanitized or tampered data
With NFs distributed across multiple cloud infrastructures, NFs may behave in an undefined manner.
Threats
  Anomalous/malicious NF behavior could access unauthorized services, consume resources, trigger DoS attack
  NFs with internal data corruption, configuration errors, etc. could cause damage to UEs
  Erroneous NF may knock a network out of service
  If the NF is misconfigured or has internal data corruption, etc., the assumption of trust becomes invalid and causes potential threats
Security Requirements
  It should be possible for network to detect anomalous NFs using data collected from UE & NFs
Key Issue #2.2 Anomalous NF behavior detection by NWDAF

## Slide 3: Proposed Solution: Remote Attestation
Attestation is when a device creates a claim about its properties and provides believable evidence of that claim to prove its veracity.
Remote Attestation is when a device makes that claim to a remote party.
Attestation can assert:
  The device has the correct hardware and software, and configuration data.
  The device is in a valid state
Attestation
A device collects claims, such as cryptographic hashes or other integrity measurements, describing the state of its hardware and software. Evidence is generated from these claims to assert that a device was in an intended operational state at that time.
Evidence can describe:
  System software on “disk” (BIOS, hypervisor, OS kernel, container management software, etc.)
  System software in memory
  Baseband software
  Hardware configuration
Evidence
Remote attestation relies on a trusted environment on the device. A Trusted Environment is a separate protected domain capable of collecting claims about and taking measurements on the untrusted environment. It typically uses key material and cryptographic functions to vouch for the authenticity of evidence and to bind it to a particular device.
Services of Trusted Environment:
  Integrity measurement and reporting
  Integrity-protected storage
  Confidential storage
Trusted Environment
Remote attestation allows a system to assess the evidence of an attester to infer its trustworthiness

## Slide 4: Remote Attestation Architecture
Performs integrity measurements and builds a set of believable claims, called Evidence. Evidence is sent to the Verifier to assert that the Attester is trustworthy. Evidence may include claims about configuration, software, hardware, etc.
Attester
Requests evidence and appraises the validity of claims in that evidence from the remote attester. The Verifier may compare claims in evidence against reference values or apply more complex logic specific to implementations.
Verifier
Protected resource that depends on attestation results to decide the extent to which it will interact with the attested device. The Verifier and Relying Party roles may be collocated.
Relying Party
Trusted Environment
Attester
Target of Remote Attestation
Verifier
Request
Evidence
Relying
Party
1
3
4
Attestation Results
Measurements
2
Untrusted Environment

## Slide 5: Remote Attestation Integrated with Framework for 5G Network Automation
Example Use Case: NWDAF Attests Trustworthiness of NF
Attester
Verifier
Relying Party
Verifier can be collocated with Relying Party or stand-alone
General Framework from 3GPP TR 23.791
NWDAF verifies the integrity of the internal hardware, software, or configuration state of the system hosting the NF instance using remote attestation.
KI #1.2
If there is a discrepancy with the evidence, the attestation results will indicate a non-trusted system, and the NWDAF should not collect or process data from the NF.
KI #2.2
NWDAF can use the attestation results and evidence as input data into the analytics function to support detecting anomalous NF behavior.
Attestation Roles
2
1
Request
2
Measurements
Evidence
3
Attestation Process
Attestation Results
4
Delivery of activity data & local analytics
AF
OAM
Data
Access
NWDAF
Delivery of
analytics data
Data
Repositories
NF
NF
1
3
4
AF

## Slide 6: Market Survey of Attestation Environments
Component Type | Attestation Environments | Example Properties to Attest
User Endpoint | ARM TrustZone Secure World, Global Platform Trusted Execution Environment, Trusted Platform Module | Firmware loader, OS loader, OS images, Secure OS, any critical application images
 |  | Software in memory
 |  | Hardware configuration
 |  | Baseband firmware
Servers hosting Network Functions | Trusted Platform Module | BIOS, OS images, container platforms, images of any critical application or other system software
 |  | Software in memory
 |  | Hardware configuration
Virtual Machines hosting Network Functions | Trusted Platform Module | BIOS, Hypervisor, hardware configuration, software in memory
 | Virtual Trusted Platform Module | Virtual BIOS, OS Images, images of any critical application or other system software
There is no limit or requirement on attestation environments or the properties that can be attested

## Slide 7: Conclusions
Remote Attestation is flexible and can be deployed in a way that aligns with various 5G Network Automation deployments
Remote Attestation provides ability for NWDAF to interrogate NFs for evidence of its trustworthiness before collecting data to defend against processing tampered data (KI# 1.2)
Evidence and Attestation Results can be used as input data for AI/ML analytics to aid NWDAF with detecting anomalous NF behavior (KI# 2.2)