## Slide 1: Virtual Resource Isolation for Applications in 5G network
Jing Ping
Nokia

## Slide 2: Background
5G will be able to support extreme and diverse requirements for throughput, latency, availability, capacity. Security is another fundamental network requirement that needs to be optimized for each specific use case, especially for those uses cases where security becomes critical (e.g., V2X platooning, enterprise VPN or Electric grids).
Operator allocates 5G network resources to vertical/enterprise customers to support various use cases and applications, the resource can be isolated from networks or network resources used by other cellular customers.
Network slicing is a key feature and business driver for 5G, which enables enterprises and operators to address specific requirements of different market segments (e.g., industrial, smart cities, healthcare, automotive). The overall security architecture of 5G network is enhanced with new security features, available as well in network slices as logical networks created within the 5G network.

## Slide 3: Motivation – business requirements
A business wants to have a secure and isolated set of network capabilities that meets its communication needs, without having to purchase and maintain the network infrastructure. In this case, a mobile network operator can use network slicing as a means to provide a virtual private network, or private slice, for the enterprise.
Isolation is a multi-faceted problem, on security dimensions, it’s ensuring that any type of intentional attack occurring in one collection of network functions /resources have no impact on any other network functions/resources;
Slice security isolation is a security feature, as it separates slice related data and activities of different customers. With the corresponding slice specific enforcements slice security isolation can prevent unauthorized access and modification to data, processes, services or functions.
DU
UPF-1
SMF-1
uRLLC
USER PLANE
CONTROL PLANE
UPF-21
SMF-2
mIoT
AMF-1
S-NSSAI#21
UE#2
S-NSSAI#22
eMBB
CU-CP RRC/PDCP-1
CU-UP-21
CU-UP-1
S-NSSAI#1
UE#1
AMF-2
CU-CP
RRC/PDCP-2
CU-UP-22
UPF-22
Enterprise A
Enterprise B
Virtual resource isolating expectation for applications in 5G network - horizontal

## Slide 4: Motivation – operation requirements
Operator allocates 5G network resources to vertical/enterprise customers to support various use cases and applications, the resource can be isolated from networks or network resources used by other cellular customers.
The network resources are isolated from logic network layer (e.g. network slice), a set of NFs/resource layer (e.g. network slice subnet, or network slice instance), virtualization layer (e.g. VNF, CNF), physical layer (e.g. physical server, RF)
Virtual resource isolating expectation for applications in 5G network - vertical

## Slide 5: Motivation – gaps and problems
A UE may select an unexpected logical/virtual network for an application based on local configuration, or outdated URSP, that causes the isolation requirements of vertical cannot be satisfied even network and resource isolation are implemented in 5G network side
Compromised or malicious UE may misuse slice and intentionally steer security sensitive application to “lower secured” slice hence steal application data, or steer low security and priority application to high priority slice, and may cause DoS on the target slice.
Issue #1: Unexpected logical network is selected for a vertical application
DU
UPF-1
uRLLC
USER PLANE
CONTROL PLANE
UPF-21/22
SMF
mIoT
S-NSSAI#21
UE
S-NSSAI#22
eMBB
CU-UP-21/22
CU-UP-1
S-NSSAI#1
AMF
CU-CP
eMBB
uRLLC/mIoT
Expected
Actual
Enterprise A
Enterprise B
X
X
X

## Slide 6: Motivation – gaps and problems
As shown in the right figure, the operator allocates logical/virtual network (e.g. identified by S-NSSAI#1) to Enterprise A for its uRLLC service and allocate logical network S-NSSAI#21 and 22 to Enterprise B for its mIoT and eMBB services. According to customer security requirement and operator policies, operator isolated resource of S-NSSAI#1 from resource of S-NSSAI#21/22. The operator and Enterprise A expected application traffic for the uRLLC service will route to dedicate resource for S-NSSAI#1.
However, as mis-behavior of the UE, logical network S-NSSAI#21 may be selected to transmit traffic of the uRLLC service, and the application data maybe leaked to NFs (e.g. CU-UP, UPF, etc.) of other resource group, which may even be outside the campus of the Enterprise A. That may violate security and other SLA of Enterprise A, operator policies and regulation. If S-NSSAI#21 support only DNN for enterprise B, the uRLLC traffic from UE even cannot reach the uRLLC server, and DoS may be triggered.
Issue #1 example: Unexpected logical network is selected for a vertical application
DU
UPF-1
uRLLC
USER PLANE
CONTROL PLANE
UPF-21/22
SMF
mIoT
S-NSSAI#21
UE
S-NSSAI#22
eMBB
CU-UP-21/22
CU-UP-1
S-NSSAI#1
AMF
CU-CP
eMBB
uRLLC/mIoT
Expected
Actual
Enterprise A
Enterprise B
X
X
X

## Slide 7: Motivation – gaps and problems
As shown in right figure, operator may allocate virtual network and network resource to specific vertical applications with using network slicing, and expect the resources are isolated for application based on corresponding policies and existing isolation solutions in network, e.g. slice aware access control for SBI based 5GC, select right CP or UP NFs considering S-NSSAIs, etc.
However, as lack of coordination between management and network layers, the isolation policies may not be correctly provisioned on NFs, so all isolation solution in control plane may not take effective. E.g. management plane expects isolate resources of apps in purple from apps in yellow and green, but incorrectly configured NSI and S-NSSAI in NFs as lack of standardized information model, which cause the NFs in yellow can access NF Services of NFs in purple.
Without appreciated isolation, a compromised or malicious low security profiled slice may impact a highly sensitive slice, e.g. steal services/resources and data of mission critical applications.
Issue #2: Unexpected isolation in network resource layer

## Slide 8: Motivation – gaps and problems
SBI and virilization technologies are applied in 5GC network, all NFs in the core network (e.g. (AMFs, SMFs, UPFs, etc.) may share common infrastructure and deployed as VM or container.
As shown in right figure, operator may allocate virtual network and network resource to specific vertical applications with using network slicing, and expect the resources are isolated for application based on corresponding policies and existing isolation solutions in network. However, as lack of coordination between 3GPP system and cloud/virtualization system, the VNF/CNF serving different application may not be correctly isolated in virtualization and physical layers. It’s even worse for partially sharing/isolating resources case (e.g. sharing some NFs but isolated others), and MEC scenario where operator’s NF may deploy with applications of verticals.
Without proper isolation and security control in cloudified environment, sensitive data of one network slice could be exposed to network functions running in other network slices through side channel attacks, although the access control is correctly performed on SBI based 5GC network.
Issue #3: Unexpected isolation in virtualization resource layer

## Slide 9: Motivation – gaps and problems
As shown in right figure (one UE with multiple allowed slices), two CU-UPs are deployed to isolate UP data of slice#2 from slice#3&4. The slice#2 may be less security sensitive and the CU-UP-1 may be provided by another vendor or deployed in different edge cloud with less protection, then it can be attacked and compromised or itself may be malicious. Currently, as same AS security context is shared by all allowed slices, the attacker may use AS keys stole from CU-UP-1 to intercept UP traffic of slice#3&4 even CU-UP-2 is deployed separately and well protection. The attacker may also fake DL UP traffic by integrity protecting the traffic with stolen keys (this kind of active attack could be more difficult and need further investigation). .
Issue #4: Unexpected isolation at Uu interface
DU
MAC
PHY
S-NSSAI#2
S-NSSAI#3
UE ATTACHED TO MULTIPLE SLICES
S-NSSAI#4
RLC
CU-CP
RRC
PDCP
RRC2
RRC3
RRC4
CU-UP-2
PDCP
SDAP
PDCP
SDAP
CU-UP-1
PDCP
SDAP
S-NSSAI#2
UE#1
S-NSSAI#3
S-NSSAI#4
UE#1

## Slide 10: Motivation – gaps and problems
As defined in TS 33501, two PLMNs can decide either to use PRINS or TLS between them. It is based on the operator policy. If we use the PRINS protocol, then IPXs can modify the data or can read the data between the PLMN. If we use TLS between the SEPPs, then IPXs can not read the data. Currently N32 traffic is not segregated per slice. Therefore, if a specific slice does not want IPX to modify or read the data, then it is not possible because N32 connections are not slice-specific.
This limitation leads to a problem where if a business demands that Slice-X data should not be read by IPXs, then whole N32 traffic needs to be diverted over an TLS then IPX loose the visibility and business use case on the non slice specific data
Issue #5: Unexpected isolation at N32 interface

## Slide 11: Motivation – gaps and problems
Issue #6: Unexpected interference at transport layer
Step 1
Step 2
Step 3
Step 4

## Slide 12: Objectives
Study how to enable verticals, operators and cloud service providers to address diverse requirements of different market segments for security and isolation, and to holistically investigate the gaps in existing specification and collect potential solutions to enforce resource isolation for applications in 5G network.
Investigate the gaps of existing specification on correctly logical network selection for vertical applications.
Investigate the gaps of existing specification on network and virtualization resource isolation and protection for vertical applications.
Investigate the gaps of existing specification on transport (e.g. Uu, N32, N3 interfaces) isolation and protection for vertical applications.
Collect potential solutions to fulfil differentiated security SLA of enterprise applications and enforce resource isolation for applications in 5G network, hence satisfy the security requirements of various business cases from different industries and improve compliance with industry regulatory and business requirements.