## Slide 1: Proposal of “WebRTC with Operator’s Assistance”
Dec. 15, 2021
NTT

## Slide 2: Benefits of WebRTC with Operator’s Assistance
WebRTC
Client
Operator A
i) To IMS
iii) OTT To Other Operators
IMS
Client
WebRTC
Entities
Interworking
WebRTC with operator’s termination and assistance:
  Can connect to IMS clients,
  Can connect to other operator’s clients if NNI is specified,
  OTT WebRTC clients can also connect to other operator’s clients.
ii) To Other Operators
IMS
Entities
WebRTC
Client
Operator A
WebRTC
Client
WebRTC
Entities
WebRTC
Entities
Operator B
NNI
OTT WebRTC
Client
Operator A
WebRTC
Client
WebRTC
Entities
WebRTC
Entities
Operator B
NNI
OTT
OTT’s
WebRTC
Entities
NNI
en

## Slide 3: WebRTC Non-Browser Clients and C-Plane Definition
We propose considering “WebRTC Non-Browser” clients, which can provides better QoE than browser clients.
WebRTC C-Plane signalling needs to be specified for that purpose.
When WebRTC C-Plane signalling is specified, the native application or conference appliance can be connected to any 3GPP operators.
 |  |  | Location of Servers (e.g. Signalling server, ICE server) | 
 |  |  | In OTT’s NW | In operator’s NW (Operator-Assist)
Client (Terminal) | WebRTC Browser |  | 3GPP Northbound API | TS24.371 (WebRTC access to the IMS)
 | WebRTC Non-Browser*1 | Dedicated for a Specific Service Provider |  | Needs additional Standardization of C-Plane
 |  | Universal for multiple Service Providers | Mostly Out of Scope | 
(*1) Described as “WebRTC device” or “WebRTC native application” in RFC8825
- Use case of WebRTC and Status of standardization -
en

## Slide 4: Summary
Specifications relevant to WebRTC technology or WebRTC services are already there.
  TS24.371, Web Real-Time Communications (WebRTC) access to the IP Multimedia (IM) Core Network (CN) subsystem (IMS); Stage 3; Protocol specification (since Rel-12)
  3GPP Northbound APIs
They give enough hints to realize the cases, where an operator supports WebRTC indirectly (via eP-CSCF or JavaScript).
An unexplored case is to support WebRTC directly. We call it WebRTC with Operator’s Assistance.
It provides more connectivity and better QoE.
It may provide another chance for operators and OTTs.
WebRTC with Operator's Assistance (which involves WebRTC C-plane and NNI) should be studied.