## Slide 1: Streaming Media Test Suite – Devices Explained

## Slide 2: Summary
The WAVE Project has launched its initial “WAVE Streaming Media Test Suite – Devices” to enable automated testing of web-based media playback on various devices like Smart TVs, media sticks, smart phones, laptops and set-top boxes.
This suite aims to streamline testing processes by allowing device implementers to prove compatibility with industry standards, reducing repetitive tests across the industry.
It features unit tests for media using CMAF formats and web streaming technologies like MSE and EME. The suite also includes preliminary tests for popular video and audio codecs, with plans to expand codec testing in 2024.

## Slide 3: What?
Tests for AVC video playback using MSE and EME (21 validated 'primary' tests)
  Each test is the combination of an HTML+JavaScript template with CMAF test content
  Duplicate tests for 25 / 50 Hz, 30 / 60 Hz and fractional frame rates
  Primarily AVC profile/level 4.0 ('cfhd') but includes level 4.2 ('chdf') for 1080p50/60
  Also some 'beta' tests that are still in validation
    Total = 46 tests (25/50) and 39 tests (for each of 30/60 and fractional frame rates)
Test Runner
  Based on Web Platform Test (WPT) test runner
    Also used by CTA WAVE 'Web Media API Snapshot' (WMAS) tests
    Packaged as a docker image
    Documentation extensively reviewed and improved in last 12 months
Observation Framework
  Analyzes recordings made from running tests on devices for compatibility with MSE spec and CTA-5003 Device Playback Capabilities Specification

## Slide 4: Why?
Improve inter-operability between apps and devices for media presentation using web APIs
  Strongest contributor interest is Smart TVs
Reduce combinatorial explosion of testing between apps and devices
  Enable device implementers to test once and present results to content providers / platforms
Improve viability of web as a format for media apps

## Slide 5: System Components
Applying
Annotations
Raw
Content
Encoding
CMAF Test
Content
Mezzanine
Content
Test Generation
HTML + JS
Test Templates
Tests
(HTML + JS + CMAF)
Run on Device under Test via Test Runner
Record Test Session on Device under Test
Analyze Recording via Observation Framework
Test Report (HTML, JSON)
Recording of tests
WAVE Streaming Media Test Suite -- Devices
Device Test Process

## Slide 6: How It Works: Annotated Mezzanine Content
Annotated video content in many different resolutions
  Based on big buck bunny for 60Hz and fractional frame rates & an EBU sequence from Croatia for 50Hz.
  Green frame on the start and red frame on the end.
Annotations burnt into the video
  Rotating QR code for observation framework.
  Human-readable text for debugging.
    Same information as in the QR code.
  Bit pattern for TV manufacturer in-house use.
  Flashing square with beeps for simple A/V sync testing.
  Red triangles to check all content is visible.
See next slide for example.
Audio content based on pseudo-random noise.
  Observation framework can reconstruct a timeline from this.

## Slide 7: Mezzanine Content

## Slide 8: CMAF Test Content
Encoded & validated mezzanine content.
  CMAF media segments (or is it fragments?).
  Metadata describing media segments provided in the form of a DASH MPD.
4 groups of streams encoded for each technology
  Testing combinations of content options.
  Testing content options individually for debugging.
  Resolutions for testing CMAF switching sets.
  Special content for testing splicing, encryption, ...
For each codec, streams to encode are defined in a sparse matrix.
  Examples for AVC video on next slides (based on what is just released).
Validation in two phases
  DASH-IF aka ‘JCCP’ validator checks the content is valid CMAF.
  Script reads in the sparse matrix & checks each stream has the correct content options, resolution, cmaf profile and other properties.

## Slide 9: HTML and JavaScript Templates
Media codec / technology independent
  Exercise MSE (and EME) playback.
  Algorithms documented in clauses 8 & 9 of WAVE Device Playback Specification.
  Common library that reads and plays CMAF content based on metadata in DASH MPD.
Mixture of templates for either video or audio or for both video+audio.
Examples
  Sequential Track Playback
    Play a CMAF video or audio track from beginning to end.
  Random Access to Fragment, Random Access to Time
    Play a CMAF video or audio track from somewhere in the middle.
  Switching Set Playback
    Play a CMAF switching set, switching between tracks at various points.
  Playback over WAVE Baseline Splice Constraints
    Playback switching from one CMAF track to a second and back again.
  Buffer Underrun and Recovery
    Playback terminating.

## Slide 10: Test Generation
Sparse matrix that defines test content to encode also defines combinations of HTML+JS templates to use with test content.
Script copies templates and inserts URLs for MPDs.

## Slide 11: Tests (1); Validated Primary Tests
buffer-underrun-and-recovery__t2 | random-access-to-fragment__t1
fullscreen-playback-of-switching-sets__ss1-1 | random-access-to-time__t1
fullscreen-playback-of-switching-sets__ss1-2 | regular-playback-of-chunked-content__chunked
low-latency-initialization__t2 | regular-playback-of-chunked-content-non-aligned-append__chunked
low-latency-short-buffer-playback__t2 | restricted-splicing-of-encrypted-content-https__splice_main-cenc_splice_ad-cenc
mse-appendwindow__t1 | sequential-playback-of-encrypted-and-non-encrypted-baseline-content-https__splice_main-cenc_splice_ad
out-of-order-loading__t1 | sequential-track-playback__t1
overlapping-fragments__ss1 | sequential-track-playback__t3
playback-of-encrypted-content-https__t1-cenc | switching-set-playback__ss1-1
playback-over-wave-baseline-splice-constraints__splice_main_splice_ad | switching-set-playback__ss1-2
random-access-from-one-place-in-a-stream-to-a-different-place-in-the-same-stream__t2 | 
These are the tests that would be referenced by a content / service provider when requiring devices to pass the CTA WAVE test suite.

## Slide 12: Tests (2); Secondary Tests for Debugging Content Options
Test | Content option tested
sequential-track-playback__t10 | Same as t1 but with only picture timing SEI message different.
sequential-track-playback__t11 | Same as t1 but with only VUI timing different.
sequential-track-playback__t12 | Same as t1 but with different sample entry type.
sequential-track-playback__t13 | Same as t1 but with 3rd possible sample entry type.
sequential-track-playback__t14 | Same as t1 but with only CMAF fragment duration different.
sequential-track-playback__t15 | Same as t1 but with only initialization constraints different
Streams for primary tests
t1 = baseline set of content options
t2 = all content options different from t1
t3 = for content options with 3 possible values, content options different from t1 and t2
If there are problems playing t2 or t3, these secondary tests can be used to isolate which content option is causing the problem.

## Slide 13: Tests (3); Secondary Tests for Debugging CMAF Switching Sets
Test | Resolution & Frame Rate
sequential-track-playback__t20 (chdf) | Same as t1 but 1080p50/60 instead of 1080p25/30.
sequential-track-playback__t21 | Same as t1 but 1600x900
sequential-track-playback__t22 | Same as t1 but 1280x720
sequential-track-playback__t23 | Same as t22 but 720p50/60 instead of 720p/25/30.
sequential-track-playback__t24 | Same as t1 but 1024x576, higher bitrate
Not generated | Same as t1 but 1024x576 lower bitrate
sequential-track-playback__t26 | Same as t1 but 960x540
sequential-track-playback__t27 | Same as t1 but 852x480
sequential-track-playback__t28 | Same as t1 but 768x432.
sequential-track-playback__t29 | Same as t1 but 720x404
sequential-track-playback__t30 | Same as t1 but 704x396
sequential-track-playback__t31 | Same as t1 but 640x360
sequential-track-playback__t32 | Same as t1 but 512x288
sequential-track-playback__t33 | Same as t1 but 480x270
sequential-track-playback__t34 | Same as t33 but half frame rate

## Slide 14: Tests (4); Beta tests for video and video+audio
AVC without audio
  truncated-playback-and-restart__splice_main_splice_ad
  long-duration-playback
AVC with audio
  random-access-of-a-wave-presentation__t1_at1
  regular-playback-of-a-cmaf-presentation__t1_at1

## Slide 15: Tests (5); Secondary Tests for Debugging CMAF Switching Sets
CMAF media profile 4CC | Description | #
ca4s | AC-4, single stream | 11
caaa | Adaptive AAC core | 3
caac | AAC core | 15
camc | AAC multichannel | 2
ceac | Enhanced AC-3, including AC-3 | 11

## Slide 16: Test Runner
Extended version of test runner used for ‘Web Platform Tests’
  Device Under Test loads HTML page from the test runner.
  Test operator connects to test runner with desktop or mobile browser.
Test operator configures a session by selecting one or more groups of tests.
  Based on CMAF media profile and/or use by HbbTV.
  Filtered by validated or beta (see later) or long duration.
Device runs the session controlled by the test runner.
  Results and debug output saved to the test runner.
See next slide for screen shot.

## Slide 17: Test Runner UI for Session Configuration

## Slide 18: Installer
Creates two docker images, one with test runner and one with observation framework.
Can be run on Windows with Docker Desktop
  Commercial product, not free to use in larger organizations.
Can be run on Unix-like systems
  Linux, Mac, Windows with WSL2 (without Docker Desktop)
Installation needs someone who knows what they’re doing with docker, IP routing, TLS server certificates, ...
  Either someone from IT or a local power user.
  Ensuring the test runner can talk to the Device Under Test and to the Observation Framework is not straightforward in some configurations.

## Slide 19: Camera
Recording & analysing 50/60Hz video playback needs camera recording at 120Hz
  Validation done with top of the range mobile phone, e.g. Samsung S23+ or equivalent
    Care needed as phones may have issues with adequately obtaining audio from TV.
Avoiding reflections and glare when setting up camera is very important
  Otherwise, Observation Framework will fail to extract QR codes
Recording made to local memory card.
  Downloaded to PC by moving the memory card across
Experiments can limit video <= 30Hz and use cheaper cameras.
Investigations in progress on streaming from camera to test runner.
  Cameras likely to be more expensive professional equipment.
  Mobile phone video streaming typically has limitations compared to recording on memory cards.

## Slide 20: Observation Framework
Processes recordings from the camera and reports results to the test runner.
  Results are merged into the results from when the test was actually run.
Two steps
  Extraction of QR codes from the recording.
  Processing of data from QR codes against test procedures in the WAVE Device Playback Specification (CTA-5003).
OF can be run on the same device as runs the test runner or a different (faster) device.
  OF can be installed either as a docker image or directly.
OF generates log files and debug output for developers to analyze when a device is reported as failing.

## Slide 21: Example of Failing Observations
From https://github.com/cta-wave/dpctf-tests/issues/152

## Slide 22: Debugging a Failing Test
Start your favorite video editor, go to the frame number from the log files and step through.
Record what happens at what frame number (e.g.)
Has the OF correctly failed the recording according to the test procedure?
Is the test procedure wrong?
Is the device wrong?

## Slide 23: System Validation
Tests run on Smart TVs at HbbTV interop event / plugfests.
  June, October 2023 and January 2024.
January 2024 used 8 different TVs from different manufacturers.
  Prioritized three best TVs from those eight.
Final regression tests based on TVs from two of those three manufacturers.

## Slide 24: Example Errors Found by this Test Suite
Dropped frames in the middle of content, either
  Media timeline is preserved, one frame persists during the period of the dropped frames.
  Media timeline is not preserved, period of the dropped frames is cut out of the media timeline, frames persist for their expected time.
Dropped frames at the start and end of the content.
  Either no video is shown, or broadcast video is shown in the case of a Smart TV.
Media timeline stalls.
  Media timeline just stops advancing for some period.
Errors with JavaScript currentTime property relative to displayed video.
  Either drift or currentTime continuing to increment after video playback has stopped.
  Likely results in loss of sync between subtitles / captions and video.
Seeking starts playback from the wrong location.
Failure to restart after buffer underflow.

## Slide 25: Give It a Try
Instructions at https://github.com/cta-wave/dpctf-deploy/tree/v2.0.0
Successfully used with four host configurations
  Linux (primary supported host environment)
  Windows using WSL2 (almost the same as Linux)
  Mac (almost the same as Linux)
  Windows using Docker Desktop commercial product
    Note "Commercial use of Docker Desktop at a company of more than 250 employees OR more than $10 million in annual revenue requires a paid subscription (Pro, Team, or Business)."
Three phases
  Deployment (one-time action, to be performed with support from IT personnel or power users)
    Note it is possible to get yourself tied in knots between virtualization systems unless done by someone who knows about Docker and IP routing between LAN, host and docker instances
    Note doing this 'for real' requires a TLS server certificate which may be a challenge in a company network. It needs to be done by someone who knows what they're doing.
  Test execution and recording
  Observation

## Slide 26: Acknowledgements
Romain Bouqueau (Motion Spell) with support from Qualcomm and CTA
Nicholas Frame, Jon Piesing (TP Vision)
Louay Bassbouss, Fritz Heiden, Martin Lasak, Ilja Gavrylov (Fraunhofer FOKUS) with support from CTA
Yan Jiang, Richard Cottingham, Peter Shorrock (Resillion) with support from Dolby, Fraunhofer IIS, CTA
Thomas Stockhammer (Qualcomm)
Zachary Cava (Walt Disney Co.)
Mike Bergman, Bill Rose, Alexandra Blasgen (CTA)

## Slide 27: Thank you