## Slide 1: 3GPP Service URLs
Thomas Stockhammer

## Slide 2: Baseline – Third-party Service Over-the Top
5GS
UE
Typical setup
Application #1 Content Guide/Web page/etc
Media Service
Provider
5G Modem + IP stack
UPF
Media service entry point
Application #2 Media Service
Portal Application Provider
IP
IP

## Slide 3: Automatic Launch of UE apps: Android App Links
Android App Links’ allows using a URL to launch a specific application on the device – but the App Link needs to be for a specific app and needs to be registered with the app manifest.
Android App Links leverage HTTP URLs and association with a website
  users who don't have the app installed go directly to content on your site.
Different types of links
  Deep links are URIs of any scheme that take users directly to a specific part of your app. To create deep links, add intent filters to drive users to the right activity in your app.
  Web links are deep links that use the HTTP and HTTPS schemes. On Android 12 and higher, clicking a web link (that is not an Android App Link) always shows content in a web browser.
  Android App Links, available on Android 6.0 (API level 23) and higher, are web links that use the HTTP and HTTPS schemes and contain the autoVerify attribute. This attribute allows your app to designate itself as the default handler of a given type of link.
iOS also has something similar – details to be checked
https://developer.android.com/training/app-links

## Slide 4: Call Flow (1)
Over the top third-party service
may leverage App Links

## Slide 5: Background
3GPP SA4 has looked now into a couple of cases where we attach a third-party service to use additional 5G System functionalities, either as supporting functions or as essential functions.
Examples:
  DASH/HLS Service + using MBMS User Services
  DASH/HLS Service + using 5G Broadcast Services (i.e. MBMS ROM)
  DASH/HLS Service + using MBS User Services
  DASH/HLS Service + using 5G Media Streaming functionalities
  XR Service using 5G Edge Enablers
The third-party service may be served/supported through a 5G system
In order to do so, a dedicated client function needs to be initialized in order to carry out specific functions

## Slide 6: Availability of 5G System functions
5GS
UE
Open Question – how can these functions on the UE and network be established?
Application #1 Content Guide/Web page/etc
Media Application
Provider
Dedicated 5GS UE Functions
Dedicated 5GS Network Functions
AF/AS
Media service entry point
Application #2 Media Application
Portal Application Provider
5G Modem + IP Stack
UPF

## Slide 7: Examples for dedicated UE/network functions
MBMS client (UE) and BMSC (see TS 26.346 and TS 26.347)
MBS client (UE) and MBSF/MBSTF (see TS 23.247, TS 26.501, TS 26.512)
Media Session Handler (UE) and 5GMS AF (see TS 26.501, TS 26.512)
  Consumption Reporting
  Metrics Reporting
  Dynamic Policies
5G Broadcast Receiver (UE)
Edge-enabling client (UE) and Edge Application Server

## Slide 8: Launching a dedicated 5G System function on device
Unclear how this can happen consistently

## Slide 9: Problem Statement and Options
Option 1: An API is created to the device function and the application initializes the function through these APIs – this is for example what TS 26.347 assumes
  Problem: the application on the device needs to have specific provisioning to establish this function
  Unlikely to be broadly available
Option 2: Using non http-URL as an Entry Point that resolves the link by specific handling
  This option is for example done for MBMS User services in TS 26.347
  The URL contains sufficient information to access service
  However, the problem here is that the URL is not automatically handled by the HLOS (e.g. Android) or browser
Option 3: Using a http/https-URL as an Entry Point that triggers some specific actions
  This allows that the service can be accessed by the user “clicking” or by attaching it to some portal and on.
  If Android for example sees a text message that has a URL, it gets interactive
  Once you have executed this click, the service bootstraps by setting up the appropriate 3GPP functions and connects to the network
How can option 3 (and possibly option 2 to some extent) be executed and implemented
How does the third-party application wake up the supporting dedicated 5GS function

## Slide 10: Progressing Option 3
The main issue is now, that you want to consult a UE-resident URL handler/resolver that bootstraps the service URL and does all the appropriate actions, for example
  enables the MBMS reception,
  sets up a 5G media streaming session (MSH – AF) and so on.
  In one specific case at least, for the MBMS ROM service, you want this to be done only on the device.
Basic idea: specify 3GPP defined http URLs that
  execute this service boot strapping.
  With a basic function on the device to support
    some pre-installed functions (like ROM).
    To support launching device functions
  Allow additional network functions to support the resolution of the service URL, for example go to a specific AF providing more service-related information and launching network functions
Until now, 3GPP has been avoiding the detailed question on how to bootstrap and deferred such aspects to implementation, device pre-configuration, and so on.
How can a 3GPP specific function get into the way?

## Slide 11: Proposal: 3GPP Service and URL Handler
5GS
UE
Adding a new set of functions that bootstraps the service launch
Application #1 Content Guide/Web page/etc
Media Application
Provider
Dedicated 5GS UE Functions
Dedicated 5GS Network Functions
AF/AS
Application #2 Media Application
Portal Application Provider
5G Modem + IP Stack
UPF
3GPP Service Handler UE
3GPP Service Handler Network
URL with 3GPP Service parameters (and media service entry point)
1
2c
2a
2b

## Slide 12: Basic principles – three different cases
Case 1: Network-only resolution
  URL is constructed, such that it is resolved in a dedicated 3GPP network function
  Service URL resolves to network function that triggers some support function in network
  Network returns entry point URL to media service
  Media service application is launched based on URL, for example using App Link functionality
Case 2: Device-only resolution
  URL is constructed to include service, service parameters and media entry point URL
  In this case, the 3GPP service URL triggers the handling of the URL by
    Launching of the dedicated 5G System functions based on the URL parameters
    Launching of the media service provider app using the the URL provided as part of the entry point URL
Case 3: Device + Network resolution
  URL is constructed to include service information as well as possibly service parameters and media entry point URL
  In this case, the 3GPP service URL triggers the handling of the URL by
    Communicating with the network function to establish functions in the network (possibly getting additional service parameters and media entry point URL)
    Launching of the dedicated 5G System functions based on the URL parameters in the UE
    Launching of the media service provider app using the the URL provided as part of the entry point URL
Overview

## Slide 13: 1: 3GPP Service and URL Handler – Network-only solution
5GS
UE
In a simple way, if no handler is available on device, the URL resolves to a 3GPP network function
Application #1 Content Guide/Web page/etc
Media Application
Provider
Dedicated 5GS Network Functions
AF/AS
Application #2 Media Application
Portal Application Provider
5G Modem + IP Stack
UPF
3GPP Service Handler Network
URL with 3GPP Service parameters (and media service entry point)
1
2
3
4

## Slide 14: Call flow network only solution
The network is triggered to launch specific 5GS functions, and redirects portal to media app

## Slide 15: 2: 3GPP Service and URL Handler – Device only resolution
5GS
UE
Adding a new set of functions that bootstraps the service launch
Application #1 Content Guide/Web page/etc
Media Application
Provider
Dedicated 5GS UE Functions
Dedicated 5GS Network Functions
AF/AS
Application #2 Media Application
Portal Application Provider
5G Modem + IP Stack
UPF
3GPP Service Handler UE
3GPP Service Handler Network
URL with 3GPP Service parameters and media service entry point
1
2a
2b

## Slide 16: Call flow UE only solution
Service handler on UE uses information to wakeup dedicate function and initiated Media Service Application

## Slide 17: 3: 3GPP Service and URL Handler - Device + Network resolution
5GS
UE
Adding a new set of functions that bootstraps the service launch
Application #1 Content Guide/Web page/etc
Media Application
Provider
Dedicated 5GS UE Functions
Dedicated 5GS Network Functions
AF/AS
Application #2 Media Application
Portal Application Provider
5G Modem + IP Stack
UPF
3GPP Service Handler UE
3GPP Service Handler Network
URL with 3GPP Service parameters (and media service entry point)
1
2c
2a
2b

## Slide 18: Call flow UE + Network resolution
The service handler collects addititional information and then the same as UE only

## Slide 19: Potential Solution for Services: 3gpp-service URLs
Create a URL for 3GPP Services as part of 3GPP specifications, e.g. 3gpp-services.com
  Verify ownership of the domain through one of the Android website association methods.
  Create a web site/redirection mechanism in case the application is not available on the device
  The URL itself needs to be sufficiently unambiguous to resolve to the main service and may include the URL to the main service as well
Install or create an app that includes an intent-filter to act as the default app for the handler
  DEFAULT category: to allow your app to respond to implicit intents.
  BROWSABLE category: required in order for the intent filter to be accessible from a web browser. Without it, clicking a link in a browser cannot route users to your app.
  The <data> tag must include the android:scheme and android:host attribute
Verify ownership details see here
This predominantly addresses case 2 and 3 for a UE based handler
<intent-filter android:autoVerify="true"> <action android:name="android.intent.action.VIEW" /> <category android:name="android.intent.category.DEFAULT" /> <category android:name="android.intent.category.BROWSABLE" /> <data android:scheme="http" /> <data android:scheme="https" /> <data android:host=“3gpp-services.com" /> </intent-filter>

## Slide 20: Set of actions and call flow
  Device may install a background app that is deep-linked to an Android app addressing 3GPP services
  Media Application provider has a service with an entry point URL
  Media Application provider negotiates all service parameters with the 5GC
  Media Application provider creates a bootstrapping URL (much like a landing page URL)
    http://3gpp-services.com/<service parameters>/<URL to application service>
  Media Application provides
    Only the 3GPP Service URL to a portal provider, search engine, etc., if the service requires the 3gpp-service launch
    Both URLs, if the 3GPP service is only an enhancement to kick off the service
  Portal application provider provides these URLs to UE, e.g. as part of a script, web page or another app
  On being executed, the background app starts up and
    Uses the service parameters to establish the 3gpp service in the background (if appropriate or available) and potentially connects to the network
    Uses the URL to the application service and kicks off the service
  If the app is not installed,
    a network service is called and runs the service URL resolution. In the simplest case, this resolution redirects to the application service
    or a 404 is returned and the portal application either terminates the service or uses the alternate over-the-top entry point

## Slide 21: Pros
Cons and Open Issues
Unclear if this can be launched as a background service (should be ok)
How could this be done for webRTC based services
Does the service scale properly?
What are security/authorization aspects?
What would it mean if every MNO would run its own background service
Can such a handler be pre-installed on a device?
API communication between 3GPP service and third party-app not established
How can you stop/start/monitor the 3GPP service?
URL is clickable, and can for example be added to web pages, text messages and so on
If service is not found, this can be returned to portal and alternative URL may be used
Can be applied for any third-party application and does not require any changes to app
Is likely extensible also to iOS to install a similar function on the device
Service can be launched including Interprocess Communication (IPC)

## Slide 22: Potential other solutions
Option 2: Can the media application service entry URL be built to launch a service handler?
  This requires that the media application itselfs understand that it requires/benefits from a 3GPP service and launches the 3GPP service app. Application needs to be specifically built for this, adding for example intent filters
Option 3: Service resolution using DNS
  This option is more aligned with the network resolution option 1
  See next slide
Option 4: ...
.

## Slide 23: DNS Resolution
A common 3gpp: URL scheme automatically launches a 3GPP resolver
The 3GPP resolver will using DNS service resolution to request SRV records
The resolution will provide all required service parameters
In case of receive-only, DNS service resolution may be happen within terminal based on existing pre-configuration
Alternative or new record types may be defined
  URI DNS record may be suitable for this use case
  mbs://netflix.com/series8 => mbs  URI-DNS => dns query URI dns://netflix.com
Example URI DNS record:
_mbs-rom._tcp IN URI 10 1 "http://www.example.com/path/service-announcement"

## Slide 24: DNS resolution
5GS
UE
Application #1 Content Guide/Web page/etc
Media Application
Provider
3GPP UE URI Handler (DNS query or server)
5G UE Functions
3GPP DNS Server
5G System Functions
URL with 3GPP Service parameters and application service entry point
Application #2 Media Application
Portal Application Provider

## Slide 25: Specific case: MBMS-ROM Service + CMAS-based launch of service
Scenario

## Slide 26: Usage of the proposed system
Define a URL for 3GPP Services as part of 3GPP specifications, e.g. 3gpp-services.com
  Define a service sub-domain mbms
  Add the relevant parameters from mbms-URL as defined in TS 26.347, clause 8.4 to the URL
In operation,
  install a background app that handles the URL
  Emergency media application provider has a service and wants to provide it through MBMS
  The 3GPP System provides a URL to the Emergency service provider with all relevant parameter
    http://3gpp-services.com/mbms/<service parameters>/<URL to application service>
  The Emergency media application service provider provides to the CMAS provider
    Only the 3GPP MBMS Service URL, if the service is only available over MBMS
    Both URLs, the unicast and the 3GPP service URL, if the 3GPP service is available on both
  The emergency service provider adds the URLs to a CMAS message as a textual description
  The user reads the message and clicks on the 3GPP Service URL
  The click deep-links to the 3GPP Service app and the service app
    identifies MBMS and launches the MBMS client
    Identifies the third party entry point and launches the URL

## Slide 27: Basic system – Emergency notifications
UE
Application #1 Content Guide/Web page/etc
3GPP UE Service Handler
5G UE Functions
Application #2 Media Application
1. CMAS message with URL
2. URL passed to the
“service handler” (background app)
3a. MBMS client activated
3b. Open UI
4a. Collect files
4b. Serve files
1. User gets emergency notifications, click on “registered” URL.
2. Android system sends the URL to the service handler (background app).
3. The service handler does two things:
  3a: Start the middleware based on part of the URL (e.g. frequency, TMGI).
  3b: Start the application and send a URL
4. The “UE Service Handler” serves as an HTTP proxy for the Application#2
  4a. Gets files from the MW
  4b. Serves files to Media app.
Can this be used to see a static website over Google Chrome using MBMS?

## Slide 28: Other potential questions and extensions
It may for example be needed to
  Encrypt the service parameters in the URL
  Sign the URLs
It may be desirable to create shortcuts for the URLs to make them more “human”-readable
The URL does not include the application service entry point, but the entry point is included in a service announcement file related to the 5G UE functions. As an example, the service entry point is part of the MBMS User Service Description.

## Slide 29: Conclusions
Until now, 3GPP specifications for 5G Media Streaming have been avoiding addressing the detailed question on how to bootstrap 3GPP defined UE and network functions such as the Media Session Handler or the MBMS/MBS client. This was deferred to implementation, device pre-configuration, and so on. However, the lack of having a specification around this topic.
Based on these discussions a solution is proposed to create a set of specification extensions:
Extend 5G Media Streaming Architecture to add a 3GPP Service and URL Handler in the UE and the network according to Figure 5.13.4-1.
Address provisioning, message exchange and call flows in order to support different use cases, namely the case for which the URL is resolved in the network, the URL is resolved in the UE, and the case for which the URL is resolved in a combination of network and UE as discussed in clause 5.13.4.
Provide a concrete URL for 3GPP services and Create a URL for 3GPP Services as part of 3GPP specifications, e.g. 3gpp-services.com, and make sure that this can be used in the context of 3GPP-based services, namely
- Verify ownership of the domain through one of the Android website association methods.
- Create a web site/redirection mechanism in case the application is not available on the device
- The URL itself needs to be sufficiently unambiguous to resolve to the main service and may include the URL to the main service as well
Address instantiations for a service URL at least for MBMS client, MBS client as well for Media Session Handler in 5G Media Streaming, including ROM services
Investigate and study the application of 3GPP Services and URL Handler beyond 5G Media Streaming.