## Slide 1: TM Forum Performance Management Interface Introduction
January, 2013

## Slide 2: Performance Management
Performance Management is part of Assurance Oversight team
Initial goal was harmonization between OSS/J QoS (JSR 90) and MTOSI RPM
Harmonization Study started in 2009 resulting in decision to build a new harmonized interface for Performance Management
TIP PM Monitoring V1.0 was released as part of TM Forum Frameworks 12.5

## Slide 3: Performance Harmonization Principles
Supporting eTOM processes & TAM Applications
  Service Quality Management
  Resource Performance Management
Based on TM Forum SID model and JOSIF infrastructures
OSS/J is close to 3GPP TS32.X series and ITU-T M.3704

## Slide 4: Performance Terminology
TIP | MTOI | OSS/J | 3GPP
Consuming Application | Requesting OS | Client | IRP Manager, Receiver
Producing Application | Target OS | Server | IRP Agent, Sender
Performance Indicator | PM Parameter, PM Data, PM Measurement | Measurement (Attribute), Measurable Attribute, Performance Parameter | Measurement (Type), Counter
Performance Indicator Group | None | None | Measurement Family/ Measurement Type
Measured Object Class | PM Object , Managed Element, 1) | Observable Object Class | Measured Object Class
Measurement Job | None | Measurement Job | Measurement Job
Granularity | Granularity | Granularity Period | Granularity Period
Collection Resolution | None | Report Period 2) | reportingPeriod

## Slide 5: Performance Harmonization Principles (Cont.)
Main system contexts considered
  Element Management – Network Management
  Network Management– Network Management
  Network Management– Service Management
Loose relation to Inventory applications
Multi-technology support – can be used for both Wireline & Mobile

## Slide 6: PM System Contexts (SC)
PM SMS
NMF
SMF
EMF
PM NMS
NMF
EMF
PM EMS
EMF
Network Element or Probe
EMF
SC 1.2
SC 1.3
SC 1.4
SC 2.3
SC 2.4
SC 3.4
SC 3.x
The various System Contexts (SC) are explained in details in TMF_PM_BA, Performance Management Business Agreement.

## Slide 7: TIP PM & 3GPP PM Similarities/Differences
Main Similarities
The measurement job concept
3GPP file format can be used (as well as MTOSI Format)
Asynchronous file transfer support
Main differences
Separation between PM production & PM collection
Ad hoc collection support
Looser relation to Inventory objects
Can be used for inter-OSS and Service layer

## Slide 8: Performance Production Vs. Performance Collection
A key concept of the interface is the separation between performance measurements production (e.g. PM Control in MTOSI) and performance measurements collection (sometimes called PM Reporting). This is based on the understanding that for practical efficiency and security reasons, the lifecycle of generating performance indicators may be very different from the lifecycle of collecting them by a performance consuming application.
Delete a Production Job
Create a Production Job
PM Producer (EM)
PM Consumer 1 (NM)
Discover capabilities
PM Consumer 2 (NM)
Data Available Notif
Modify a Collection Job
Create a Collection Job
Discover capabilities
Delete a Collection Job
Data Available Notif
Modify a Collection Job
Create a Collection Job
Discover capabilities
Delete a Collection Job

## Slide 9: General Scenario – Production, Collection & Thresholds

## Slide 10: Performance Monitoring Interface
TIP PM Monitoring V1.0 was released as part of TM Forum Frameworks 12.5 in September 2012
Includes four Services:
  PM Production Job
  PM Collection Job
  PM Ad-hoc Collection
  PM Retrieval (PM Metadata Discovery)

## Slide 11: The Measurement Production Service
Create a Measurement Production Job
  For an Object Class and additional filtering
  For a list of network objects (or service objects)
  Optionally, create a collection with the production
Delete a Measurement Production Job
Get a Measurement Production Job
Get Measurement Production Jobs

## Slide 12: The Measurement Collection Service
Create a Measurement Collection Job
  For an Object Class and additional filtering
  For a list of network objects (or service objects)
Modify a Measurement Collection Job (The measurements cannot be modified)
Suspend a Measurement Collection Job
Resume a Measurement Collection Job
Delete a Collection Measurement Job
Get a Measurement Collection Job
Get Measurement Collection Jobs (by attributes)
Notifications upon receiving results of Measurement Results

## Slide 13: The Ad-hoc Collection Service
Create Ad-hoc Collection
  For an Object Class and additional filtering
  For a list of network objects
Get Ad-hoc Collections
Notifications upon receiving results of Measurement Results

## Slide 14: The Collection Retrieval Service (Optional)
Discovery of the PM Producer Capabilities
  Supported Object Classes
  Supported measured objects
  Supported indicators groups per object
  Supported indicators per object class (and optionally per indicator group)
  Supported transport mechanism
  Supported file format
  Common time granularity of indicators

## Slide 15: EM-NM System Context (1)
Data Available Notification
Delete Production & Collection Job
Create a Production & Collection Job
PM Producer (EM)
PM Consumer (NM)
Discover capabilities

## Slide 16: EM-NM System Context (2)
Delete a Production Job
Create a Production Job
PM Producer (EM)
PM Consumer (NM)
Discover capabilities
PM Consumer (NM)
Data Available Notification
Modify a Collection Job
Create a Collection Job
Discover capabilities
Delete a Collection Job

## Slide 17: EM-NM-NM(SM) System Context (1)
Delete a Production Job
Create a Production Job
PM Producer (EM)
PM Consumer 1 (NM)
Discover capabilities
PM Consumer 2 (NM)
Data Available Notification
Modify a Collection Job
Create a Collection Job
Discover capabilities
Delete a Collection Job
Data Available Notification
Modify a Collection Job
Create a Collection Job
Discover capabilities
Delete a Collection Job

## Slide 18: PM Thresholds Work
Current PM Interface work is focusing on Thresholds Definitions
Thresholds will be defined over the interface supporting:
  Management of Threshold Jobs
  Generation of Multi-severity alarms
The TIP PM Thresholds additional part is planned for Frameworks 13.0