## Slide 1: Discussion on potential ways for integration of ONAP and 3GPP MnS
Source: Huawei

## Slide 2: Background of SA5#127 meeting discussion
Extracted from S5-196573 Notes of OAM sessions from the Chairman notes:
Assumption: The 3GPP-ONAP integration solution should consider stage2 of 3GPP notification is unchanged.
Objectives: this slides try to align the understanding of identified integration options (including Op1,Op2 and Op4, Op3 need more clarification) by using “NotifyNewAlarm” as an example for stage3 solution.

## Slide 3: Option1: Envelop/payload: 3GPP notification unchanged (assuming all information are there), VES header unchanged (add new ENUM value)
3GPP MnS Producer
3GPP MnS Consumer
ONAP VES Collector
3GPP generic NotifynewAalrm
(Defined in 3GPP)
ONAP VES CommonEventHeader
(Defined in ONAP)
3GPP generic NotifynewAalrm
(Defined in 3GPP)
Keypoint:
3GPP specified generic NotifyNewAlarm information is used as payload of ONAP VES Event for 3gpp fault domain.
ONAP provides enum value 'fault3gpp‘ attributes in CommonEventHeader as “envelop” .
3GPP MnS consumer uses 3GPP generic NotifyNewAlarm information
ONAP VES collector uses the combination of CommonEventHeader and 3GPP generic NotifyNewAlarm information
Actions to ONAP:
Add ENUM Value ‘Fault3GPPField’ for attribute ‘domain’ in commonEvenHeader
Add Value ‘fault3gppField’
For ‘Fault3GPPField’ definition, add reference to 3GPP generic ‘notifyNewAlarm’ JSON Schema
Add reference to 3gpp defined generic notifyNewAlarm JSON schema.
For example:
Add “fault3gppField”:{
“#ref:/3gpp fault supervision MnS.json#notifyNewAlarm”
}
Actions to 3GPP:
Separate the Fault3GPPField JSON Schema in several module for flexible reference.
Provide separate code files so that ONAP can directly refer and reuse.

## Slide 4: Option2-Escalation: copy some 3GPP payload into VES extension.
3GPP MnS Producer
3GPP MnS Consumer
ONAP VES Collector
3GPP generic NotifynewAalrm
(Defined in 3GPP)
Fault3GPPField
(Defined in 3GPP)
ONAP VES CommonEventHeader
(Defined in ONAP)
Two attributes (notificationId and eventTime) mapped to
Other attributes
Actions to 3GPP:
Based on the mapping work for 3GPP generic NotifyNewAlarm and ONAP VES CommonEventHeader (As TS 28.532 Table 12.2.2.2.1.2-1 described), specifies ‘Fault3GPPField’ with attributes of notifyNewAlarm which can’t be mapped to ONAP VES CommonEventHeader.
Reuse Fault3GPPField to compose 3GPP generic NotifyNewAlarm information
Provide separate code files so that ONAP can directly refer and reuse.
Actions to ONAP:
Add ENUM Value ‘Fault3GPPField’ for attribute ‘domain’ in commonEvenHeader
Add Value ‘fault3gpp’ Field
For ‘Fault3GPPField’ definition, add reference to 3GPP generic ‘notifyNewAlarm’ JSON Schema
Add reference to 3gpp defined fault3gppfieldJSON schema.
For example:
Add “fault3gppField”:{
“#ref:/3gpp fault3gppfield.json#fault3gppfield”
}
Keypoint:
1. 3GPP specifies ‘Fault3GPPField’ JSON schema as payload of ONAP VES for 3gpp fault domain. The Fault3GPPField includes attributes of 3GPP generic NotifyNewAlarm which is not mapped to ONAP VES CommonEventHeader.
2. ONAP Specifies notificationId and eventTime in VES commonEventHeader

## Slide 5: Option4-Mapping2: 3GPP notification stage2 unchanged (assuming all information are there), VES specification unchanged. SA5 decide which stage2 attributes can map to the VES header attributes. The whole notification of 3GPP stage2 go into the VES payload
3GPP MnS Producer
3GPP MnS Consumer
ONAP VES Collector
3GPP generic NotifynewAalrm
(Defined in 3GPP)
FaultDomain
(Defined in ONAP)
ONAP VES CommonEventHeader
(Defined in ONAP)
3GPP generic NotifynewAalrm
(Defined in 3GPP)
3GPP Defined Mapper
Actions to 3GPP:
Provide the mapping work for 3GPP generic NotifyNewAlarm and ONAP VES CommonEventHeader;
Provide the mapping work for 3GPP generic NotifyNewAlarm and ONAP defined FaultDomain;
Keypoint:
1. 3GPP specifies generic NotifyNewAlarm information.
2. ONAP specifies VES CommonEventHeader and FaultDomain.
3.3GPP defines mapping work for 3GPP generic NotifyNewAlarm and ONAP VES specification.
No Action to ONAP

## Slide 6: Observation of current ONAP VES Specification-Perf3gpp
https://wiki.onap.org/display/DW/VES+7.1
Observation1: ONAP VES specification introduce the Information Element (Similar like 3GPP stage2 work) for ‘Perf3gpp’, which includes following 3gpp defined attributes:
formatVersion: 3GPP PM reporting file format version from pre-standard TS 28.550 v2.0.0
granularityPeriod: Granularity period for the PM report in seconds
measObjInstIdList: Array of monitored object local distinguished name ids per 3GPP TS 32.300
measuredEntityDn: Distinguished name per 3GPP TS 28.550
measuredEntitySoftwareVersion: Software version for the NF providing the PM data as specified in 3GPP TS 28.550
measuredEntityUserName: User Definable name for the measured object per 3GPP TS 28.550
Measinfo: Array of monitored object local distinguished name ids per 3GPP TS 32.300
……
Observation2: ‘Perf3gpp’ is not specified in the ONAP VES code (similar like 3GPP stage3 work)
ONAP VES code link:
https://git.onap.org/dcaegen2/collectors/ves/tree/etc/CommonEventFormat_30.0.1.json

## Slide 7: Observation of current 3GPP ONAP integration specification- FM
‘notfiyNewAlarm’ Integration described in TS 28.532
Observation1: Two attributes ’notification Id’ and ’eventTime’ are specified in VES commonEventHeader
Observation2: TS 28.532 described ‘fault3gppFields’ JSON schema specific for ONAP VES integration, which capture notifyNewAlarm attribute except ‘notification Id’ and ‘eventTime’
‘payload’ Part
‘Envolop’ Part
Stage2
Stage3
Code defined in ONAP
Code defined in 3GPP
Analysis: The current specification taking option2 approach.

## Slide 8: Observation of current ‘notifyNewAlarm’ JSON schema in TS 28.532
TS 28.532 Clause A.2.1 Generic fault supervision management service
TS 28.532 Clause A.2.2 JSON schema of ‘fault3gppField’ for integration with ONAP VES
Observation1: TS 28.532 defined two JSON schema for generic fault supervision MnS and for integration with ONAP VES, most of the attributes are same expect ‘notificationId’ and ‘eventTime’, which means 3GPP SA5 needs to maintain two JSON schemas for notifyNewAlarm
Analysis: There is potential redundancy with this approach which needs to be resolved.

## Slide 9: Detailed Proposal for endorsement (1)
3GPP MnS Producer
3GPP MnS Consumer
ONAP VES Collector
3GPP MnS ( e.g.generic NotifynewAalrm)
(Defined in 3GPP)
ONAP VES CommonEventHeader
(Defined in ONAP)
3GPP MnS(e.g. generic NotifynewAalrm)
(Defined in 3GPP)
Proposal:
3GPP specifies a complete MnS solution for the communication between 3GPP MnS consumer and 3GPP MnS producer.
ONAP owns VES specification.
3GPP provides the recommendation for mapping of selected 3GPP attributes into VES fields (VES API version specific) to support VES compliant implementations.
3GPP specified MnS solution can be extended to satisfy with the needs for ONAP integration purpose.
Some interactions might be needed with ONAP, in particular if 3GPP requires to add an new ENUM value for attribute ‘domain’ in commonEventHeader
Benefit of this approach:
De-coupling of VES and 3GPP enables Operators to utilize all benefits of ONAP implementations while enabling the technologies to evolve independently.
3GPP MnS Producer
3GPP MnS Consumer
ONAP VES Collector
3GPP generic NotifynewAalrm
objectClass: Value A
objectInstance: Value B
notificationId: Value C
eventTime: Value D
systemDN: Value E
notificatioType:Value F
probableCause: ValueG
perceivedSeverity:ValueH
……
ONAP VES CommonEventHeader
sourceId:
eventId: Value C
eventName:
lastEpochMicroses: Value D
startEpochMicrosec: Vlaue D
domain:
priority:
…..
3GPP generic NotifynewAalrm
objectClass: Value A
objectInstance: Value B
notificationId: Value C
eventTime: Value D
systemDN: Value E
notificatioType:Value F
probableCause: ValueG
perceivedSeverity:ValueH
……
Example for integration approach for NotifynewAlarm
Mapping: Populate the value to ONAP header
Proposal-1: the group to endorse the following 3GPP-ONAP integration option and send LS to ONAP.
ONAP could also add a new field to VES header if 3GPP mapping recommendation doesn’t meet their requirements.

## Slide 10: Detailed Proposal for endorsement (2)
3GPP MnS Producer
3GPP MnS Consumer
ONAP VES Collector
3GPP MnS ( e.g.generic NotifynewAalrm)
(Defined in 3GPP)
ONAP VES CommonEventHeader
(Defined in ONAP)
3GPP MnS(e.g. generic NotifynewAalrm)
(Defined in 3GPP)
XXX domain
ONAP VES CommonEventHeader
(Defined in ONAP)
XXX interfaces
(Defined in XXX)
Proposal-2:
The same cooperation methodology could also be reused by the ONAP and cooperation with other domain-specific groups.This information could also be communicated with ONAP in the LS.
Benefit of this approach:
De-coupling of VES and 3GPP (or any domain-specific formats) enables Operators to utilize all benefits of ONAP implementations while enabling the technologies to evolve independently.

## Slide 11: Thank you!