## Slide 1: Interaction between CHF and V-SMF for LBO (SA5#142e)
Chen Shan Huawei

## Slide 2: Charging Architecture
TS 32.240
4.3.1.1 Charging Trigger Function
The Charging Trigger Function (CTF) generates charging events based on the observation of network resource usage as described in clause 4.1.1. In every network element and service element that provides charging information, the CTF is the focal point for collecting the information pertaining to chargeable events within the network element, assembling this information into matching charging events, and sending these charging events towards the CDF
TS 32.290
NF consumer (CTF) …
The CTF is the logic function, which defined the behaviour about the collection and reporting the charging information.
The standards does not specify how many CTFs is used in one NF, does not specify one CTF only serve one charging service
For EPC charging, the LBO scenarios is supported and no issues about the 2 CTFs.

## Slide 3: Solutions
The CTF is the focal point and logic function, specified in the TS 32.240.
Two proposed solutions, but only one charging architecture.
Solution 1: combine charging sessions for V-CHF and H-CHF
The V-CHF and H-CHF strongly impact on each other:
SMF must have the same chargeable events and same charging information for the V-CHF and H-CHF
SMF must have different charging context: charging resource ref , CHF address, State Machine, security mechanism,
Error handling issues shall same:
  In the case of the CTF request times out and interaction with two CHFs, CTF shall terminate the interaction with both CHFs.
  In the case, there are two CHFs involved, retries shall be avoided
  If the response from a second CHF results in a termination, this shall trigger a Charging Data Request [Terminate] to the first CHF with the reason for failure towards the second CHF.
Solution 2: individual charging session for V-CHF and H-CHF
The V-CHF and H-CHF do not impact on each other.
CTF have the separate chargeable event (may be same or different) and the separate charging information (may be same or different) for the V-CHF and H-CHF
Separate charging context: charging resource ref , CHF address, State Machine, security mechanism,
Error handling is separate.
  if the error can be handled in the charging resource of one CHF internal, it is no related to the another CHF.
  if the charging resource 1 error impacts on the PDU Session,another charging resource 2 will be changed which caused by the PDU session
Common Part:
SMF has the different charging session(charging resource) with V-CHF and H-CHF
For one PDU session, No impaction on PCF and UPF ( According to TS 23501, the interaction between PCF and UPF with SMF, not related to the CTF)

## Slide 4: Evaluation
 | Solution 1 | Solution 2
Supported Scenarios | H-CHF indicates the retail charging and V-CHF indicates wholesale. Retail and wholesale are strongly bound. If the retail is valid and does not charge (corresponding to the Continue in failure handling)., the wholesale must also be terminated. ， | H-CHF indicates the retail charging and V-CHF indicates wholesale. Retail and wholesale are separated which is controlled by each other individually. Even if there is no retail charging, the wholesale needs to be recorded as long as the PDU session continues.
Impact on Implementation | For a UE, V-CHF and H-CHF has impacted on each other, and the interaction way is specified in the standards, which is related to the implementation. | For a UE, there is no strong binding between V-CHF and H-CHF, the roaming negotiation can be performed between V-CHF and H-CHF. Multiple implementation are available.
Impact on SMF and CHF | The SMF needs to maintain two charging contexts and a set of charging information. From CHF side, the operation of the CHF need to consider the unknown behaviors of other CHFs, including the errors , management behaviors and the load (time out). The implementation of the CHF is complex and big impact on the live network. | The SMF needs to maintain two charging contexts and a set of charging information (the same QBC and FBC information). From CHF side, no change is required.

## Slide 5: Thank you!