## Slide 1: Discussion Paper on exposure via OSS
Source: AsiaInfo, Alibaba

## Slide 2: Background
  SA5 has discussed and agreed use cases and related solution regarding exposure via OSS. However, there is an LS relay from GSMA that suggest to only consider exposure via BSS. There is an need for further justify exposure via OSS from the business and technical perspective.
  This discussion paper propose to address such issue.

## Slide 3: The type of Exposure
  exposure via OSS
  Exposed MnS can be exposed via a dedicated exposure function (e.g.EGMF) or directly via the MnS producer for exposed MnS (e.g. NSSMF, etc)，the consumer can consume the exposed MnS via the dedicated exposure function.
  exposure via BSS
  Exposed MnS is exposed directly via MnS producer for exposed MnS or via the dedicated exposure function, for example NSMF, NSSMF, etc. exposed MnS is exposed via BSS, the consumer can consume the exposed MnS via BSS.

## Slide 4: Issues on Exposure via BSS
  Non-public network cases where BSS may not needed
  Vertical customer, such as electricity, may set up its own NPN. In order to manage such network, The vertical can directly interact with the OSS for the management of the NPN without the support of BSS.
  Frequency and Large volume of data exchange for exposure via BSS
  Vertical may have the requirement to consume the MnS regarding KPI monitoring (e.g. QoS) from the OSS. For example, the service provider for certain kind of application (e.g. cloud gaming) may require frequent consumption of exposed MnS so that based on the performance, the service provider can decide whether to allow its customer to get access to the network slice. The interval for obtaining such MnS may be less than 1 minute. Such kind of frequent interaction for expsoure may cause poor service performance and overload for BSS.

## Slide 5: Non public network cases
NOP Network
PNI-NPN
(dedicated resources)
NOP OSS
NOP BSS
Management
service platform
Vertical customer
Product-level interaction
NOP Network
SNPN
NOP OSS
NOP BSS
Management service platform
Vertical customer
Product-level interaction
Exposed MnS interaction
Exposed MnS interaction
  PNI-NPN as dedicated resources to vertical
  the MnS exposure may still go through Operator's management system if the network resources of the PNI-NPN is shared resources. However, there may have another case where the network resource of PNI-NPN is delicately allocated to the Vertical customer. In this case, the customer may have its own managemnet service plateform to manage the network resources and the MnS exposure can comes from OSS directly.
  SNPN with dedicated Management service platform
  The vertical has its own SNPN. The NOP OSS performs the main management tasks related to the SNPN (e.g. provisioning, fault supervision, performance assurance), while allowing the vertical to retain some control over this SNPN. (e.g. to allow UEs registered into the SNPN to access public network services) .In this case，the vertical consumes the management capabilities exposed by the NOP OSS, according to the business agreement between the two parties.

## Slide 6
NS management service exposure classification
category | NS management service exposure | For example | Reference
Query | Network Slice Performance measurements | Performance measurements for NSSF | TS28.552
 | Network Slice Key Performance Indicators (KPI) | one-single-network-slice-related KPI | TS28.554
 | Network Slice fault supervision | fault supervision of NS instance | TS28.545
Control | Network Slice lifecycle management | Network slice feasibility check, Network slice resource capacity planning | TS28.531
 | network slice SLS assurance SLS control | adjustment of attributes Of ServiceProfile | TS28.535、TS28.541
 | Network slice recourse control | modification of Network slice instance virtualized part | TS28.531

## Slide 7: Proposal
  Based the discussion, it is suggest to send LS to GSMA to explain the use case and requirement for the exposure directly via OSS.