## Slide 1: Discussion paper to Add StateManagementEntity support for 5G S5-224242
Nokia, Nokia Shanghai Bell

## Slide 2
Rationale
  State Management Data defined in TS 28.625 and ITU T Recommendation X.731 and ITU T Recommendation X.733 are very useful tools to exchange the state of IOCs between Consumer and Producer
  In TS 28.624, State Management Data Definition IRP is defined to specify and to standardise the generic attributes for modelling and managing the resources of 3G networks at the Itf N.
  TS 28.625 document specifies StateManagementEntity as an Archetype, that may represent any IOC defined in the Network Resource Models, e.g. Generic Network Resource Model, Core Network Resource Model, UTRAN Network Resource Model or GERAN Network Resource Model. This Archetype consists of attributes defined in ITU T Recommendation X.731 and ITU T Recommendation X.733, and the attributes defined for this Archetype can be imported and used in any IOC of the Network Resource Models, where such attributes are needed.
  TS 28.626 defines the 3GPP State Management Data Definition IRP Solution Set definitions for IRP CORBA, IRP XML and IRP JSON.

## Slide 3
Rationale
  TS 28.622 document specifies the Generic network resource information that can be communicated between an MnS producer and MnS consumer in deployment scenarios using the Service Based Management Architecture (SBMA).
  TS 28.541 document specifies the Information Model and Solution Set for the Network Resource Model (NRM) definitions of NR, NG-RAN, 5G Core Network (5GC) and network slice.
  ITU-T Recommendation X.731 Amendment 2 (01/2001): Amendment to support lifecycle state, has introduced a new state “lifecycle state”.
  State Management Data is useful for many scenarios where the Producer and Consumer are able to exchange and control the states of an MOI, and example of the same being asynchronous mode of provisioning operations.

## Slide 4
Observations
Observation 1
State Management Data definitions in TS 28.624, TS 28.625 and TS 28.626 are not extended for 5G NRMs, i.e., NR, NG-RAN, 5G Core Network (5GC) and network slice.
Observation 2
State Management Data definitions in TS 28.624, TS 28.625 and TS 28.626 are not extended for the following:
  Service Based Management Architecture (SBMA)
  Network Resource Model (NRM) definitions of NR, NG-RAN, 5G Core Network (5GC) and network slice.
  Generic Network Resource Model (NRM) definitions in TS 28.622
  YANG definitions
  OpenAPI definition in YAML format
Observation 3
Lifecycle state is introduced by ITU-T Recommendation X.731 Amendment 2: Amendment to support lifecycle state is not introduced in 3GPP.

## Slide 5
Observations
Observation 4
Generic NRM specified in TS 28.622 and NRMs specified in TS 28.541, do not refer to State Management Data definitions in TS 28.624, TS 28.625 and TS 28.626.
State Management related attributes from ITU‑T Recommendation X.731 [7] are defined in IOCs specified in TS 28.541 and TS 28.622, as listed blelow.
  NRCellDU IOC attributes operationalState, administrativeState
  NROperatorCellDU IOC attribute administrativeState
  SnssaiInfo IOC attribute administrativeState
  NetworkSlice IOC attributes operationalState, administrativeState
  NetworkSliceSubnet IOC attributes operationalState, administrativeState
  ThresholdMonitor IOC attributes operationalState, administrativeState
  ManagedNFService IOC attributes operationalState, administrativeState, usageState

## Slide 6
Proposal
Introduce lifecycle state attribute to StateManagementEntity
Extend StateManagementEntity Archetype for Generic NRMs defined for SBMA and 5G NRMs.
Introduce YANG and OpenAPI using YAML for StateManagementEntity

## Slide 7
StateManagementEntity and LifecycleState
  StateManagementEntity
  operationalState
  usageState
  administrativeState
  alarmStatus
  proceduralStatus
  availabilityStatus
  controlStatus
  standbyStatus
  unknownStatus
  LifecycleState ::= ENUMERATED { planned (0), installed (1), pendingRemoval (2) }

## Slide 8
References
  [1] 3GPP TS 28.541: "Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3", v17.6.0
  [2] 3GPP TS.28.622: "Generic Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS)"
  [3] 3GPP TS.28.623: "Telecommunication management; Generic Network Resource Model (NRM) Integration Reference Point (IRP); Solution Set (SS) definitions"
  [4] 3GPP TS 28.624: "Telecommunication management; State management data definition Integration Reference Point (IRP); Requirements"
  [5] 3GPP TS 28.625: "Telecommunication management; State Management Data Definition Integration Reference Point (IRP); Information Service (IS) "
  [6] 3GPP TS 28.626: "Telecommunication management; State management data definition Integration Reference Point (IRP); Solution Set (SS) definitions"
  [7] ITU-T Recommendation X.731: "Information technology - Open Systems Interconnection - Systems Management: State management function“
  [8] ITU-T Recommendation X.731: "Amendment 2: Amendment to support lifecycle state“
  [8] ITU-T Recommendation X.721: "Amendment 1: States to support lifecycle”

## Slide 9: Thank you!