## Slide 1: Charging Triggers in Stage 2 and Stage 3 (SA5 #152)
Chen Shan
Huawei

## Slide 2: The triggers in Charging Data Message Stage2
Triggers in the charging Stage 2
  TS 32.255: SMF triggers for PDU session, quota management.
  TS 32.254: NEF triggers for API invocation/notification.
  TS 32.256: AMF triggers for registration, location, N2 connection…
  …. SMSF, Prose charging trigger, Network slice charging trigger

## Slide 3: The Triggers in the CHF CDRs in Stage2
Triggers in the CHF CDRs Stage 2
  TS 32.254: NEF triggers in NEF CHF CDR.
  TS 32.257: EAS Deployment in CHF CDRs ….

## Slide 4: The Triggers in the Open API in the Stage3
Triggers in the Stage 3
  TS 32.291: The “Triggers” is reported in the Charging Data Request in the message
  TS 32.291: “TriggerType” is the Enumeration data type, which specify the Triggers defined in the Service Charging Specifications in the Stage 2 , I.e. the 32.255.

## Slide 5: The Triggers in the CHF CDRs in Stage3
Triggers in the Common Field of CHF-CDR
  5G Common charging data in CHF-CDR specified in TS 32.298 clause 5.1.5.0
Source: TS 32.290 V18.0.0
  UUC level triggers
  Message/Main level
  In the TS 32.298 CHF CDR and the corresponding ASN.1
  “Trigger” only covers SMF Triggers which specify the Triggers defined in the Service Charging Specifications in the Stage 2 , i.e. the 32.255.
  “sMFTrigger” is aligned with the data type “ TriggerType“ specified in the TS 32.291.
  ASN.1 for CHF CDRs

## Slide 6: Summary
Problems
    The relationship of Triggers in CHF CDR between TS 32.298 and TS 32.XXX service charging specifications
      Every service charging specifications includes the clause for the CHF record data, including the triggers such as SMF triggers in data connectivity CHF CDR in the TS 32.255, NEF triggers in exposure CHF CDR in the TS 32.254.
      The CHF record data in service charging specification stage 2 should be aligned with the TS 32.298 Stage 3.
      In the TS 32.298, Only SMF triggers are included.
    The relationship of Triggers in message between TS 32.291 and TS 32.XXX service charging specifications
      The triggers is transferred in the charging data request/response specified in service charging specifications, including such as SMF triggers in the TS 32.255, NEF triggers in the TS 32.254.
      The triggers in service charging specification Stage 2 should be aligned with the TS 32.291 Stage 3.
      In the TS 32.291, Only SMF triggers are included.
Meeting | CR | Title
SA5 #148 | S5-233451 | Rel-17 CR 32.298 Addition of the Triggers in the CHF CDR
 | S5-233452 | Rel-18 CR 32.298 Addition of the Triggers in the CHF CDR
SA5 #149 | S5-234287 | Rel-17 CR 32.298 Addition of the NF Triggers in the CHF CDR
 | S5-234288 | Rel-18 CR 32.298 Addition of the NF Triggers in the CHF CDR
SA5 #150 | S5-235476 | Rel-17 CR 32.298 Addition of the NF Triggers in the CHF CDR
 | S5-235479 | Rel-18 CR 32.291Correction on the TriggerType
 | S5-235477 | Rel-18 CR 32.298 Addition of the NF Triggers in the CHF CDR
 | S5-235478 | Rel-17 CR 32.291Correction on the Trigger Type
SA5 #151 | S5-236601 S5-236598 S5-236599 S5-236600 S5-236722 | Rel-17 CR 32.257 Remove the Triggers in Charging Data message Rel-17 CR 28.201 Remove the Triggers in Charging Data message Rel-18 CR 32.254 Remove the Triggers in Charging Data message Rel-18 CR 32.256 Remove the Triggers in Charging Data message Rel-18 pCR 28.203 Update of triggers
4 Opinions for the corrections (From R18 for all the stage2)
  Option A: If required, add the NF triggers in the CHF CDR TS 32.298.----Proposed in the CRs at SA5 #148 and 149.
  Option B: If required, add the trigger type definition and binding in the 32.291 and add the all NF triggers in the and CHF parameters and ASN.1 in the TS 32.298. ---- Proposed in the CRs at SA5 #150.
  Option C: If not required, remove all the triggers in the message level and CHF CDR in the stage 2 because Stage 3 is not supported. The SMF trigger is an exception because SMF triggers are already covered.--- Proposed in the CRs at SA5 #151.
  Option D: If required, the common triggers is not applicable and add the special Trigger for each stage2 ---Proposed in the pCRs at SA5 #151.
      .

## Slide 7: Option A --- Add NF triggers
Add the special triggers in the CHF CDR
Add the general NF triggers in the CHF CDR
    To keep alignment with the CHF CDRs specified in the service specifications, the following item should be added.
    For NEF charging, the message level triggers is specified in the TS 32.254
    For Edge computing charging, the message level triggers is specified in the TS 32.257.
    For NSPA charging, the triggers in Used Unit Container is specified in the TS 28.202.
    Other NF consumers which not specify the trigger in the CHF CDR will not present in the CHF CDR.
    Add the NF triggers in the CHF CDR which can be used for any NF consumer (e.g. AMF, NEF), except SMF.

## Slide 8: Option B --- Add the triggers in TS 32.291
…
…
Add the detailed trigger types for SMSF, AMF, NEF…and other NF consumers
  Take the SMSF as the example
  Stage 2 TS 32.274
  Stage 3 TS 32.291
  Other Trigger Type are added.
  IMS Nodes
  AMF
  NEF
  NSPA
  NSM

## Slide 9: Option B --- Add the triggers in TS 32.298
…
Add the detailed trigger Type for SMSF, AMF, NEF…and other NF consumers
    Take the SMSF as the example
  Stage 2 TS 32.274
  Stage 3 TS 32.298
  SMF
    Extend the Trigger and the sMFTrigger is not used.
    Define new trigger types for all NF consumers.
    Define new data type of trigger types “string” for all NF consumers and reference to the TS 32.291.
TriggerType ::= OCTET STRING

## Slide 10: Option C --- Remove the triggers in Stage2
    In the Stage 2, the following triggers have been specified.
    For NEF charging, the message level triggers is specified in the TS 32.254
    For Edge computing charging, the message level triggers is specified in the TS 32.257.
    For NSPA charging, the triggers in Used Unit Container is specified in the TS 28.202.
    Remove the triggers in the service specifications stage2 .Take NSPA triggers as the example
Remove the triggers in the charging data message and CHF CDR
  NSPA
  AMF
  NEF

## Slide 11: Option D --- Add the special triggers in Stage2
    In the Stage 2, the following triggers have been specified.
      For NSACF charging, the NSAC triggers in Used Unit Container is specified in the TS 28.203.
    Remove the common triggers specified in the TS 32.290.
Remove the triggers in the charging data message and CHF CDR
  Common Trigger
  Special Trigger for each Stage 2 Charging specifications

## Slide 12: CH Rapporteur Call (SA5-152pre)
Agenda Item | Tdoc Number | Title | Notes | Source | Release
7.3 Charging Maintenance and Rel-18 small Enhancements | S5-236597rev1 | Discussion paper on triggers in charging stage 2 and stage 3 | Triggers need to be reported. However, event-based triggers and session-based triggers are processed in different ways. The event-based trigger (i.e. IEC/PEC/ECUR) does not need to reported in the “Trigger” IE. Other parameters, e.g. NEF API charging information for NEF charging can includer the trigger related information. The common triggers for session-based triggers in the TS 32.290, may be separated into two types triggers: quota management trigger and service special trigger, which is the open issues, need to be re-evaluated. Clarify the trigger reporting case by case in the stage 2 service specifications. | Huawei | R18

## Slide 13: Charging scenarios/Trigger Support (1)
NF (CTF) | Charging Scenarios | Trigger Level | Trigger in the message | Supported | TS Specification
SMF | SCUR | PDU Session level RG level/QoS flow | Charging Data Request: Trigger in the Request message Trigger in the Multiple Unit Usage Charging Data Response: Trigger in the Response message Trigger in the Multiple Unit Information CHF CDR SMF Trigger | TS 32.291 Yes TS 32.298 Yes | TS 32.255
NEF | PEC, either IEC or ECUR | Not Applicable | Charging Data Request: Trigger in the Request message Trigger in the Multiple Unit Usage Charging Data Response: Not Applicable CHF CDR NEF specific triggers | TS 32.291 No TS 32.298 No | TS 32.254
AMF | PEC, either IEC or ECUR | Not Applicable | Charging Data Request: Trigger in the Request message Charging Data Response: Trigger in the Response message CHF CDR Not Show | TS 32.291 No TS 32.298 No | TS 32.256
SMSF | PEC, either IEC or ECUR | Not Applicable | Charging Data Request: Trigger in the Multiple Unit Usage Charging Data Response: Not Applicable CHF CDR Not Applicable | TS 32.291 No TS 32.298 No | TS 32.274

## Slide 14: Charging scenarios/Trigger Support (2)
NF (CTF) | Charging Scenarios | Trigger Level | Trigger in the message | Supported | TS Specification
EES | IEC or PEC | Not Applicable | Charging Data Request: Trigger in the Request message Charging Data Response: Not Applicable CHF CDR Edge enabling services triggers | TS 32.291 No TS 32.298 No | TS 32.275
IMS Nodes | IEC, PEC, ECUR or SCUR | Not Applicable | Charging Data Request: Trigger in the Request message Trigger in the Multiple Unit Usage Charging Data Response: Trigger in the Response message CHF CDR Trigger in Used Unit Container | TS 32.291 No TS 32.298 No | TS 32.260
5G DDNMF | PEC, IEC or ECUR | Not Applicable | Charging Data Request: Trigger in the Request message Trigger in the Multiple Unit Usage Charging Data Response: Trigger in the Response message Trigger in the Multiple Unit Information CHF CDR ??? | TS 32.291 No TS 32.298 No | TS 32.277
MMS Node | PEC, IEC or ECUR | Not Applicable | Charging Data Request: Not Applicable Charging Data Response: Not Applicable CHF CDR ??? | TS 32.291 No TS 32.298 No | TS 32.270

## Slide 15: Charging scenarios/Trigger Support (3)
NF (CTF) | Charging Scenarios | Trigger Level | Trigger in the message | Supported | TS Specification
NSPA | PEC | Not Applicable | Charging Data Request: Trigger in the Request message Trigger in the Multiple Unit Usage Charging Data Response: Not Applicable CHF CDR Trigger in the Used Unit Container | TS 32.291 No TS 32.298 No | TS 28.201
NSM | PEC | Not Applicable | Charging Data Request: Not Applicable Charging Data Response: Not Applicable CHF CDR Not Applicable | TS 32.291 No TS 32.298 No | TS 28.202
NSACF | IEC, PEC, ECUR or SCUR | Not Applicable | Charging Data Request: Trigger in the Request message Trigger in the Multiple Unit Usage Charging Data Response: Trigger in the Response message Trigger in the Multiple Unit Information CHF CDR Triggers in Message level Trigger in the Used Unit Container | TS 32.291 No TS 32.298 No | TS 28.203 (Pending)
NSAAA | IEC, PEC and ECUR | Not Applicable | Charging Data Request: Trigger in the Request message Charging Data Response: Not Applicable CHF CDR ??? | TS 32.291 No TS 32.298 No | TS 28.204 (Pending)

## Slide 16: Suggestion (SA5-152)
Charging Data Request
  Triggers used for the IEC, PEC, ECUR charging scenarios should not be reported in the Charging Data Request, the special charging information already can provide the Reasons for triggers.
  Triggers used for the SCUR charging scenarios should be reported in the Charging Data Request.
Charging Data Response
  Triggers used for the IEC, PEC, ECUR charging scenarios should not be included in the Charging Data Response. The trigger setting for IEC, PEC, ECUR from CHF (disable/enable the triggers) can be done by Charging profile Mechanism (Pending, FFS).
      Remove the Common Trigger in the charging data request (Rel-18 CR 32.256 Update on Triggers for AMF charging)
  Triggers used for the SCUR charging scenarios should be reported in the Charging Data Request. The trigger setting for SCUR from CHF (change the triggers category, disable/enable the triggers) can be done by “Trigger” filed in the charging data response.
      Option 1 : Reuse the Common Trigger and TriggerType attributes. The TriggerType is used for all NF SCUR charging scenarios. (Rel-18 CR 32.291 Update the Trigger Type for IMS Charging)
      Option 2: The corresponding common Trigger and TriggerType are only used for the SMF trigger. For other NF SCUR charging scenarios, The common trigger is not applicable, the special triggers should be added. (Rel-18 CR 32.260 Update on Triggers for IMS charging)
CHF CDR
  Triggers used for the IEC, PEC, ECUR charging scenarios should not be covered in the CHF CDR.
  Triggers used for the SCUR charging scenarios should be covered in the CHF CDR. (Rel-18 CR 32.260 Update on Triggers for IMS charging)

## Slide 17: Rel-18 CR 32.256 Update on Triggers for AMF charging
Remove the Common Trigger in the charging data request

## Slide 18: Rel-18 CR 32.291 Update the Trigger Type for IMS Charging
  In the service description of Nchf_ConvergedCharging, how to record the triggers used for IMS SCUR charging scenario in the Nchf_Convergedcharging is missing.
  To keep alignment with the triggers specified in the IMS service specifications TS 32.260, the corresponding trigger types in the Open API should be added for IMS Node.
Reuse the Common Trigger and TriggerType attributes

## Slide 19: Rel-18 CR 32.260 Update on Triggers for IMS charging--- Triggers
For other NF SCUR charging scenarios, The common trigger is not applicable, the special triggers should be added.

## Slide 20: Rel-18 CR 32.260 Update on Triggers for IMS charging--- CHF CDR
Triggers used for the SCUR charging scenarios should be covered in the CHF CDR.

## Slide 21: Thank you!