## Slide 1: Discussion on Using OAM system to configure EAS information for federation
Yajie Hu,
Source: Huawei, Hisilicon

## Slide 2: NF (EES, ECS) on-boarding procedure within single OP
NF (ECS, EES)On-boarding procedure
  NF on-boarding procedure is defined in ETSI GS NFV-MAN 001; ECS, EES on-boarding procedure for single Operator scenario is defined in 3GPP TS 28.538 which is using the NF on-boarding procedure
  Configuration of ECS profile for ECS onboarding or ECS profiles updating; Configuration of EES profile for EES onboarding or EES profiles updating
Resource allocation
Configuration of VNF

## Slide 3: Requirement on inter OP EAS on-boarding for Federation
Home ECSP
Partner ECSP
App#1
App#2
App#4
OP B
Partner OP A
ASP
App#2
Federation agreement for inter ECSP edge service agreement (APP#2)
Service agreement (APP#2)
inter-OP EAS on-boarding should be covered by interaction between two OAM systems
OP-E/WBI(s) should contains Mff and support the features for:
  On-barding and Configuration EAS
  Configuration parameters of ECS/EES profile should be also accordingly supported for inter-OP EAS on-boarding

## Slide 4: Overall procedure for inter-OP EAS on-boarding
Federator A
OAM A
EES A
EAS B
OAM B
Federator B
ECS B
4. Update ECS configuration info (ECS A info – related EAS B info)
0. Pre-condition: ECS B already on-boarded
2. Interaction between OAM A and OAM B for EAS onboarding and configuration:
  providing EAS image by OAM B to OAM A
  Respond the result with on-boarded information（e.g. ECS address info）
3. Determination and modified the configuration profile of affected ECS
1. Receiving requirement for inter-OP EAS onboarding
On-boarding and configuration update procedure
  EAS on-boarding: Federator B receiving the requirement for inter-OP EAS onboarding; and provide EAS image by OAM B to OAM A; the Federator B will return the result with on-boarded information（e.g. ECS address info）
  ECS configuration information update: when inter-OP EAS on-boarding procedure is performed, the Federator B will trigger the OAM B to update the ECS configuration information with ECS A info – related EAS B info

## Slide 5
Thank You!