## Slide 1: ACR selection in DN side
Wenliang Xu (Ericsson)

## Slide 3
ACR scenario selection
There are two solutions addressing ACR scenario selection for the initial ACR:
  EES selects it in sol#19 upon request from EEC and has EN:
  Editor's note: It is FFS how the EES can know the supported service continuity scenarios of the T-EES and T-EAS.
  EEC selects it in sol#35 after EAS discovery
The quorum member includes AC, EEC, serving EES and serving EAS with different ACR support capabilities.
No solution addressed T-EAS discovery stage during subsequent ACR yet in TR.
If ACR happens according to the selected one or multiple ACRs, later the T-EES and T-EAS are involved in the picture forming a new quorum (i.e. AC, EEC, T-EES becomes serving EES and T-EAS becomes serving EAS) and new quorum members may have a different ACR support capabilities available for ACR selection re-negotiation (probably more ACR scenarios or a different single ACR scenario can be used for next ACR)

## Slide 4
ACR selection for subsequent ACR (1)
It can happen during the T-EAS discovery stage by triggered by EEC, which is similar as sol#35 by replacing EAS discovery with T-EAS discovery.
It is also possible for S-EES made decision (sol#19) upon EEC request during ACR after EEC is aware of the selected Targets.

## Slide 5
ACR selection for subsequent ACR (2)
pCR S6-222091 provided another option during S-EAS/S-EES side triggered ACR scenario to decide ACR scenarios to be used in the next ACR.
=> an example of S-EAS decided ACR scenario (similar to sol#35 replacing EEC with S-EAS)