## Slide 1: Linked EAS requirements
Jian Zhang, Yajie (Huawei)

## Slide 2
The scenarios where AC connects to multiple EASs are classified into two types:
First type: general multiple EASs scenario  AC doesn’t have the specific performance requirements (e.g. No need the same or similar service KPI requirements)
-- In R17, “list of EASs” has been included in AC profile, both the EAS discovery procedure and ACR procedure can be performed independently.
Second type: linked EAS scenario  AC has the same or similar service KPI requirements
Linked EAS requirements

## Slide 3
EAS#1 (game server)
UE
UE
DC#1
UE
In location#2: Same KPI due to the same distance
In location#1: Same KPI cannot be maintained
In location#3: Same KPI cannot be maintained
In across EDN or across data center, same service KPI can only be maintained occasionally (e.g. in UE location#2)
In same EDN or same data center, same service KPI can be always maintained
EAS#2 (capture server)
EAS#1 (game server)
DC#2
EAS#2 (capture server)
Same data center or across data center?
Move to
Move to
Proposal: selecting linked EAS from same DC/EDN is the first priority if available.
selecting linked EAS can fall back to different DC/EDN, if not available

## Slide 4
Conclusion
The Linked EAS(s) are for the purpose of obtaining same KPI experience from the EAS(s).
Linked EAS(s) should be provided from the same location in a EDN (e.g. data center) which provides same KPI experience from the EAS(s).
If EEL cannot support linked EAS(s), then linked EAS(s) are used like list of EAS(s) as in R17 where the EAS(s) can be discovered from different locations or EDNs.